## Slide 1: On CABAC Initialization (JCTVC-H0561)
Liwei Guo, Marta Karczewicz
Feb. 2012

## Slide 2: Introduction
In HM, each slice type (I/P/B) has a separate set of initialization value
Proposed solution for storage reduction
  Contexts from different slice types share the same initialization value.
*The actual number may be lower since some contexts are used only for certain slice type
 | I | P | B
# of initialization value (estimated) | 187 | 208 | 212

## Slide 3: Method 1
Contexts from P slice and B slice share the same initialization set
  We use I slice initialization value in HM5 as Init_Set_Intra, and B slice initialization value in HM5 as Init_Set_Inter
Slice Type | I | P | B
Initialization Set | Init_Set_Intra | Init_Set_Inter | Init_Set_Inter

## Slide 4: Method 2
A subset of contexts is defined.
  If belonging to this subset, contexts in the all 3 slice types share the same initialization values
In our implementation, the context subsets:
  skip flag, merge flag, merge index, AMP_X position, AMP_Y position, inter prediction direction, mvd, reference frame index, deltaQP, root cbf flag, mvp index, level_greater_than_1, level_greater_than_2, ALF flag, ALF UVLC, ALF SVLC, SAO FLAG, SAO UVLC, SAO SVLC

## Slide 5: Estimation of initialization value reduction
 | HM5.0 | Method1 | Method2
# of Initialization values | 607 | 399 | 462

## Slide 6: Simulation results – Method 1
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.1% | -0.1% | 0.0% | 0.1% | -0.1%
Class C | 0.0% | 0.0% | -0.3% | 0.0% | 0.2% | 0.0%
Class D | 0.0% | 0.4% | 0.3% | 0.0% | -0.4% | 0.6%
Class E | 0.0% | -0.3% | -0.1% | 0.0% | -0.8% | -0.5%
Class F | 0.0% | 0.1% | 0.4% | 0.1% | -0.8% | 0.1%
Overall | 0.0% | 0.1% | 0.0% | 0.0% | -0.3% | 0.0%
 | 0.0% | 0.1% | 0.0% | 0.0% | -0.3% | 0.1%
Enc Time[%] | 97% |  |  | 97% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 

## Slide 7: Method 1- 1500 bytes slice
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.2% | -0.3% | 0.0% | 0.0% | -0.6%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
Class D | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | -0.1%
Class E | 0.0% | -0.4% | -0.4% | 0.1% | -0.3% | 0.2%
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | -0.1% | -0.1% | 0.1% | 0.0% | -0.1%
 | 0.0% | -0.1% | -0.1% | 0.1% | 0.0% | -0.1%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 8: Method 2
All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
0.0% | -0.1% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0%
Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
-0.1% | -0.1% | 0.0% | 0.0% | -0.2% | -0.1% |  |  | 
Low delay P HE |  |  | Low delay P LC |  |  | Low delay P HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 

## Slide 9: Method 2 - 1500 bytes slice
All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% |  |  | 
Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | -0.1%
Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
0.0% | 0.2% | -0.1% | 0.0% | 0.1% | 0.0% |  |  | 
Low delay P HE |  |  | Low delay P LC |  |  | Low delay P HE-10 |  | 
Y | U | V | Y | U | V | Y | U | V
0.0% | 0.0% | -0.1% | 0.1% | 0.1% | -0.1% |  |  | 

## Slide 10: Conclusions
Two methods proposed to reduce initialization value storage
  P slice and B slice using the same initialization value set
  For a subset of the contexts, same initialization values used for the 3 slice types
Both methods show almost no impact on coding efficiency
Recommend adoption into HM
Thanks to MediaTek for cross-checking (JCTVC-H0671)

## Slide 11
Thank you!