## Slide 1
<number>
JCTVC-H0562: Informal Subjective Quality Comparison of Compression Performance of HEVC WD 5 with AVC High Profile
Michael Horowitz
8th JCTVC Meeting in San Jose USA
1-10 February 2012
Notes: <number>

## Slide 2: Objective
<number>
Compare the subjective compression performance between HEVC WD5 and AVC High Profile
Proposed subjective quality assessment:
  Focus on low delay configuration
  Complement objective results in G399 & H0360
Notes: <number>

## Slide 3: Software Configuration
<number>
HEVC
  HM 5.0 software
  Test conditions in JCTVC-G1200 (some sequences with modified QP values)
AVC
  JM 18.2 Software updated with the described changes in JCTVC-H0360 and previously in JCTVC-G399
    P frames with a 1+3 reference frame setting as in HM 5.0
    Hierarchical QP assignment as in HM 5.0
Notes: <number>

## Slide 4: Subjective Evaluation Conditions
<number>
Equipment and room conditions
  42”, 1080p, Viera-class Panasonic plasma monitor
  Subjects sat 2 to 4 feet from the monitor
  Viewing angle never exceeded 45 degrees
  Darkened room
Video sequences were
  Presented side-by-side
  Presented in a randomized double blind fashion
  Displayed at native size
  Played four times in immediate succession with five-to-ten second pauses between presentations
Notes: <number>

## Slide 5: Sequences and Bit Rates
<number>
Configuration | Class | Sequence | AVC Bit Rate (Mbps) | HEVC Bit Rate (Mbps)
 |  |  | Target/Achieved | Target/Achieved
Low Delay | 1080p 1080p 720p 720p 720p | Kimono | 2.0/2.07 | 1.0/1.02 (49.2% of AVC rate)
 |  | ParkScene | 2.0/1.94 | 1.0/0.96 (49.5% of AVC rate)
 |  | Vidyo3 | 1.0/1.10 | 0.5/0.56 (50.5% of AVC rate)
 |  | Vidyo1 | 1.0/1.08 | 0.5/0.55 (51.1% of AVC rate)
 |  | Raven | 2.5/2.54 | 1.25/1.27 (50.0% of AVC rate)
Notes: <number>

## Slide 6: Subjective Quality Assessment Results
<number>
Configuration | Sequence | Number of Viewers | AVC | HEVC | No Preference
Low Delay | Kimono | 22 | 3 | 18 | 1
 |  |  | 14% | 82% | 5%
 | ParkScene | 22 | 4 | 10 | 8
 |  |  | 18% | 45% | 36%
 | Vidyo3 | 13 | 5 | 4 | 4
 |  |  | 38% | 31% | 31%
 | Vidyo1 | 13 | 7 | 2 | 4
 |  |  | 54% | 15% | 31%
 | Raven | 22 | 4 | 7 | 11
 |  |  | 18% | 32% | 50%
Total |  | 92 | 23 | 41 | 28
 |  | 100% | 25% | 45% | 30%
Notes: <number>

## Slide 7: Conclusions
<number>
For the selected video sequences and bit rates:
  On average, a preference for the HEVC encoded video
  In 75% of the cases, no preference or HEVC better
  Subjective evaluation results encouraging