## Slide 1
<number>
JCTVC-H0569 (Non-CE3): An Adaptive Interpolation Filtering Technique for Improved Subjective Quality in the LC Configuration
Faouzi Kossentini
8th JCTVC Meeting in San Jose. USA
1-10 February 2012
Notes: <number>

## Slide 2: Motivation
The LC configuration has both ALF and SAO disabled.
The LC configuration should have a tool to adapt to video content with sudden variations and special effects (e.g., fade, flashes).
The tool should achieve the complexity-coding efficiency tradeoffs appropriate for LC.
We propose Adaptive Interpolation Filtering (AIF) as a tool that achieves the above requirements.
<number>

## Slide 3: HM 5.0 Interpolation
<number>
1/4 | { -1, 4, -10, 57, 19, -7, 3, -1 }
1/2 | { -1, 4, -11, 40, 40, -11, 4, -1 }
HM 5.0 chroma filters
1/8 | { -2, 58, 10, -2 }
1/4 | { -4, 54, 16, -2 }
3/8 | { -6, 46, 28, -4 }
1/2 | { -4, 36, 36, -4 }
HM 5.0 luma filters
Notes: <number>

## Slide 4: Proposed AIF Technique
<number>
The new filters have identical characteristics to the default filters:
  Same number of coefficients
  Same symmetry properties
  Same bit depth
1/4 | {a0, a1, a2, a3, a4, a5, a6 }
1/2 | {b0, b1, b2, b3, b3, b2, b1, b0 }
Same HM 5.0 Filtering Structure
1/8 | { a0, a1, a2, a3 }
1/4 | { b0, b1, b2, b3 }
3/8 | { c0, c1, c2, c3 }
1/2 | { d0, d1, d1, d0 }
Newly-generated luma filters
Newly-generated chroma filters
Notes: Filter selection occurs at the slice level. Luma_filter_mode_flag is sent in slice header
<number>

## Slide 5: Proposed AIF Technique
<number>
For each slice, select between the HM5.0 default filter(s) and the corresponding newly-generated filter(s).
A 2-bit/4-bit value is signaled to the decoder to specify whether default or new luma/chroma filter(s) are are used.
All PUs of a slice use the same luma and chroma filters.
Only default chroma filters are allowed when default luma filters are used.
Notes: Filter selection occurs at the slice level. Luma_filter_mode_flag is sent in slice header
<number>

## Slide 6: Simulation Results
<number>
 | Random Access LC |  | 
 | Y | U | V
Class A | -1.0% | -0.1% | 0.1%
Class B | -0.6% | -0.2% | -0.1%
Class C | -0.4% | -0.4% | -0.3%
Class D | -0.3% | -0.4% | -0.3%
Class E |  |  | 
Overall | -0.5% | -0.3% | -0.2%
 | -0.5% | -0.3% | -0.2%
Enc Time | 102% |  | 
Dec Time | 99% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 7: Simulation Results
<number>
 | Low delay B LC |  | 
 | Y | U | V
Class A |  |  | 
Class B | -0.6% | -1.1% | -0.8%
Class C | -0.8% | -0.7% | -0.9%
Class D | -0.7% | -0.2% | -0.1%
Class E | -1.1% | -8.3% | -5.6%
Overall | -0.8% | -2.1% | -1.5%
 | -0.8% | -2.0% | -1.6%
Enc Time | 102% |  | 
Dec Time | 99% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 8: Simulation Results
<number>
 | Low delay P LC |  | 
 | Y | U | V
Class A |  |  | 
Class B | -8.6% | -4.1% | -4.4%
Class C | -4.5% | -2.1% | -1.8%
Class D | -2.4% | -1.1% | -0.8%
Class E | -10.4% | -15.2% | -11.6%
Overall | -6.4% | -4.9% | -4.2%
 | -6.4% | -5.0% | -4.2%
Enc Time | 105% |  | 
Dec Time | 100% |  | 
Notes: Call attention to encoder compute – down from 130+ % at the last meeting
All results in this presentation are relative to HM 3.0.
<number>

## Slide 9: Subjective Evaluation: Conditions
<number>
Equipment and room conditions:
  42”, 1080p, Viera-class Panasonic plasma monitor
  Subjects sat 2 to 4 feet from the monitor
  Viewing angle never exceeded 45 degrees
  Darkened room
Video sequences were:
  Presented side-by-side
  Presented in a randomized double blind fashion
  Displayed at native size
  Played four times in immediate succession with five-to-ten second pauses between presentations
Notes: <number>

## Slide 10: Subjective Evaluation: Sequences & Bit Rates
<number>
Sequence | HM-5.0 LC |  | AIF |  | Bit-rate deviation (%)
 | QP | Bit-rate (kbps) | QP | Bit-rate (kbps) | 
BQTerrace | 37 | 866.81 | 37 | 831.82 | -4.04%
Vidyo1 | 37 | 190.98 | 37 | 190.77 | -0.11%
Vidyo1_Fade | 37 | 323.01 | 34 | 281.65 | -12.80%
Vidyo3 | 37 | 226.81 | 37 | 221.59 | -2.30%
Vidyo3_Fade | 37 | 374.92 | 34 | 363.58 | -3.02%
SpinCalendar | 37 | 339.82 | 37 | 318.89 | -6.16%
*Note: The HM-5.0 bit rate is always larger than the AIF bit rate.
Notes: We believe RA results are lower compared with the LD as a result of the use of future pictures in B slices
<number>

## Slide 11: Subjective Quality Assessment Results
<number>
Sequence | Number of viewers | HM-5.0 LC | AIF | No Preference | Remarks
BQTerrace | 7 | 0 | 7 | 0 | Seven viewers noted that AIF is slightly better than the anchor.
 |  | 0% | 100% | 0% | 
Vidyo1 | 7 | 0 | 6 | 1 | Five viewers noted that AIF is better than the anchor.
 |  | 0% | 86% | 14% | 
Vidyo1_Fade | 7 | 0 | 7 | 0 | Seven viewers noted that AIF is clearly better than the anchor.
 |  | 0% | 100% | 0% | 
Vidyo3 | 7 | 0 | 5 | 2 | Four viewers noted that AIF is better than the anchor.
 |  | 0% | 71% | 29% | 
Vidyo3_Fade | 7 | 0 | 7 | 0 | Seven viewers noted that AIF is clearly better than the anchor.
 |  | 0% | 100% | 0% | 
SpinCalendar | 7 | 0 | 7 | 0 | Seven viewers noted that AIF is slightly better than the anchor.
 |  | 0% | 100% | 0% | 
Total | 42 | 0 | 39 | 3 | Overall, AIF decoded streams look better than the anchor ones.
 | 100% | 0% | 93% | 7% | 
Notes: We believe RA results are lower compared with the LD as a result of the use of future pictures in B slices
<number>

## Slide 12: Conclusions
<number>
BD-Rate relative to HM 5.0 LC:
  2.5%. 2.4% and 1.9% average Y, U and V BD-Rate reductions (respectively) compared with HM 5.0
Complexity relative to HM 5.0 LC
  Same average decoding time
  ~3% increase in average encoding time
  Virtually no increase in encoding complexity for encoders with a pre-analysis pass (e.g., where a rough ME is used)
Improved subjective quality for many test sequences, including VC sequences and those with special effects.