## Slide 1: Level definition to limit memory bandwidth of MC JCTVC-H0600
Kenji Kondo and Teruhiko Suzuki
Sony

## Slide 2: Summary
Memory bandwidth is important issue for MC because
  the decoder throughput is limited by bandwidth of MC in especially large image application.
Discuss the desirable restriction
Propose simple two ideas.
  Restrict small MC block and bi-prediction.
  Limit maximum number of motion vectors
Experiment
  BD% impact for block restriction
  Number of MVs of current anchor streams
Conclusion

## Slide 3: Discussion of desirable restriction
Possible to constrain the max memory bandwidth
  In relevant small region
    A restriction for PU level is best to limit the bandwidth but it will increase the coding efficiency loss.
    A restriction for picture level is difficult to design hardware both encoder and decoder, but it will decrease the coding efficiency loss.
    We think that the restriction for each LCU or CU is good trade-off.
Easy to check the conformance
  To motivate us to protect this level definition.
Good flexibility for new level
  In the future, new level may be defined by something reason.
Harmless coding performance

## Slide 4: Idea to limit max bandwidth
PU restriction
Limit max number of motion vectors

## Slide 5: PU restriction
Case | Restricted modes |  |  |  |  |  | 
Lv. A0 |  |  |  |  |  |  | 
Lv. A1 | Bi-4x4 |  |  |  |  |  | 
Lv. A2 | Bi-4x4 | Bi-4x8 |  |  |  |  | 
Lv. A3 | Bi-4x4 | Bi-4x8 | Bi-8x4 |  |  |  | 
Lv. A4 | Bi-4x4 | Bi-4x8 | Bi-8x4 | Uni-4x4 |  |  | 
Lv. A5 | Bi-4x4 | Bi-4x8 | Bi-8x4 | Uni-4x4 | Bi-8x8 |  | 
Lv. A6 | Bi-4x4 | Bi-4x8 | Bi-8x4 | Uni-4x4 | Bi-8x8 | Uni-4x8 | 
Lv. A7 | Bi-4x4 | Bi-4x8 | Bi-8x4 | Uni-4x4 | Bi-8x8 | Uni-4x8 | Uni-8x4

## Slide 6: Average BD% for class A, B, E

## Slide 7: Proposal for max number of MVs
LCU size | Restriction case 1 | Restriction case 2 | Restriction case 3
16x16 | 16 | 8 | 4
32x32 | 64 | 32 | 16
64x64 | 256 | 128 | 64
The memory bandwidth of case 1 is corresponding to level 3 of AVC.
The case 2 is level 3.1 and above of AVC.
The case 3 is added for more strong restriction.

## Slide 8: Max number of MVs per one LCU for class C, D

## Slide 9: Max of MVs per one LCU for class A, B

## Slide 10: Conclusions
Introduced desirable restriction.
Proposed two ideas to limit max memory bandwidth
  PU restriction
  Limit number of motion vectors
We propose to further study above ideas in AhG of memory bandwidth.