## Slide 1: Profiles and Levels in HEVC (H0637r3) Ajay Luthra Motorola Mobility (aluthra@motorola.com) Feb 1, 2012

## Slide 2: Profiles and Levels
Support both fixed and flexible Profiles and Levels specifications
Fixed
  Used in the systems with fixed interoperating points
    E.g. Digital TV broadcasting with one-way communication
Flexible
  Can be used in the systems with two-way communication and variable interoperable points
    E.g. Digital TV distribution to tablets, smart phones, smart TVs using DASH
<number>

## Slide 3: Profiles and Levels
Fixed Profiles and Levels
  Levels
    Align the numbers corresponding to SDTV and HDTV with those in AVC
      Level 3 : Support 720x480 at 30 frames per sec, 720x576 at 25 frames per sec, 640x480 at 30 frames per sec, 960x540 (QHD) at 30 frames per sec
      Level 4: Support 1280x720 at 60 frames per sec, 1920x1080 at 30 frame per sec
      Level 5: Support 1920x1080 at 60 frames per sec
      Level 6: Support 4kx2k at 60 frames per sec
    Sub-levels (e.g. 3.1, 3.2 etc.) are not recommended
<number>

## Slide 4: Profiles and Levels
Fixed Profiles and Levels
  Profiles
    Naming convention
      Use neutral names, like Profile ‘A’, do not use the names like Main, High etc. that wrongly convey the focus of the standard and the attributes of the profiles
    Do not force fit the Onion (concentric) structure
    At this stage specify only one profile corresponding to the highest efficiency
<number>

## Slide 5: Profiles and Levels
Flexible Profiles and Levels
  Allow clients and servers to negotiate the coding tools and attributes associated with levels
    E.g., in AVC one can negotiate support of Constrained Baseline Profile + B pictures, or Main minus CABAC etc.
    Buffers’ sizes, maximum bit rate etc.
    As an example, negotiation can happen using XML
  Allow attributes associated with the coding tools to be negotiated
    E.g. maximum search range in B-pictures
<number>

## Slide 6: Profiles and Levels
Flexible Profiles and Levels
  HEVC should standardize the names of the coding tools that can be negotiated
  HEVC should standardize the attributes associated with those tools that can be negotiated
  HEVC should standardize the names of the various parameters associated with the Levels whose values can be modified
<number>