## Slide 1: H0667 Slice header element frequency issues
Ambarella

## Slide 2: Issues
Slices can occur every Treeblock (LCU)
Changes to some elements cause cache thrashing, pipeline stalls and flushing
high level syntax parsed in CPU not dedicated pipelines
Some elements in slice header intended for frequent use (1500 byte MTU) have light hardware impact.
Heavy impact elements rarely modulated throughout frame.

## Slide 3: Set analysis
Set | Hardware impact | Teleconf | Broad-cast
Modes (slice_type, Qp) | Light | Dynamic | Dynamic
reference picture management (short_term_ref_pic_set()) | Medium? | Static | Static
reference picture list modification | Medium | Dynamic | Static
Slice identifiers | Light | Dynamic | Dynamic
Parameter set identifiers | Light | Static+ | Static
Deblocking loop filter control | Heavy | Static | Static
ALF loop filter control | Medium | Dynamic | Static
Motion prediction weights | Light | Static | Static
Wavefront substream pointers | Light | ? | Dynamic

## Slide 4: Recommendations
Have a BoG-like detailed discussion between implementers and slice header connoisseurs to reach common understanding.
Move infrequently changing, medium-to-heavy impact elements into parent header (PPS, APS..)
Restrict the frequency of those elements wherever they are stuffed
Limit number of changes per frame to something that is appropriate to Profile & Level, so that entire set can be reasonably cached during whole frame.