## Slide 1: Sharp’s proposals for HEVC scalability Extension (m23618)
<number>
Hisao Kumai, Tomoyuki Yamamoto, Andrew Segall, Norio Ito
Sharp Corporation
MPEG 99th Meeting in San Jose, 6-10 February, 2012
Notes: <number>

## Slide 2: Overview summary
Introducing hybrid system for 4K2K broadcast using MPEG-2 video scalable coding is expected
  Current scope of HEVC scalability extension can only use H.264/AVC as base layer
  MPEG-2 video widely implemented in digital TV, and digital TV standard cannot change often
    Enhancement layer:4K2K HEVC via internet
    Base layer:HD MPEG-2 video via broadcast(existing system)
Sharp proposes a mixed-codec scalability modes for HEVC extension
  Add “light mode” using coding standard independent information given by base layer when coding enhancement layer
    Coding standard independent information: red arrow
    Coding standard dependent information: blue arrow
  The “light mode” is expected to give less computational or algorithmic complexity.
Experimental results(BD-rate) shows that adding such mode is valuable
    2x scalability Y: -32～-38% in RA HE with few modifications
    1.5x scalability Y: -13% in RA HE
<number>

## Slide 3
Notes: <number>

## Slide 4: Use cases for hybrid TV
<number>

## Slide 5: Experiments
<number>
 | 2x | 
 | HEVC | HEVC(EL)
IntraPeriod | 8 | only first
DecodingRefreshType | CDR | CDR
GOPSize | 8 | 8
I slice | 1 | only first
P slice | 0 | 1(inter-layer intra)
B slice | 3 | 3
b slice | 4 | 4
InternalBitDepth | 8 | 8
High Resolution vs. Enhancement Layer |  |  | 
 | Random access(Intra Period 8) |  | 
 | Y BD-rate[%] | U BD-rate[%] | V BD-rate[%]
Class A | -37.9 | -27.3 | -32.9
Class B | -37.5 | -26.1 | -30.2
Class C | -32.7 | -21.3 | -22.1
All | -36.0 | -24.9 | -28.4
 | 1.5x | 
 | HEVC | HEVC(EL)
IntraPeriod | 32 | only first
DecodingRefreshType | CDR | CDR
GOPSize | 8 | 8
I slice | 1 | only first
P slice | 0 | 1(inter-layer intra)
B slice | 15 | 3
b slice | 16 | 4
InternalBitDepth | 8 | 8
High Resolution vs. Enhancement Layer |  |  | 
 |  | Random access | 
 | Y BD-rate[%] | U BD-rate[%] | V BD-rate[%]
Class B | -13.0 | -7.2 | -9.9
2x Spatial Scalability
1.5x Spatial Scalability
test conditions
test conditions
results
results

## Slide 6: H.264/AVC and MPEG-2 video base layer compatibility mixed codec modes for scalability extension
<number>
    Red arrow: Coding standard independent information
    Blue arrow: Coding standard dependent information