## Slide 1
Long-term picture coding
JCTVC-H0694
Karsten Suehring, Heiko Schwarz, Thomas Wiegand

## Slide 2: Motivation
current coding uses delta lsb POC to signal long term pictures
problems:
values and used bits will get larger with increasing POC distance
lsb modulo coding might create conflicts unless the lsb is large
lt-POC: 150
lt-POC: 50
current POC: 200
50 ue(v)
100 ue(v)

## Slide 3: Proposed method
Only a restricted number pictures can actually be stored in DPB at any point in time
Full absolute or lsb POC is not necessary to identify a picture in DPB to be marked as long-term
Encoder only needs to encode a safe identification of the long-term picture in the DPB
  A bit-string taken from the binary representation of POC is used for identification
Encoder can choose to add additional identification information
  Trade-off between coding efficiency and error resilience

## Slide 4: Basic concept
Example 1: If the picture in the first line shall be identified among the candidates listed below, only one bit of the POC value is necessary.

## Slide 5: Basic concept
Example 2: If the POC values have more similarity, a longer bit-string may be necessary to safely identify the picture on the first line.
This happens only for small POC differences which is unlikely for long-term pictures

## Slide 6: Picture marking: 1 long-term
DPB
00000111
RPS
00001010
00001001
00001000
00000001
POC: 10
POC: 9
POC: 8
POC: 7
POC: 1
position: 2, size: 1, value: 0
short-term pictures don‘t need to be considered
Encoder chooses one identifying bit

## Slide 7: Picture marking: 1 long-term
DPB
00000111
RPS
00001010
00001001
00001000
00000001
POC: 10
POC: 9
POC: 8
POC: 7
POC: 1
position: 1, size: 1, value: 0
Encoder chooses another identifying bit

## Slide 8: Picture marking: 1 long-term
DPB
00000111
RPS
00001010
00001001
00001000
00000001
POC: 10
POC: 9
POC: 8
POC: 7
POC: 1
position: 1, size: 2, value: 00
Encoder chooses two identifying bits for increasing error resilience

## Slide 9: Picture marking: 1 long-term
DPB
00000111
RPS
00001010
00001001
00001000
00000001
POC: 10
POC: 9
POC: 8
POC: 7
POC: 1
position: 0, size: 8, value: 00000001
Encoder chooses eight identifying bits for increasing error resilience even more

## Slide 10: Picture marking: 2 long-term, first
DPB
00000111
RPS
00001010
00001001
00001000
00000001
POC: 10
POC: 9
POC: 8
POC: 7
POC: 1
position: 3, size: 2, value: 00
current
First long-term pictures needs at least two identifying bits

## Slide 11: Picture marking: 2 long-term, second
DPB
00000111
RPS
00001010
00001001
00001000
00000001
POC: 10
POC: 9
POC: 8
POC: 7
POC: 1
position: 3, size: 1, value: 1
current
After the first long-term picture has been coded, only one identifying bit is needed for the second long-term

## Slide 12: Syntax
if( long_term_ref_pics_present_flag ) { | 
num_long_term_pics | ue(v)
for( i = 0; i < num_long_term_pics; i++ ) { | 
delta_poc_lsb_lt_minus1[ i ] | ue(v)
used_by_curr_pic_lt_flag[ i ] | u(1)
lt_bit_pos[ i ] | u(4)
lt_bit_len[ i ] | un(v)
if (lt_bit_len>1) { | 
lt_bit_value[ i ] | u(v)
} | 
used_by_curr_pic_lt_flag[ i ] | u(1)
} | 

## Slide 13: Unary codes
Coding of bit string length and value
Concept:
Code | Value
1 | 
0 1 x0 | x0
0 0 1 x0 x1 | x0 x1
0 0 0 1 x0 x1 x2 | x0 x1 x2
... | ...

## Slide 14: Unary codes
Coding of bit string length and value
Improved code:
Code |  | Value
1 |  | 0
0 1 |  | 1
0 0 1 | x0 x1 | x0 x1
0 0 0 1 | x0 x1 x2 | x0 x1 x2
... |  | ...
lt_bit_len
lt_bit_value

## Slide 15: Results
Based on Common conditions for reference picture marking and list construction proposals
Case 2.6 (Interview type scene cuts)
 | 10/30 with 4800 frames | 20/60 with 9600 frames
HM 5.1 | 71827 | 144169
Proposal | 38255 | 10523
 | -46,74% | -46,83%
 | 10/30 with 4800 frames | 20/60 with 9600 frames
HM 5.1 | 71827 | 144169
Proposal | 38255 | 10523
 | -46,74% | -46,83%
60 fps
24 fps

## Slide 16: Results
Based on Common conditions for reference picture marking and list construction proposals
Case 3.3 (two long-term pictures based on decoder feedback)
 | 200 ms RTT 600 frames | 1000 ms RTT 600 frames
HM 5.1 | 10523 | 14375
Proposal | 9558 | 9231
 | -9,17% | -35,78%
60 fps
24 fps
 | 200 ms RTT 240 frames | 1000 ms RTT 240 frames
HM 5.1 | 3349 | 4787
Proposal | 3974 | 3629
 | 18,66% | -24,19%

## Slide 17: Picture marking: picture loss - encoder
DPB
00000111
RPS
00001010
00001001
00001000
00000001
POC: 10
POC: 9
POC: 8
POC: 7
POC: 1
position: 2, size: 1, value: 0
Previously marked unused
Encoder could choose one bit, if no errors are expected

## Slide 18: Picture marking: picture loss - decoder
DPB
00000111
RPS
00001010
00001001
00001000
00000001
POC: 10
POC: 9
POC: 8
POC: 7
POC: 1
position: 2, size: 2, value: 00
marking lost
Encoder chooses two bits, to avoid conflicts with lost markings

## Slide 19: Summary
Effective long-term coding (up to ~45% gain on long-term syntax elements)
Full 32-bit POC (no lsb issues)
Loss-aware encoding possible
  The encoder can choose the trade-off between coding efficiency and error resilience