## Slide 1: BoG report on interlace indicators

## Slide 2
Background
JCTVC agreed to define a picture-level SEI and VUI flag to signal interlace indications
  Picture-level SEI with 5 flags and 3 reserved bits
    A flag to indicate whether the coded picture is frame or field
    A flag to indicate the parity of each field
    A flag to indicate the scanning method of the original source of a coded sequence
    A flag to indicate whether the coded frame or field is a dummy frame resulting from a repetition process
    A flag to indicate which field is temporally first when a picture is a frame
  VUI flag specifies:
    Presence of the picture-level SEI
    Coded sequence shall contain coded pictures consisting of frames only (progressive or interlace) or fields only

## Slide 3
BoG output
It is agreed that redundant one flag in SEI is removed
  Picture-level SEI with 4 flags and 4 reserved bits
    A flag to indicate whether the coded picture is frame or field
    bottom_field_flag to indicate the parity of each field
    progressive_source_flag to indicate the scanning method of the original source of a coded sequence
    duplicate_flag to indicate whether the coded frame or field is a dummy frame resulting from a repetition process, such as 3:2 pulldown
    top_field_first_flag to indicate which field is temporally first when a picture is a frame
  VUI flag: field_sequence_flag
    Specify the presence of the picture-level SEI
    Specify that that a coded sequence shall contain coded pictures consisting of frames only (progressive or interlace) or fields only

## Slide 4
Recommendation
Review and adopt the draft text

## Slide 5
Appendix