## Slide 1: BoG report on reduction of SAO BO offset buffer (20:15-22:30, Feb. 4)
T. Yamakage (BoG Chair)
JCTVC-H0726

## Slide 2: Summary
Participants
  Patrice Onno (Canon)
  Woo-Shik Kim, Do-Kyoung Kwon, Madhukar Budagavi (TI)
  Tomohiro Ikai (Sharp)
  Ohji Nakagami, Ali Tabatabai, Ehsan Maani (Sony)
  Koohyar Minoo, Yue Yu (Motorola Mobility)
  Yu-Wen Huang (MediaTek)
  Elena Alshina (Samsung)
  Toru Matsunobu (Panasonic)
  Chaired by T. Yamakage
4 (+ 1) contributions reviewed
  H0436, H0174, H0406, H0438 (and H0553)
Recommendation
  To study 3 candidates for adoption
JCTVC-H0726

## Slide 3: Background Information
Current syntax worst case (WD 5)
  256 regions x 16 offsets x 4 bits x 3 colors (for 8bit )
    49,152 bits = 6,144 bytes / picture
If LCU-based syntax is adopted, reduction of number of band offset has more benefit from the viewpoint of coding efficiency (i.e., overhead reduction)
JCTVC-H0726

## Slide 4: Contributions Reviewed
CE8.d.1: JCTVC-H0436 (TI)
  Select from 4 fixed groups, 8 bands, for luma and chroma
CE8.e.2: JCTVC-H0174 (Canon)
  Proposal-A: 1 floating group, 8 bands, select from 3 modes, signalling center position, for luma and chroma
  Proposal-B: 1 floating group, 8 bands, 1 mode, signalling center position of the band, for luma and chroma
Non-CE: JCTVC-H0406 (Sony)
  Floating 1 group with 4 bands for chroma
Non-CE: JCTVC-H0438 (TI/Sharp)
  Select from 4 fixed groups, 8 band for luma
  Select from 4 fixed group, 8 bands with half size of band (only center) for chroma
Non-CE: JCTVC-H0553 (Motorola Mobility)
  LCU based, no need to signal offset position 4 Bands for BO_0 and 8 bands for BO_1
JCTVC-H0726

## Slide 5: Comparison of Each Proposal
H0436
H0438
H0174
H0406
JCTVC-H0726

## Slide 6: Comparison Table (1/2)
 |  |  | BD-rate |  |  |  | 
 |  |  | Y | Cb | Cr | description | complexity
WD5 |  |  |  |  |  |  | 
H0174-B | Canon | CE | 0.0% | -0.4% | -0.3% | 1 floating group, 8 band, 1 mode, center position of the band, for luma and chroma | Offset buffer in decoder size is 1/2 for luma and chroma, need signalling of center
H0438 | TI/Sharp | Non-CE | 0.0% | -1.0% | -1.0% | 4 fixed group, 8 band for luma, 4 fixed group, 8 bands with half size of band (only center) for chroma | Offset buffer in decoder size is 1/2 for luma and chroma
H0406 | Sony | Non-CE | 0.0% | -0.4% | -0.4% | 1 floating group, 4 band, 1 mode, starting position of the band, for luma and chroma | Offset buffer in decoder size is 1/4 for luma and chroma, need signalling of center
H0174-A | Canon | CE | 0.0% | -1.7% | -1.9% | 1 floating group, 8 band, selected from 3 modes, center position, for luma and chroma | Offset buffer in decoder size is 1/2 for luma and chroma, need signalling of center
H0436 | TI | CE | 0.0% | -0.3% | -0.3% | 4 fixed group, 8 band, luma and chroma | Offset buffer in decoder size is 1/2 for luma and chroma
JCTVC-H0726

## Slide 7: Comparison Table (2/2)
 | Decoder buffer in bytes | Decoder LUT (if all LUT table scheme is implemented) | Encoder | Enc relative to HM5 BO (BO is below 0.5% of total encoding time) | cross-check | WD | SW to CE8
WD5 | 6144 | 32*3 | Decide from 2 BO modes | 1x |  |  | 
H0174-B | 3552 | 32*3 | Determine center offset | 1x | H0229 | yes | yes
H0438 | 3072 | 32*3 | Decide from 4 BO modes | 1x | H0338 | yes | no
H0406 | 2016 | 32*3 | Determine center offset | 1x | H0617 | yes | no
H0174-A | 3552 | 32*4*3 | Determine center offset, decide from 3 modes | 1.2x | H0229 | yes | yes
H0436 | 3072 | 32*3 | Decide from 4 BO modes | 1x | H0332 | yes | yes
Recommendation:
To study H0174-b, H0438 and H0406 for adoption.
JCTVC-H0726

## Slide 8: JCTVC-H0553 (LCU-based SAO)
Determine min and max value of LCU
  From 64x64 pixels, need to find mix/max value.
  2 comparison per pixel
  No need to signal mix/max value per LCU
    Encoder and decoder can operate in the same manner
    4 bands for BO_0
    8 bands for BO_1
JCTVC-H0726