## Slide 1: BoG report on non-CE ALF contributions (14:30-18:00, Feb. 5 16:10-17:30, Feb.6)
T. Yamakage (BoG Chair)
JCTVC-H0732_r2

## Slide 2: Participants
Kenneth Andersson (Ericsson)
Yu-Wen Huang, Chig-Yeh Chen (MediaTek)
Madhukar Budagavi, Munhua Zhou (TI)
Seishi Takamura, Masaaki Matsumura, Shohei Matsuo (NTT)
Peisong Chen (Broadcom)
Semih Esenlik (Panasonic)
Kei Kawamura (KDDI)
Kazuo Sugimoto (Mitsubishi)
Ali Tabatabai, Ehsan Maani, Masaru Ikeda (Sony)
R. Allen (Altera)
PoLin Lai (Samsung)
In Suk Chong (Qualcomm)
Tomohiro Ikai (Sharp)
Chaired by T. Yamakage

## Slide 3: Contributions reviewed
JCTVC-H0372 Panasonic Proposal
  Non-CE8: Line memory reduction fix at independent slice and tile boundaries
JCTVC-H0571 eBrisk/Samsung Information
  A Comparison of HM-5.0 ALF with H0068’s Proposed Single-Shape ALF for Some Video Sequences
JCTVC-H0418 Samsung Proposal
  Non-CE8: Unification of k-index mapping for ALF luma filter coefficients of the two shapes
JCTVC-H0409 Sony Proposal
  Harmonization of number of ALF classes between RA and BA modes
JCTVC-H0415 Samsung/Sony Proposal
  Non-CE8: ALF BA feature computation only accessing 3x3 area
JCTVC-H0094 NTT Proposal
  Non-CE8: Modification of directional classification for block-based adaptation on ALF
JCTVC-H0483 Sharp Proposal
  Harmonization of ALF Luma and Chroma Center Coefficient Prediction
JCTVC-H0420 Samsung Information
  Non-CE8: Information on codebook size for LCU-based ALF

## Slide 4: JCTVC-H0372 (Panasonic) –1/3–
Title:
  Non-CE8: Line memory reduction fix at independent slice and tile boundaries.
VB processing
Problem
  In the case when the loop filters are not allowed to use samples from the neighbouring slice or tile, double padding at independent slice and tile boundaries. At independent slice and tile boundaries, boundary padding and VB padding are applied at the same time.

## Slide 5: JCTVC-H0372 (Panasonic) –2/3–
Proposal
  Switch off VB padding at independent slice and tile boundaries.
    If the loop_filter_across_slice_flag is 0, VB padding is not applied at the horizontal slice boundaries in ALF operation.
    If the tile_boundary_independence_idc is 1 and loop_filter_across_tile_flag is 0, VB padding is not applied at the horizontal tile boundaries in ALF operation.
  "num_sgu_alf_padding" needs to be signalled in slice header.
Benefits
  Coding gain 0.2% for independent tiles and 0.1% for independent slices. Improvement in the subjective quality.
VB processing

## Slide 6: JCTVC-H0372 (Panasonic) –3/3–
Discussion
  How many LCUs are included needs to be signalled. This approach works for tile and fixed size slice. When MTU based slice is used, this signalling may not be helpful. Inserting the number of LCU in the slice header is difficult. This would not work MTU based slice. Not completely remove the problem, but this should be solved. Due to lack of deblocking filter.
  The syntax element comes after CU flag? May be signalled in LCU by CABAC. Therefore, not so much impact on coding efficiency (e.g. 0.1 bit per LCU). This flag can be combined with slice end flag.
  Some coding artifact is observed on the presented still image. Is this because of this proposal? No.
Recommendation
  Subjective viewing is recommended in the future in AHG/CE.
VB processing

## Slide 7: JCTVC-H0409 (Sony) –1/2–
Title:
  Harmonization of number of ALF classes between RA and BA modes
Proposal:
  16 classes are possible for the BA mode instead of current 15 classes in WD5 in order to harmonize the number of classes between RA and BA modes. This method merges the smooth areas into one class since they do not have any directional characteristics.
BA feature
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Quantized block activity
Block direction
HM 5.0
Proposed
1
2
3
4
6
7
8
9
0
11
12
13
14
Quantized block activity
Block direction
5
10
15

## Slide 8: JCTVC-H0409 (Sony) –2/2–
Discussion:
  Question about subjective quality. This is simplification. One expert expressed that this will not harm subjective picture quality.
  Needs to improve the text.
  3 or 4 branch will be removed.
Recommendation:
  Recommend adoption (refer to JCTVC-H0409-v5)
BA feature

## Slide 9: JCTVC-H0415 (Samsung/Sony) –1/2–
Title:
  Non-CE8: ALF BA feature computation only accessing 3x3 area
Proposal:
BA feature

## Slide 10: JCTVC-H0415 (Samsung/Sony) –2/2–
Discussion:
  In general, preferable to narrow memory access area.
  Computation benefit.
  Does not have significant meaning when the current filter shapes are used.
  0.1-0.2% loss.
  Inconsistency with the current or newly adopted filter shape
Recommendation:
  No action
BA feature

## Slide 11: JCTVC-H0094 (NTT) –1/2–
Title:
  Non-CE8: Modification of directional classification for block-based adaptation on ALF
Proposal:
  A flexible directional classification framework for BA that allocates a directional classification pattern to each classified activity domain is proposed.
BA feature

## Slide 12: JCTVC-H0094 (NTT) –2/2–
Discussion:
  What is the purpose of this proposal?
  Improvement. But, on average, loss is observed. Gain is up to 0.03%.
  If it is simplification, new branch is necessary, but if skip is adopted, some filtering operation can be skipped. Therefore, average filtering operations may be reduced. But seems to add the complexity. In worst case, same as WD5. In encoder, somehow worse than HM5. How many operations are additionally required?
  May reduce the average decoding time by using ""DirNone"". Enc time reduction 1%, dec time reduction 2-3%. No subjective picture quality loss. Objective loss is about 0.1%. Max of 3% dec time reduction.
  Adding flexibility may increase complexity.
  An organization supports to adopt.
Recommendation:
  Further study in AHG/CE.
BA feature

## Slide 13: JCTVC-H0483 (Sharp) –1/2–
Title:
  Harmonization of ALF Luma and Chroma Center Coefficient Prediction
Problem statement:
  Regarding Chroma center coefficient coding,
    – If i is equal to AlfCodedLengthChroma – 1, the coefficient cC[i] is derived as
    cC[ i ] = 255 – sum – alf_coeff_chroma[ i ]
    Where
    sum = alf_coeff_chroma[ AlfCodedLengthChroma – 2 ] + j( alf_coeff_chroma[ j ] << 1 ) (8 469)
    with j = 0..AlfCodedLengthChroma – 3
  The luma filter coefficients cL with elements cL[ i ][ j ], i = 0..AlfNumFilters–1, j = AlfCodedLengthLuma–1 are derived as follows:
    If alf_pred_method_is equal to 0 or the value of i is equal to 0,
      cL[ i ][ j ] = alf_coeff_luma[ i ][ j ] + 255 – k(2*alf_coeff_luma[ i ][ k ]) – 2*cL[ i ][ j – 1 ]
    where k=0..j-2
  An inconsistency the ALF coefficient coding for luma and chroma
Filter shapes

## Slide 14: JCTVC-H0483 (Sharp) –2/2–
Proposal
  Option (2): If changing Chroma center coefficient coding to match with Luma, the text of Chroma center coefficient coding would be changed to:
    If i is equal to AlfCodedLengthChroma – 1, the coefficient cC[i] is derived as
      cC[ i ] = alf_coeff_chroma[ i ] + 255 – sum; (8 468)
    where
      sum = alf_coeff_chroma[ AlfCodedLengthChroma – 2 ] + j( alf_coeff_chroma[ j ] << 1 ) (8 469)
    with j = 0..AlfCodedLengthChroma – 3
Recommendation
  Recommend adoption (to follow as luma processing for center coefficient prediction, i.e., option 2 in H0483_r2)
Filter shapes

## Slide 15: JCTVC-H0420 (Samsung)
Title:
  Non-CE8: Information on codebook size for LCU-based ALF (Information)
Abstract:
  Informational results of using variable codebook size for LCU-based ALF implemented on top of the latest release of CE8.a.2 is presented, in which the codebook size is set to be resolution-dependent. Results indicate increasing codebook size for high resolution does not improve coding efficiency.
Recommendation
  No action.
Filter shapes

## Slide 16: JCTVC-H0571 (eBrisk/Samsung) –1/3–
Title:
  A Comparison of HM-5.0 ALF with H0068’s Proposed Single-Shape ALF for Some Video Sequences
  Information document, but rather proposing to keep the current filter shapes (two filter shapes)
Abstract:
  The advantages of using HM-5.0’s two ALF filter shapes are reported. Using both common-test-set and non-common-test-set video sequences, it is shown that a single-shape ALF solution (CE8.b.2) doesn’t allow enough adaptively to handle all kinds of video content.
Filter shapes

## Slide 17: JCTVC-H0571 (eBrisk/Samsung) –2/3–
Presentation by TI
Filter shapes
New slide
 | AI-HE |  |  | RA-HE |  |  | LB-HE |  |  | LP-HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Average | -0.1% | -0.2% | -0.2% | -0.1% | -0.3% | -0.5% | 0.1% | -0.3% | -0.3% | 0.0% | -0.4% | -0.6%
Min | -0.3% | -1.2% | -0.9% | -0.5% | -1.9% | -1.9% | -0.3% | -1.3% | -2.0% | -0.4% | -3.1% | -2.2%
Max | 0.1% | 0.1% | 0.1% | 0.3% | 0.3% | 0.2% | 0.5% | 0.9% | 0.5% | 0.5% | 0.9% | 0.2%
BD-Rate on 19 additional sequences
(VQEG, KTA, EBU, TU-Munich)

## Slide 18: JCTVC-H0571 (eBrisk/Samsung) –3/3–
Discussion:
  On average, not big difference, but some difference on some video conferencing sequences. For some KTA sequences, not good as well (max 1.5%, ave. 0.8% loss), in particular zoom and pan (for non common test condition 3 sequences). Should not focus on one particular point. How many outliers were there when the current shape was adopted in Torino?
  Subjective viewing of Vidyo1 did not show significant difference (CI overlaps).
  Why Class F is omitted in this presentation? Recommendation is to show min and max.
  Two shapes can be implemented in a single shape (Cf. H0418). How can it be achieved? Same complexity?
Suggestion by the BoG chair:
  To provide absolute gain of the particular sequences and confirm relative loss by single filter shape, and then re-visit.
Recommendation
  No evidence to revert the decision of Session A to adopt JCTVC-H0068
Filter shapes

## Slide 19: JCTVC-H0418 (Samsung) –1/2–
Title:
  Non-CE8: Unification of k-index mapping for ALF luma filter coefficients of the two shapes
Problem:
  The k-index mapping maps ALF luma coefficients to different order of exponential Golomb code. In HM5.0, the two k-index mapping tables for two filter shapes have different index ranges, leading to additional processing steps in entropy coding and decoding for ALF luma coefficients.
Proposal:
  Unification of k-index mapping for ALF luma filter coefficients of the two shapes is proposed (i.e., remove k-index syntax, i.e., one flag is sufficient).
  The unification of k-index mapping tables using the same index range removes the associated processing steps, with exactly the same coding results.Syntax change is proposed.
Filter shapes

## Slide 20: JCTVC-H0418 (Samsung) –2/2–
Discussion:
  Encoder can have a choice to save the burden. Single shape is for simplification.
  Even if this simplification, coefficient (multiplexer) position is different. In hardware, need to share multiplier. Need to design filter twice.
  Multiplier can be shared, with small overhead of multiplexer in decoder.
  In encoder, may need two filters to be processed. It can be implemented by one filter operation, since filter shape can be determined when filter coefficients are designed (Estimated error can be obtained from the correlation matrix and the designed filter coefficients).
Recommendation:
  Conditionally, recommend for adoption, if two shapes are kept.  No action
Filter shapes