## Slide 1: Analysis of differences of various ALF signalling schemes
<number>
2012/02/08
JCTVC-H0735
Tomoo Yamakage
JCTVC-H0735

## Slide 2: Purpose
Various ALF schemes are proposed to support various application domains
  Video conferencing: two-way communication, low latency
  Broadcasting: one-way transmission, live or long latency
  VOD, DVD, BD, etc.: one-way transmission, long latency
All applications are equally important for HEVC
  However, each signalling scheme has pros. and cons.
This contribution analyzes various ALF schemes, mainly in terms of latency point of view, in order to provide information to the committee members so that the members can find the best way
Discussion of syntax part and signal processing part (decoder) should be isolated
<number>
2012/02/08
JCTVC-H0735

## Slide 3: Introduction: How ALF encoder works
From R-D point of view, Wiener-based filter design has been adopted in HM
  Other filter design schemes might be possible (e.g. optimize for subjective picture quality --- some proprietary scheme will be developed in the future)
Wiener-based filter is designed by the following steps:
  Gather the statistics (distortion) of a region during encoding the region
    A region may be a picture, a slice (sub-frame), or an LCU
    Depending on the size of the region, latency will vary
      Larger region enables various optimization, but latency increases
  Design optimal filter coefficients by solving the correlation matrix
  Apply the designed filter to a block (LCU or CU) and determine whether the block should be filtered based on distortion (filter on vs off)
  Note 1: This process can be decoupled from signalling
<number>
2012/02/08
JCTVC-H0735

## Slide 4: Various proposed schemes
Current design (WD5 / HM5)
  ALF coef. signalling: APS
  CU flag signalling: Slice header
JCTVC-H0066
  ALF coef. signalling: LCU data
  LCU flag signalling: LCU data
JCTVC-H0274
  ALF coef. signalling: Slice header or APS
  CU flag signalling: Slice header
<number>
2012/02/08
JCTVC-H0735

## Slide 5: Differences of signalling in various ALF schemes
 | WD5 | H0066 | H0274
ALF coef. | APS | LCU | Slice header
CU on/off | Slice header | LCU | Slice header
<number>
2012/02/08
JCTVC-H0735
SPS
PPS
APS
Slice header
Slice data
H0066
LCU
LCU
LCU
SPS
PPS
APS
Slice header
Slice data
H0274
SPS
PPS
APS
Slice header
Slice data
WD5
LCU level on/off only

## Slide 6: How H0066 singalling can achieve picture-based encoding
Gather the statistics of a picture during encoding
Design optimal filter coefficients by solving the correlation matrix
Apply the designed filter to each block (LCU) and determine whether the block should be filtered based on distortion (filter on vs off)
Interleave filter coefficients and LCU on/off flag into each LCU data
  Interleaving is difficult, since LCU data has been encoded by CABAC
<number>
2012/02/08
JCTVC-H0735
SPS
PPS
APS
Slice header
Slice data
H0066
LCU
LCU
LCU

## Slide 7: How H0274 singalling can achieve LCU-based encoding
Gather the statistics of an LCU during encoding the LCU
Design optimal filter coefficients by solving the correlation matrix
Apply the designed filter to the block (LCU or CU) and determine whether the block should be filtered based on distortion (filter on vs off)
Store LCU data to a buffer, and filter coefficients and CU on/off flag(s) to the other buffers
  Number of generated bits for the LCU can be derived exactly, therefore, MTU-size slice scenario can be realized in the same manner as H0066
  Marginal complexity increase to use several buffers
When a slice encoding is completed, transmission of the slice header/data can start
<number>
2012/02/08
JCTVC-H0735
SPS
PPS
APS
Slice header
Slice data
H0274

## Slide 8: Comparison chart
 | Picture-based encoding | LCU-based encoding (incl. MTU-size slice) | Latency to start transmission (*) (*) 1280x720@60p is assumed. |  | 
 |  |  | 1 slice/pic | Multiple-slice/pic (e.g. 2 slices/pic) | MTU-size slice
WD5 | OK | OK, but marginal complexity | Picture ( < 17 msec.) | Picture ( < 17 msec.) | Picture ( < 17 msec.)
H0066 | Possible, but high complexity | OK | Slice ( < 17 msec. ) (*) | Slice ( < 9 msec.) (*) | Slice ( < 9 msec.) (*)
H0274 | OK | OK, but marginal complexity | Picture ( < 17 msec.) | Slice ( < 9 msec.) | MTU/Picture ( < 17 msec.)
<number>
2012/02/08
JCTVC-H0735
(*) If transmission of a slice will start right after all slice data is ready.
Note: Assuming 1x realtime encoder.

## Slide 9: Question: How to evaluate the latency of MTU-based slice?
Class E sequences are regarded as typical video conference sequences
  1280 x 720 @60p
  3 kbits / picture@Qp37, which is much smaller than MTU size
If we assume the smallest overhead to carry HEVC data, 4 pictures/MTU.
  Latency due to MTU size packing becomes 4 pictures!
If we assume one MTU carries one picture data or a part of picture data, overhead to pack a picture into MTU is significant.
  3 kbits for picture data, 9 kbits for padding!
<number>
2012/02/08
JCTVC-H0735
Sequence | Qp | kbps
Vidyo1 | 22 | 2101.31
 | 27 | 755.67
 | 32 | 359.13
 | 37 | 189.94
Vidyo3 | 22 | 2773.94
 | 27 | 900.83
 | 32 | 419.15
 | 37 | 222.22
Vidyo4 | 22 | 2386.76
 | 27 | 751.02
 | 32 | 325.50
 | 37 | 168.28
HM 5.0 anchor data
The discussion of MTU-based slice and latency should be isolated.

## Slide 10: Conclusion
Various ALF schemes are analyzed from the viewpoint of latency
Both H0066 and H0274 can support picture-based encoding
  H0066 encoder requires high complexity (i.e., interleaving)
Both H0066 and H0274 can support fixed slice encoding
  H0274 encoder requires marginal complexity (i.e., buffering)
Both H0066 and H0274 can support MTU-based slice encoding
  H0274 encoder requires marginal complexity (i.e., buffering)
The latency becomes slice-level latency in both cases.
  If transmission of a slice will start right after all slice data is ready.
<number>
2012/02/08
JCTVC-H0735
Considering the provided information, the committee should discuss the best way.