## Slide 1: Two ALF Configurations in CD/HM6
<number>
2012/04/xx
Picture-based ALF (Picture optimization)
  For high efficiency with high latency  Random Access
  When designing ALF coef., current frame is used. Therefore, the encoding of whole picture is performed at first, and then, ALF coef. is designed and CU level filter control (on/off) is determined.
LCU-based ALF (Slice-based signalling) (LCU Optimization)
  For good efficiency with low latency  AI, LB and LP
  During the encoding of each LCU, ALF coef. is designed using current frame and CU level filter control (on/off) is determined.
<number>
On/off ctrl
Coef.
SPS
PPS
APS
Slice header
Slice data
APS mode
SPS
PPS
APS
Slice header
Slice data
Slice header mode

## Slide 2: HM-6.0 ALF
Picture optimization
  Anchor: ALF-off
  Test: ALF-on w/ ticket #400?
  Inaccurate run times
Main (AI/RA/LDB/LDP)
  -1.7%/ -3.2% / -2.3% / -3.2% (ave.)
  -2.9%/ -4.8% (Class A)
HE10 (AI/RA/LDB/LDP)
  -1.9%/ -3.4%/ -2.5%/ -3.7% (ave.)
  -3.0%/ -5.1% (Class A)

## Slide 3: HM-6.0 ALF
LCU optimization
  Anchor: ALF-off
  Test: ALF-on w/ CE2 restriction
  Inaccurate run times
Main (AI/RA/LDB/LDP)
  -1.1%/ -2.0% / -1.6% / -2.7% (ave.)
  -2.0%/ -3.0% (Class A)
HE10 (AI/RA/LDB/LDP)
  -1.2%/ -2.2%/ -1.6%/ -3.1% (ave.)
  -2.1%/ -3.4% (Class A)

## Slide 4: CE2 Subtests
Simplification study
  CE2.b: Simplification of ALF signalling
  CE2.e: Depth of LCU division for filtering control
  Recommend to adopt all simplifications
Slice boundary processing study for LCU-based mode
  CE2.f: Line memory reduction fix at independent slice and tile boundaries
   Make recommendation after subjective viewing
Signalling/syntax study
  CE2.a: Signalling mode change from "switch between APS mode and slice header mode" to "switch between APS mode and interleaving mode“
   Recommend CE2.a.1 and CE2.a.2 as baseline Options and further study in AHG6
BA vs RA study, including BA simplification
  CE2.c: Number of classes in BA mode
  CE2.d: Number of regions in RA mode
   Discuss CE2.c to reduce testing for further study in AHG6
Encoder optimization study for LCU-based encoding (non-normative)
  CE2.g: Encoder complexity reduction for LCU-based optimization
Luma/chroma filter coefficients unification study in LCU-based encoding
  CE2.h: Reuse luma filter coefficients in chroma filtering for LCU-based optimization
   Should be integrated IF Option 1 or 3 in AHG6 further study is recommended
Combination study
  CE2.i: Combination subtests
   Not adopted as it is (further study in conceptually in AHG6)
<number>
2012/04/xx

## Slide 5: CE2 Subtests
Simplification study
  CE2.b: Simplification of ALF signalling
  CE2.e: Depth of LCU division for filtering control
  Recommend to adopt all simplifications
Slice boundary processing study
  CE2.f: Line memory reduction fix at independent slice and tile boundaries
   Make recommendation after subjective viewing
Signalling/syntax study
  CE2.a: Signalling mode change from "switch between APS mode and slice header mode" to "switch between APS mode and interleaving mode“
   Recommend CE2.a.1 and CE2.a.2 as baseline Options and further study in AHG6
BA vs RA study, including BA simplification
  CE2.c: Number of classes in BA mode
  CE2.d: Number of regions in RA mode
   Discuss CE2.c to reduce testing for further study in AHG6
Encoder optimization study for LCU-based encoding (non-normative)
  CE2.g: Encoder complexity reduction for LCU-based optimization
Luma/chroma filter coefficients unification study in LCU-based encoding
  CE2.h: Reuse luma filter coefficients in chroma filtering for LCU-based optimization
   Should be integrated IF Option 1 or 3 in AHG6 further study is recommended
Combination study
  CE2.i: Combination subtests
   Not adopted as it is (further study in conceptually in AHG6)
<number>
2012/04/xx

## Slide 6: Results of CE2.b and CE2.e for Simplification
Anchor = HM-6.0 CE2 anchor |  | Picture-based ALF |  |  |  | LCU-based ALF |  |  | 
Test |  | AI | RA | LDB | LDP | AI | RA | LDB | LDP
 |  | Y | Y | Y | Y | Y | Y | Y | Y
CE2.b.1 | Remove Run prediction | 0.0% | 0.0% | 0.0% | 0.0% | N/A | N/A | N/A | N/A
CE2.b.2 | Remove explicit K table | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
CE2.b.3_1 | alf_pred_flag = 1 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
CE2.b.3_0 | alf_pred_flag = 0 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
CE2.b.4_1 | alf_nb_pred_luma_flag = 1 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
CE2.b.4_0 | alf_nb_pred_luma_flag = 0 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
CE2.b.5 | QP independent quant. | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | 0.3%
CE2.e.1_2 | CU ctrl depth <= 2 | 0.0% | 0.0% | 0.0% | 0.0% | N/A | N/A | N/A | N/A
CE2.e.1_1 | CU ctrl depth <= 1 | 0.0% | 0.0% | 0.0% | 0.0% | N/A | N/A | N/A | N/A
CE2.e.1_0 | CU ctrl depth <= 0 | 0.0% | 0.1% | 0.1% | 0.1% | N/A | N/A | N/A | N/A
<number>
2012/04/xx

## Slide 7: CE2 Recommendation for Simplification of ALF
CE2.b.1: Remove run prediction of ALF coefs.  No loss
  Remove run prediction of ALF coefs. in APS in picture-based ALF. (Cf. No run prediction in LCU-based ALF.)
CE2.b.2: Remove explicit signaling of K-table  No loss
  Remove explicit signaling of K-table in both picture-based ALF and LCU-based ALF. (i.e., Implicit K-table will be used.)
CE2.b.3: Remove alf_pred_flag  No loss
  Remove alf_pred_flag and not to use prediction in both picture-based ALF and LCU-based ALF.
CE2.b.4: Remove alf_nb_pred_luma_flag  No loss
  Remove alf_nb_pred_luma_flag and not to use prediction in both picture-based ALF and LCU-based ALF.
CE2.b.5: Qp independent quantization in LCU mode 0.1-0.3% loss
  Use Qp independent quantization of ALF coefs. in LCU-based ALF. (i.e., same as picture based ALF)
CE2.d.1: Depth of CU division  0.1% loss (Depth=0, i.e., LCU on/off)
  Use only LCU level on/off control in picture-based ALF. (i.e., same as LCU-basd ALF)
<number>
2012/04/xx

## Slide 8: CE2 Subtests
Simplification study
  CE2.b: Simplification of ALF signalling
  CE2.e: Depth of LCU division for filtering control
  Recommend to adopt all simplifications
Slice boundary processing study
  CE2.f: Line memory reduction fix at independent slice and tile boundaries
   Make recommendation after subjective viewing
Signalling/syntax study
  CE2.a: Signalling mode change from "switch between APS mode and slice header mode" to "switch between APS mode and interleaving mode“
   Recommend CE2.a.1 and CE2.a.2 as baseline Options and further study in AHG6
BA vs RA study, including BA simplification
  CE2.c: Number of classes in BA mode
  CE2.d: Number of regions in RA mode
   Discuss CE2.c to reduce testing for further study in AHG6
Encoder optimization study for LCU-based encoding (non-normative)
  CE2.g: Encoder complexity reduction for LCU-based optimization
Luma/chroma filter coefficients unification study in LCU-based encoding
  CE2.h: Reuse luma filter coefficients in chroma filtering for LCU-based optimization
   Should be integrated IF Option 1 or 3 in AHG6 further study is recommended
Combination study
  CE2.i: Combination subtests
   Not adopted as it is (further study in conceptually in AHG6)
<number>
2012/04/xx

## Slide 9: Results of CE2.f
<number>
2012/04/xx
Anchor = HM-6.0 CE2 anchor |  |  | Picture-based ALF |  |  |  | LCU-based ALF |  |  | 
Test |  | Summary | AI | RA | LDB | LDP | AI | RA | LDB | LDP
 |  |  | Y | Y | Y | Y | Y | Y | Y | Y
CE2.f.1 | H0372 (line memory) | Switching off the Virtual Boundary padding at bottom tile boundaries when loop_filter_across_tiles_enabled_flag is equal to 0 | -0.1% | -0.1% | -0.1% | -0.1% |  |  |  | 
Decision will be made after subjective viewing

## Slide 10: CE2 Subtests
Simplification study
  CE2.b: Simplification of ALF signalling
  CE2.e: Depth of LCU division for filtering control
  Recommend to adopt all simplifications
Slice boundary processing study
  CE2.f: Line memory reduction fix at independent slice and tile boundaries
   Make recommendation after subjective viewing
Signalling/syntax study
  CE2.a: Signalling mode change from "switch between APS mode and slice header mode" to "switch between APS mode and interleaving mode“
   Recommend CE2.a.1 and CE2.a.2 as baseline Options and further study in AHG6
BA vs RA study, including BA simplification
  CE2.c: Number of classes in BA mode
  CE2.d: Number of regions in RA mode
   Discuss CE2.c to reduce testing for further study in AHG6
Encoder optimization study for LCU-based encoding (non-normative)
  CE2.g: Encoder complexity reduction for LCU-based optimization
Luma/chroma filter coefficients unification study in LCU-based encoding
  CE2.h: Reuse luma filter coefficients in chroma filtering for LCU-based optimization
   Should be integrated IF Option 1 or 3 in AHG6 further study is recommended
Combination study
  CE2.i: Combination subtests
   Not adopted as it is (further study in conceptually in AHG6)
<number>
2012/04/xx

## Slide 11: Results of CE2.a
<number>
2012/04/xx
CE2.a.1 as baseline of Option 1 (LCU-mode) for further AHG6 study
CE2.a.2 as baseline of Option 3 (LCU-mode) for further AHG6 study
Anchor = HM-6.0 CE2 anchor |  |  | Picture-based ALF |  |  |  | LCU-based ALF |  |  | 
Test |  | Summary | IO | RA | LDB | LDP | IO | RA | LDB | LDP
 |  |  | Y | Y | Y | Y | Y | Y | Y | Y
CE2.a.1 | LCU-based signalling (1 filters) | Move ALF parameters from slice header to slice data (LCU interleaved way) | N/A | N/A | N/A | N/A | 0.0% | 0.0% | -0.1% | -0.2%
CE2.a.2_16_1 | CE2.a.1 + APS (16 APS filters, 1 LCU filter) | Allow each LCU to use picture-level ALF coefficients signalled in APS | N/A | N/A | N/A | N/A | -0.4% | -0.7% | -0.3% | -0.6%
CE2.a.2_1_1 | CE2.a.1 + APS (1 APS filter, 1 LCU filter) |  | N/A | N/A | N/A | N/A | -0.1% | -0.3% | -0.1% | -0.3%

## Slide 12: Additional Test for LCU mode
Option 1 (Same syntax structure as CE2.a.1)
  Nothing in APS, new filter or codebook filter or off in LCU (no BA/RA)
Option 2-1 (RA), Option 2-2 (BA)
  RA/BA information and filter coefficients in APS, on/off in LCU
Option 3-1 (RA), Option 3-2 (BA)
  RA/BA information and filter coefficients in APS,
  new filter or codebook filter or selecting APS filter or off in LCU
<number>
2012/04/xx
SPS
PPS
APS
Slice header
Slice data
LCU
LCU
LCU
On/off ctrl
Coef. or index
AHG6 activity
SPS
PPS
APS
Slice header
Slice data
LCU
LCU
LCU
CE2.a.2
16 or 1 filters
Single filter
SPS
PPS
APS
Slice header
Slice data
LCU
LCU
LCU
CE2.a.1
Single filter

## Slide 13: Option 1 (CE2.a.1 syntax + Simplification)
Syntax structure for LCU mode
  Nothing in APS, new filter or codebook filter or off in LCU (no BA/RA)
  Encoding scheme
    In each LCU, ALF coef. is designed using the original data of the current LCU
    Whether the designed coef .or a coef. in the codebook that stores previously signalled coefs. is used or off is decided
  Possible implementation problem
    Need to store coef. For above LCU row
      Can be solved by shifting ALF filtering by 4 lines (Cf. JCTVC-F271)
SPS
PPS
APS
Slice header
Slice data
LCU
LCU
LCU
On/off ctrl
Coef. or index
Single filter
<number>
AHG6 activity

## Slide 14: Option 2 (Simplification of CE2.a.2 syntax)
Syntax structure for LCU mode (2-1:RA), (2-2:BA)
  RA/BA information and filter coefficients in APS, on/off in LCU
  Encoding scheme 1 (Coef. design using previous frames)
    During encoding of previous frames, statistics of ALF on LCUs is collected
    Design Wiener-based filters based on the statistics
    Use one of the designed RA/BA filters as filter information signalled in APS
      A set of designed filters with the same temporal level may be used
    During encoding of an LCU, ALF on/off is decided on the fly
  Encoding scheme 2 (Coef. design using current frame)
    Same design scheme as above, but ALF on/off can not be decided on the fly during the first-pass encoding
  Possible implementation problem
    For scheme 2, two-pass encoding or ALF on/off flag interleaving is needed
<number>
2012/04/xx
SPS
PPS
APS
Slice header
Slice data
LCU
LCU
LCU
On/off ctrl
Coef.
16 filters
AHG6 activity

## Slide 15: Option 3 (CE2.a.2 syntax + Simplification)
Syntax structure for LCU mode (3-1:RA), (3-2:BA)
  RA/BA information and filter coefficients in APS,
  new filter or codebook filter or selecting APS filter or off in LCU
  Encoding scheme
    ALF coef. design is the same as Option 1 and 2
    Previous frames to design ALF coef. in APS, and current frame to design ALF coef. In LCU
    In each LCU, a filter (1) signalled in APS, (2) signalled in this LCU, or (3) signalled previously and stored may be used, or filtering is not performed
  Possible implementation problem
    Same as Option 1
<number>
2012/04/xx
SPS
PPS
APS
Slice header
Slice data
LCU
LCU
LCU
On/off ctrl
Coef. or index
16 filters
Single filter
AHG6 activity

## Slide 16: Test Results for LCU mode
<number>
2012/04/xx
Option |  |  | HE10-AI |  |  | HE10-RA |  |  | HE10-LDB |  |  | HE10-LDP |  |  | Average |  | 
W/o Class F |  |  | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
1 | N/A |  | -1.2 | -0.3 | -0.2 | -2.1 | -0.5 | -0.8 | -1.6 | -0.2 | -0.2 | -3.0 | -0.2 | -0.4 | -2.0 | -0.3 | -0.4
2 | BA | PRE | -1.6 | -3.2 | -3.5 | -2.8 | -3.0 | -2.7 | -1.8 | -3.5 | -3.5 | -3.4 | -5.7 | -5.9 | -2.4 | -3.9 | -3.9
 | BA | CUR | -1.7 | -3.1 | -3.3 | -3.2 | -1.4 | -1.1 | -2.0 | -3.4 | -3.3 | -3.9 | -5.9 | -5.8 | -2.7 | -3.5 | -3.4
 | RA | PRE | -1.4 | -3.2 | -3.4 | -2.5 | -2.8 | -2.6 | -1.7 | -3.4 | -3.6 | -3.2 | -5.4 | -5.7 | -2.2 | -3.7 | -3.8
 | RA | CUR | -1.5 | -3.0 | -3.2 | -2.8 | -1.6 | -1.4 | -2.0 | -3.4 | -3.4 | -3.7 | -5.6 | -5.5 | -2.4 | -3.4 | -3.4
3 | BA | PRE | -1.6 | -3.1 | -3.4 | -2.9 | -2.6 | -2.5 | -1.9 | -3.3 | -3.3 | -3.6 | -5.2 | -5.2 | -2.5 | -3.6 | -3.6
 | RA | PRE | -1.4 | -3.1 | -3.3 | -2.5 | -2.5 | -2.3 | -1.8 | -3.0 | -3.0 | -3.3 | -4.8 | -4.8 | -2.2 | -3.4 | -3.4
Anchor: ALF off, HM-6.0 SAO with LCU opt.
Test: Proposed ALF with PIC (i.e., CUR) or LCU (i.e., PRE) opt.
and CE2 pixel access constraints (for LCU opt.), HM-6.0 SAO with LCU opt.
AHG6 activity

## Slide 17: Study of PIC/LCU mode Unification by Option 2
<number>
2012/04/xx
SPS
PPS
APS
Slice header
Slice data
LCU
LCU
LCU
On/off ctrl
Coef.
16 filters
AHG6 activity
Picture-based encoding (PIC mode) in CD/HM6
LCU-based encoding (LCU mode) in Option 2
As shown above, the difference is only signalling location of ALF on/off flag (embedded in slice header or interleaved in each LCU)
SPS
PPS
APS
Slice header
Slice data

## Slide 18: Comparison of CD/HM6 vs Option 2
<number>
2012/04/xx
Option 2 |  |  | HE10-AI |  |  | HE10-RA |  |  | HE10-LDB |  |  | HE10-LDP |  |  | Average |  | 
W/o Class F |  |  | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
2 | BA | PRE | -1.6 | -3.2 | -3.5 | -2.8 | -3.0 | -2.7 | -1.8 | -3.5 | -3.5 | -3.4 | -5.7 | -5.9 | -2.4 | -3.9 | -3.9
 | BA | CUR | -1.7 | -3.1 | -3.3 | -3.2 | -1.4 | -1.1 | -2.0 | -3.4 | -3.3 | -3.9 | -5.9 | -5.8 | -2.7 | -3.5 | -3.4
 | RA | PRE | -1.4 | -3.2 | -3.4 | -2.5 | -2.8 | -2.6 | -1.7 | -3.4 | -3.6 | -3.2 | -5.4 | -5.7 | -2.2 | -3.7 | -3.8
 | RA | CUR | -1.5 | -3.0 | -3.2 | -2.8 | -1.6 | -1.4 | -2.0 | -3.4 | -3.4 | -3.7 | -5.6 | -5.5 | -2.4 | -3.4 | -3.4
Anchor: ALF off, HM-6.0 SAO with LCU opt.
Test: Proposed ALF with PIC (i.e., CUR) or LCU (i.e., PRE) opt.
and CE2 pixel access constraints (for LCU opt.), HM-6.0 SAO with LCU opt.
CD/HM6 | HE10-AI |  |  | HE10-RA |  |  | HE10-LDB |  |  | HE10-LDP |  |  | Average |  | 
W/o Class F | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
PIC Opt. (CUR) (BA/RA hybrid) | -1.9 | -3.5 | -3.7 | -3.4 | -2.8 | -2.8 | -2.5 | -3.3 | -2.8 | -3.7 | -3.7 | -3.4 | -2.9 | -3.3 | -3.2
LCU Opt.(CUR) | -1.2 | -0.5 | -0.5 | -2.2 | -0.9 | -1.1 | -1.6 | -0.8 | -0.8 | -3.1 | -1.4 | -1.3 | -2.0 | -0.9 | -0.9
Anchor: ALF off, HM-6.0 SAO with the same PIC/LCU opt. setting as ALF
Test: HM-6.0 ALF with PIC/LCU opt. and CE2 pixel access constraints (for LCU opt.),
HM-6.0 SAO with the same PIC/LCU opt. setting as ALF
AHG6 activity
Unification to Option 2 for PIC/LCU mode should be considered.

## Slide 19: CE2 Subtests
Simplification study
  CE2.b: Simplification of ALF signalling
  CE2.e: Depth of LCU division for filtering control
  Recommend to adopt all simplifications
Slice boundary processing study for LCU-based mode
  CE2.f: Line memory reduction fix at independent slice and tile boundaries
   Make recommendation after subjective viewing
Signalling/syntax study
  CE2.a: Signalling mode change from "switch between APS mode and slice header mode" to "switch between APS mode and interleaving mode“
   Recommend CE2.a.1 and CE2.a.2 as baseline Options and further study in AHG6
BA vs RA study, including BA simplification
  CE2.c: Number of classes in BA mode
  CE2.d: Number of regions in RA mode
   Discuss CE2.c to reduce testing for further study in AHG6
Encoder optimization study for LCU-based encoding (non-normative)
  CE2.g: Encoder complexity reduction for LCU-based optimization
Luma/chroma filter coefficients unification study in LCU-based encoding
  CE2.h: Reuse luma filter coefficients in chroma filtering for LCU-based optimization
   Should be integrated IF Option 1 or 3 in AHG6 further study is recommended
Combination study
  CE2.i: Combination subtests
   Not adopted as it is (further study in conceptually in AHG6)
<number>
2012/04/xx

## Slide 20: Results of CE2.c and CE2.d
<number>
2012/04/xx
Anchor = HM-6.0 CE2 anchor |  |  | Picture-based ALF |  |  |  | LCU-based ALF |  |  | 
Test |  | Summary | AI | RA | LDB | LDP | AI | RA | LDB | LDP
 |  |  | Y | Y | Y | Y | Y | Y | Y | Y
CE2.c.1-1_10 | BA filter < 10 | Restrict number of ALF filters in each picture using merge process in HM6. | 0.0% | 0.1% | 0.1% | 0.3% | N/A | N/A | N/A | N/A
CE2.c.1-1_7 | BA filter < 7 |  | 0.0% | 0.1% | 0.1% | 0.3% | N/A | N/A | N/A | N/A
CE2.c.1-1_4 | BA filter < 4 |  | 0.1% | 0.2% | 0.2% | 0.5% | N/A | N/A | N/A | N/A
CE2.c.1-1_1 | BA filter < 1 |  | 0.5% | 0.9% | 0.7% | 1.4% | N/A | N/A | N/A | N/A
CE2.c.1-2_7 | H0417 BA (7) | Restrict number of ALF filters in each picture by modifying BA table. | 0.1% | 0.1% | 0.1% | 0.2% | N/A | N/A | N/A | N/A
CE2.c.1-2_4 | H0417 BA (4) |  | 0.1% | 0.2% | 0.1% | 0.2% | N/A | N/A | N/A | N/A
CE2.c.2 | H0094 | Restrict number of ALF filters to 1, 4 or 6, by switching 3 kinds of BA table. | 0.0% | 0.3% | 0.0% | 0.0% | N/A | N/A | N/A | N/A
CE2.d.1_16 | 16 regions in RA | The depth of quadtree in ALF shall be 2 (16 region RA) or 3 (64 region RA) | 0.3% | 0.6% | 0.4% | 0.7% |  |  |  | 
CE2.d.1_64 | 64 regions in RA |  | 0.3% | 0.5% | 0.3% | 0.4% |  |  |  | 
Further discussion/study in CE2 and/or AHG6
Further study
in AHG6
based on Option 2.
No need to discuss

## Slide 21: CE2 Subtests
Simplification study
  CE2.b: Simplification of ALF signalling
  CE2.e: Depth of LCU division for filtering control
  Recommend to adopt all simplifications
Slice boundary processing study for LCU-based mode
  CE2.f: Line memory reduction fix at independent slice and tile boundaries
   Make recommendation after subjective viewing
Signalling/syntax study
  CE2.a: Signalling mode change from "switch between APS mode and slice header mode" to "switch between APS mode and interleaving mode“
   Recommend CE2.a.1 and CE2.a.2 as baseline Options and further study in AHG6
BA vs RA study, including BA simplification
  CE2.c: Number of classes in BA mode
  CE2.d: Number of regions in RA mode
   Discuss CE2.c to reduce testing for further study in AHG6
Encoder optimization study for LCU-based encoding (non-normative)
  CE2.g: Encoder complexity reduction for LCU-based optimization
Luma/chroma filter coefficients unification study in LCU-based encoding
  CE2.h: Reuse luma filter coefficients in chroma filtering for LCU-based optimization
   Should be integrated IF Option 1 or 3 in AHG6 further study is recommended
Combination study
  CE2.i: Combination subtests
   Not adopted as it is (further study in conceptually in AHG6)
<number>
2012/04/xx

## Slide 22: Results of CE2.g (non-normative)
<number>
2012/04/xx
Need further discussion in CE2 and AHG6
Anchor = HM-6.0 CE2 anchor |  |  | Picture-based ALF |  |  |  | LCU-based ALF |  |  | 
Test |  | Summary | AI | RA | LDB | LDP | AI | RA | LDB | LDP
 |  |  | Y | Y | Y | Y | Y | Y | Y | Y
CE2.g.1 | not use bottom or right 4 pel | Restrict usage of bottom or right N lines during parameter estimation. | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.2% | 0.2% | 0.3%

## Slide 23: CE2 Subtests
Simplification study
  CE2.b: Simplification of ALF signalling
  CE2.e: Depth of LCU division for filtering control
  Recommend to adopt all simplifications
Slice boundary processing study for LCU-based mode
  CE2.f: Line memory reduction fix at independent slice and tile boundaries
   Make recommendation after subjective viewing
Signalling/syntax study
  CE2.a: Signalling mode change from "switch between APS mode and slice header mode" to "switch between APS mode and interleaving mode“
   Recommend CE2.a.1 and CE2.a.2 as baseline Options and further study in AHG6
BA vs RA study, including BA simplification
  CE2.c: Number of classes in BA mode
  CE2.d: Number of regions in RA mode
   Discuss CE2.c to reduce testing for further study in AHG6
Encoder optimization study for LCU-based encoding (non-normative)
  CE2.g: Encoder complexity reduction for LCU-based optimization
Luma/chroma filter coefficients unification study in LCU-based encoding
  CE2.h: Reuse luma filter coefficients in chroma filtering for LCU-based optimization
   Should be integrated IF Option 1 or 3 in AHG6 further study is recommended
Combination study
  CE2.i: Combination subtests
   Not adopted as it is (further study in conceptually in AHG6)
<number>
2012/04/xx

## Slide 24: Results of CE2.h (4/26)
<number>
2012/04/xx
  Reuse luma filter coefficients in chroma filtering for LCU-based optimization
This subtest is related to Options 1 and 3. If Option 1 or 3 is recommeded by AHG6, it is recommended to adopt CE2.h, since chroma provides 0.7% to 3.1% gain which means overall gain (Y/U/V) seems “gain”
Anchor = HM-6.0 CE2 anchor |  |  | Picture-based ALF |  |  |  | LCU-based ALF |  |  | 
Test |  | Summary | AI | RA | LDB | LDP | AI | RA | LDB | LDP
 |  |  | Y | Y | Y | Y | Y | Y | Y | Y
CE2.h.1 | Reuse luma filter on chroma | Allow chroma to use luma ALF filter coefficients. | N/A | N/A | N/A | N/A | 0.1% | 0.1% | 0.2% | 0.2%

## Slide 25: CE2 Subtests
Simplification study
  CE2.b: Simplification of ALF signalling
  CE2.e: Depth of LCU division for filtering control
  Recommend to adopt all simplifications
Slice boundary processing study for LCU-based mode
  CE2.f: Line memory reduction fix at independent slice and tile boundaries
   Make recommendation after subjective viewing
Signalling/syntax study
  CE2.a: Signalling mode change from "switch between APS mode and slice header mode" to "switch between APS mode and interleaving mode“
   Recommend CE2.a.1 and CE2.a.2 as baseline Options and further study in AHG6
BA vs RA study, including BA simplification
  CE2.c: Number of classes in BA mode
  CE2.d: Number of regions in RA mode
   Discuss CE2.c to reduce testing for further study in AHG6
Encoder optimization study for LCU-based encoding (non-normative)
  CE2.g: Encoder complexity reduction for LCU-based optimization
Luma/chroma filter coefficients unification study in LCU-based encoding
  CE2.h: Reuse luma filter coefficients in chroma filtering for LCU-based optimization
   Should be integrated IF Option 1 or 3 in AHG6 further study is recommended
Combination study
  CE2.i: Combination subtests
   Not adopted as it is (further study in conceptually in AHG6)
<number>
2012/04/xx

## Slide 26: Results of CE2.i
<number>
2012/04/xx
CE2.i.1 should not be adopted. However, the concept of CE2.i.1 is under the study in AHG6.
Anchor = HM-6.0 CE2 anchor |  |  | Picture-based ALF |  |  |  | LCU-based ALF |  |  | 
Test |  | Summary | AI | RA | LDB | LDP | AI | RA | LDB | LDP
 |  |  | Y | Y | Y | Y | Y | Y | Y | Y
CE2.i.1 | Combination | JCTVC-H0066 | N/A | N/A | N/A | N/A | 0.8% | 1.0% | 0.4% | 0.8%

## Slide 27: Next Topic (Apr. 19, 20, 25)
Confirm whether Option 2 should be further studied.
After reaching the conclusion for signalling scheme of LCU based ALF, it should be discussed whether we should have two ALF modes (picture-based ALF and LCU-based ALF) or a unified single mode.
  Only 0.2-0.3% gain for Option 2. (A unified mode (i.e., LCU-based ALF) is recommended, if Option 2 is recommended)
RA vs BA discussion
  Number of maximum filters in RA or BA needs to be studied
    May need testing of more than 16 regions for RA (64 regions are tested)
      No gain by RA64 (Confirmed (Cf. JCTVC-I240))
    May need testing of less than 16 filters for BA (Further test on-going)
  Results for higher resolution sequences
Independent ALF control for each component (Done)
  Normative change to allow independent control
    Encoder allows independent control (This option is recommended)
    Encoder controls chroma only when luma is on
How ALF will be defined in an HEVC profile?
  Some suggestion to consider “Option2_RA/BA plus independent ALF on/off control for each component” as the first priority for Main Profile
  However, this discussion should be delegated to AHG8 activity
<number>
2012/04/xx
AHG6 activity

## Slide 28: Next Topic (Apr. 18)
Confirm whether Option 2 should be further studied.
After reaching the conclusion for signalling scheme of LCU based ALF, it should be discussed whether we should have two ALF modes (picture-based ALF and LCU-based ALF) or a unified single mode. (Cf. Slides 16 and 17, Discuss during the meeting?)
RA vs BA discussion
  Number of maximum filters in RA or BA needs to be studied
    May need testing of more than 16 regions for RA (64 regions are tested)
      No gain by RA64 (need cross-check report to confirm this)
    May need testing of less than 16 filters for BA (No need to test)
  Results for higher resolution sequences
Independent ALF control for each component (Done, to be reported)
  Normative change to allow independent control
    Encoder allows independent control (This option is recommended)
    Encoder controls chroma only when luma is on
How ALF will be defined in an HEVC profile?
<number>
2012/04/xx
AHG6 activity

## Slide 29: Results for RA16 vs. RA64 for Option 2 (Apr. 18)
<number>
2012/04/xx
Need to wait for cross-checking, but RA64 seems not to give additional coding gain.
  Even in Class A sequences, no gain is observed.
  RA16 would be used for discussion of RA vs BA.
Anchor = HM-6.0 HE10 ALF off |  |  | Option 2 ALF |  |  | 
Test |  | Summary | AI | RA | LDB | LDP
 |  |  | Y | Y | Y | Y
RA test | RA16 on Option 2 | RA16 | -1.4% | -2.5% | -1.7% | -3.3%
 | RA64 on Option 2 | RA64 | -1.5% | -2.5% | -1.7% | -3.2%
AHG6 activity

## Slide 30: Next Topic (Apr. 18)
Confirm whether Option 2 should be further studied.
After reaching the conclusion for signalling scheme of LCU based ALF, it should be discussed whether we should have two ALF modes (picture-based ALF and LCU-based ALF) or a unified single mode. (Cf. Slides 16 and 17, Discuss during the meeting?)
RA vs BA discussion
  Number of maximum filters in RA or BA needs to be studied
    May need testing of more than 16 regions for RA (64 regions are tested)
      No gain by RA64 (need cross-check report to confirm this)
    May need testing of less than 16 filters for BA (No need to test)
  Results for higher resolution sequences
Independent ALF control for each component (Done, to be reported)
  Normative change to allow independent control
    Encoder allows independent control (This option is recommended)
    Encoder controls chroma only when luma is on
How ALF will be defined in an HEVC profile?
<number>
2012/04/xx
AHG6 activity

## Slide 31: Independent ALF control for each component (Apr. 19)
<number>
2012/04/xx
Anchor = HM-6.0 HE10 ALF off |  |  | Option 2 ALF |  |  | 
Test |  | Summary | AI | RA | LDB | LDP
 |  |  | Y | Y | Y | Y
RA_prev | Option 2 (normative restriction) | Normative restriction | -1.5 | -2.5 | -1.7 | -3.1
 | Independent control | No restriction | -1.4 | -2.4 | -1.6 | -3.1
 | Chroma control restriction by encoder | Non-normative restriction | -1.4 | -2.5 | -1.6 | -3.0
BA_prev | Option 2 (normative restriction) | Normative restriction | -1.7 | -2.9 | -1.8 | -3.4
 | Independent control | No restriction | -1.6 | -2.8 | -1.7 | -3.3
 | Chroma control restriction by encoder | Non-normative restriction | -1.6 | -2.8 | -1.7 | -3.3
AHG6 activity
Need cross-checking
Luma/chroma independent ALF control is recommended.

## Slide 32: Syntax comparison (HM6.0 ALF)
<number>
2012/04/xx
aps_rbsp( ) { | Descriptor
aps_id | ue(v)
aps_scaling_list_data_present_flag | u(1)
if( aps_scaling_list_data_present_flag ) | 
scaling_list_param( ) | 
aps_deblocking_filter_flag | u(1)
if(aps_deblocking_filter_flag) { | 
disable_deblocking_filter_flag | u(1)
if( !disable_deblocking_filter_flag ) { | 
beta_offset_div2 | se(v)
tc_offset_div2 | se(v)
} | 
} | 
aps_sao_interleaving_flag | u(1)
if( !aps_sao_interleaving_flag ) { | 
aps_sample_adaptive_offset_flag | u(1)
if( aps_sample_adaptive_offset_flag ) | 
aps_sao_param( ) | 
} | 
aps_adaptive_loop_filter_flag | u(1)
if( aps_adaptive_loop_filter_flag ) | 
alf_param( ) | 
aps_extension_flag | u(1)
if( aps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
aps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
slice_header( ) { | Descriptor
first_slice_in_pic_flag | u(1)
if( first_slice_in_pic_flag = = 0 ) | 
slice_address | u(v)
slice_type | ue(v)
entropy_slice_flag | u(1)
if( !entropy_slice_flag ) { | 
…… | 
if( adaptive_loop_filter_enabled_flag ) { | 
slice_adaptive_loop_filter_flag | u(1)
if( slice_adaptive_loop_filter_flag && alf_coef_in_slice_flag ) | 
alf_param( ) | 
if( slice_adaptive_loop_filter_flag && !alf_coef_in_slice_flag ) | 
alf_cu_control_param( ) | 
} | 
if( seq_loop_filter_across_slices_enabled_flag && ( slice_adaptive_loop_filter_flag ¦ ¦ slice_sample_adaptive_offset_flag ¦ ¦ !disable_deblocking_filter_flag ) ) | 
slice_loop_filter_across_slices_enabled_flag | u(1)
if( tiles_or_entropy_coding_sync_idc > 0 ) { | 
num_entry_point_offsets | ue(v)
if( num_entry_point_offsets > 0 ) { | 
offset_len_minus1 | ue(v)
for( i = 0; i < num_entry_point_offsets; i++ ) | 
entry_point_offset[ i ] | u(v)
} | 
} | 
} | 
alf_param() { | Descriptor
alf_cb_enable_flag | u(1)
alf_cr_enable_flag | u(1)
alf_one_luma_unit_per_slice_flag | 
if( alf_cb_enable_flag ) | 
alf_one_cb_unit_per_slice_flag | u(1)
if( alf_cr_enable_flag ) | 
alf_one_cr_unit_per_slice_flag | 
if( !alf_coef_in_slice_flag ) { | 
alf_num_lcu_in_width_minus1 | ue(v)
alf_num_lcu_in_height_minus1 | ue(v)
} else | 
alf_num_lcu_in_slice_minus1 | u(v)
endCtbrY = (numCtb − 1 + firstCtbAddr) / numCtbInWidth | 
endCtbrX = (numCtb − 1 + firstCtbAddr) % numCtbInWidth | 
for( i = 0; i < numCtb; i++ ) { | 
rx = ( i + firstCtbAddr) % numCtbInWidth | 
ry = ( i + firstCtbAddr) / numCtbInWidth | 
endrX = ( ry = = endCtbrY ) ? ( endCtbrX ) : ( numCtbInWidth − 1 ) | 
if( ( rx = = 0 ) && ( i − numCtbInWidth >= 0 ) && ( alf_one_luma_unit_per_slice_flag = =0 ) ) | 
alf_repeat_row _flag[0] | u(1)
alf_unit( rx, ry, 0, i, endrX, alf_one_luma_unit_per_slice_flag ) | 
if( alf_cb_enable_flag ) { | 
if( ( rx = = 0 ) && ( i − numCtbInWidth >= 0 ) && ( alf_one_cb_unit_per_slice_flag = =0 ) ) | 
alf_repeat_row _flag[1] | u(1)
alf_unit(rx, ry, 1, i, endrX, alf_one_cb_unit_per_slice_flag ) | 
} | 
if( alf_cr_enable_flag ) { | 
if( ( rx = = 0) && ( i − numCtbInWidth>= 0) && ( alf_one_cr_unit_per_slice_flag = =0 ) ) | 
alf_repeat_row _flag[2] | u(1)
alf_unit(rx, ry, 2, i, endrX, alf_one_cr_unit_per_slice_flag ) | 
} | 
} | 
} | 
alf_unit(rx, ry, cIdx, lcuIdx, endrX, oneUnitFlag ) { | Descriptor
if( oneUnitFlag ) { | 
if( lcuIdx = = 0 ) { | 
alf_lcu_enable_flag[ cIdx ][ ry ][ rx ] | u(1)
if( alf_lcu_enable_flag[ cIdx ][ ry ][ rx ] ) | 
alf_info( rx, ry, cIdx ) | 
} | 
} else { | 
if( !alf_repeat_row _flag[ cIdx ] ) { | 
if( rx = = 0 ¦¦ alfRun[ cIdx ][ ry ][ rx ] < 0 ) | 
if( lcuIdx –numCtbInWidth < 0 ) | 
alfRun[ cIdx ][ ry ][ rx ] = 0 + alf_run_diff | u(v)
else | 
alfRun[ cIdx ][ ry ][ rx ] = alfRun[ cIdx ][ ry − 1 ][ rx ]+ alf_run_diff | s(v)
alfRun[ cIdx ][ ry ][ rx+ 1 ] = alfRun[ cIdx ][ ry ][ rx ] − 1 | 
if( rx == 0 ¦¦ alfRun [ cIdx ] [ rx ][ ry ] < 0) { | 
if( ry > 0 && ( lcuIdx − numCtbInWidth > = 0 ¦ ¦ alfAcrossSlice) ) | 
alf_merge_up_flag | u(1)
if( !alf_merge_up_flag ) { | 
alf_lcu_enable_flag[ cIdx ][ ry ][ rx ] | u(1)
if( alf_lcu_enable_flag[ cIdx ][ ry ][ rx ] ) | 
alf_info( rx, ry, cIdx ) | 
} | 
} | 
} else | 
alfRun[ cIdx ][ ry ][ rx ] = alfRun[ cIdx ][ ry − 1 ][ rx ] | 
} | 
} | 
alf_info( rx, ry, cIdx ) { | Descriptor
if(NumALFFiltersInStoredBuffer[cIdx] > 0) | 
alf_new_filter_set_flag | u(1)
if( alf_new_filter_set_flag = = 0 && NumALFFiltersInStoredBuffer[cIdx] > 0) | 
alf_stored_filter_set_idx[ cIdx ] | u(v)
else { | 
if( cIdx = = 0 ) { | 
alf_no_filters_minus1 | ue(v)
if( alf_no_filters_minus1 = = 1 ) | 
alf_start_second_filter | ue(v)
else if( alf_no_filters_minus1 > 1 ) | 
for( i = 1; i < 15; i++ ) | 
alf_filter_pattern_flag[ cIdx ][ ry ][ rx ][ i ] | u(1)
if( alf_no_filters_minus1 > 0 ) | 
alf_pred_flag[ cIdx ][ ry ][ rx ] | u(1)
for( i = 0; i < AlfNumFilters; i++ ) | 
alf_nb_pred_luma_flag[ cIdx ][ ry ][ rx ][ i ] | u(1)
if( AlfNumFilters > 1 ) { | 
alf_min_kstart_minus1 | ue(v)
for( i = 1; i < 4; i++ ) | 
alf_golomb_index_flag[ i ] | u(1)
} | 
for( i = 0; i < AlfNumFilters; i++ ) | 
for( j = 0; j < AlfCodedLength; j++ ) | 
alf_filt_coeff[ cIdx ][ ry ][ rx ][ i ][ j ] | ge(v)
} else | 
for( j = 0; j < AlfCodedLength; j++ ) | 
alf_filt_coeff[ cIdx ][ ry ][ rx ][ 0 ][ j ] | se(v)
} | 
} | 
alf_cu_control_param() { | Descriptor
alf_cu_control_flag | u(1)
if( alf_cu_control_flag ) { | 
alf_cu_control_max_depth | ue(v)
alf_length_cu_control_info | se(v)
for( i = 0; i < NumAlfCuFlag; i++ ) | 
alf_cu_flag[ i ] | u(1)
} | 
} | 
AHG6 activity

## Slide 33: Syntax comparison (Option2 (luma/chorma independent ALF on/off))
<number>
2012/04/xx
aps_rbsp( ) { | Descriptor
aps_id | ue(v)
aps_scaling_list_data_present_flag | u(1)
if( aps_scaling_list_data_present_flag ) | 
scaling_list_param( ) | 
aps_deblocking_filter_flag | u(1)
if(aps_deblocking_filter_flag) { | 
disable_deblocking_filter_flag | u(1)
if( !disable_deblocking_filter_flag ) { | 
beta_offset_div2 | se(v)
tc_offset_div2 | se(v)
} | 
} | 
aps_sao_interleaving_flag | u(1)
if( !aps_sao_interleaving_flag ) { | 
aps_sample_adaptive_offset_flag | u(1)
if( aps_sample_adaptive_offset_flag ) | 
aps_sao_param( ) | 
} | 
for(cIdx=0;cIdx<3;cIdx++) { | 
alf_aps_filter_flag[cIdx] | u(1)
if( alf_aps_filter_flag[cIdx] ) | 
alf_picture_info(cIdx) | 
} | 
aps_extension_flag | u(1)
if( aps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
aps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
alf_picture_info(cIdx) { | Descriptor
if( cIdx = = 0 ) { | 
alf_no_filters_minus1 | ue(v)
if( alf_no_filters_minus1 = = 1 ) | 
alf_start_second_filter | ue(v)
else if( alf_no_filters_minus1 > 1 ) | 
for( i = 1; i <16; i++ ) | 
alf_filter_pattern_flag[ cIdx ] [ i ] | u(1)
for( i = 0; i < AlfNumFilters; i++ ) | 
for( j = 0; j < AlfCodedLength; j++ ) | 
alf_filt_coeff[ cIdx ] [ i ][ j ] | ge(v)
} else | 
for( j = 0; j < AlfCodedLength; j++ ) | 
alf_filt_coeff[ cIdx ] [ 0 ][ j ] | se(v)
} | 
slice_data( ) { | Descriptor
CtbAddrRS = SliceCtbAddrRS | 
CtbAddrTS = CtbAddrRStoTS[ CtbAddrRS ] | 
moreDataFlag = 1 | 
do { | 
…. | 
for(cIdx=0;cIdx<3; cIdx++) | 
if(alf_slice_filter_flag[cIdx]) | 
alf_lcu_enable_flag[ cIdx ][ ry ][ rx ] | ae(v)
moreDataFlag = coding_tree( xCtb, yCtb, Log2CtbSize, 0 ) | 
CtbAddrTS++ | 
… | 
} while( moreDataFlag ) | 
} | 
AHG6 activity

## Slide 34: Source Codes (Apr. 20, 24 and 26 update)
Software | Decoder (TComAdaptiveLoopFilter.cpp) | Encoder (TEncAdaptiveLoopFilter.cpp)
HM5.0 ALF | 3084 | 4287
HM6.0 ALF | 2219 | 4468
Option2 ALF: Pre + RA | 2182  1159 (755) | 3013  2447
Option2 ALF: Pre + BA | 2236  1159 (755) | 3014  2447
<number>
2012/04/xx
Comparison of the number of activated source code lines in HM5.0 ALF, HM6.0 ALF and Option2 ALF
AHG6 activity
Source code for Option2 has been highly cleaned up for HM7 integration.
Numbers in parenthesis are omitting the support of slice/tile/I-PCM process.

## Slide 35: Recommendation (Apr. 19, 20, 25)
Study Options 1 to 3
  Option 1 syntax supported by several companies
    Some voices that Option 1 seems the best trade-off between complexity and coding efficiency
    Some concern about the coefficient buffer
  Option 2 syntax supported by several companies
    Some concern about error resilience and overhead to signal ALF coefs. in APS
    Some voices that Option 2 seems the best trade-off between complexity and coding efficiency
Simplification
  Adopt all simplification tested in CE2.b and CE2.e
  Region Adaptive ALF (RA16) as the first priority, but Block Adaptive ALF (BA16) is also another candidate (not concluded, Cf. JCTVC-I0363)
    Reduction of 16 filters for BA should be also discussed (Cf. JCTVC-I0215)
  Unify two signalling modes into one mode (i.e., Option 2 LCU mode)
  Independent ALF control for luma and each chroma component
  Source code and draft text cleanup (Cf. JCTVC-I157)
(Profile discussion should be done in AHG8 or in JCT-VC)
<number>
2012/04/xx
AHG6 activity