## Slide 1
1. Summary
2. Proposed Method
3. Experimental Results
4. Conclusion
Contents
Parallel AMVP candidate list construction (JCTVC-I0036)
2012-04-29
China TV Lab. / Media Part
Qin Yu, Siwei Ma (Peking University)
Hongbin Liu, Jie Jia (LG Electronics)

## Slide 2: Summary
Proposed method
  Solution 1 : CU based
    Replace inner candidates with the outside ones of the CU
  Solution 2 : CU based
    All PUs in the CU share the same set of motion information with inter 2Nx2N PU
  Solution 3 : region based
    Disable candidates that are within the region
Experiment results
  Solution 1: 0.2%, 0.2 %, 0.2 % BD-rate increase for Y, U, V
  Solution 2: 0.1% , 0.1% , 0.0% BD-rate increase for Y, U, V
  Solution 3: 0.0%, 0.1%, -0.1% BD-rate increase for Y, U, V
Crosscheck
  JCTVC-I0321 (by Intel)
  JCTVC-I0410 (by Microsoft)
JCTVC-I0036
<number>/9

## Slide 3: Proposed Method
Solution 1: CU based parallel AMVP
  Replace the inner PUs with the ones outside the current CU
JCTVC-I0036
  An additional position derivation operation for Size_2NxN, Size_Nx2N, Size_nLx2N, Size_nRx2N, Size_2NxnU and Size_2NxnD partition
  Five additional position derivation operations for NxN partition
  0.2%, 0.2%, 0.2% BD-rate increase on Y, U and V
<number>/9

## Slide 4: Proposed Method
Solution 2: motion information used by 2Nx2N inter PU is used by all PUs in a CU (only applied to 8x8 CU)
JCTVC-I0036
<number>/9

## Slide 5: Proposed Method
Solution 3: region based parallel AMVP
  All PUs in the region construct the AMVP candidate list in parallel, and candidates within the region is disabled
  Proposed method is employed when log2_parallel_merge_level_minus2 is 1.
JCTVC-I0036
<number>/9

## Slide 6: Experiment Result
Solution 2
At decoder: AMVP candidate list only need to be constructed once for PUs (in a CU) sharing the same reference picture.
At encoder: reduce the number of AMVP candidate lists for 8x8 CU by 80%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.2% | 0.2% | 0.1% | 0.3% | 0.2%
Class B | 0.1% | 0.1% | 0.1% | 0.0% | 0.1% | 0.0%
Class C | 0.1% | 0.2% | 0.2% | 0.1% | 0.1% | 0.0%
Class D | 0.1% | 0.1% | 0.3% | 0.2% | 0.1% | 0.0%
Class E |  |  |  |  |  | 
Overall | 0.1% | 0.2% | 0.2% | 0.1% | 0.1% | 0.0%
 | 0.1% | 0.2% | 0.2% | 0.1% | 0.1% | 0.0%
Class F | 0.2% | 0.2% | 0.3% | 0.2% | 0.1% | 0.3%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | 104% |  |  | 99% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.2% | -0.3% | 0.0% | -0.1% | 0.3%
Class C | 0.1% | 0.2% | 0.1% | 0.1% | 0.1% | 0.2%
Class D | 0.1% | 0.1% | 0.3% | 0.1% | 0.1% | -0.5%
Class E | 0.0% | 0.1% | 0.3% | 0.0% | -0.1% | 0.2%
Overall | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
 | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0%
Class F | 0.3% | 0.3% | 0.3% | 0.3% | 0.7% | 0.5%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | 86% |  |  | 88% |  | 
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.2% | 0.2%
Class C | 0.1% | -0.4% | 0.0% | 0.1% | 0.0% | -0.2%
Class D | 0.1% | -0.2% | -0.9% | 0.0% | 0.6% | -0.1%
Class E | 0.1% | 0.2% | -0.1% | 0.1% | 0.7% | 0.3%
Overall | 0.1% | -0.1% | -0.3% | 0.0% | 0.3% | 0.0%
 | 0.1% | -0.1% | -0.2% | 0.0% | 0.3% | 0.1%
Class F | 0.4% | 0.5% | 0.4% | 0.3% | 1.5% | 1.2%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | 89% |  |  | 88% |  | 
JCTVC-I0036
<number>/9

## Slide 7: Experiment Result
Solution 3
When deriving the spatial MVP candidate, an additional check to determine whether the current PU and its neighboring PU belong to the same region is required
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.2% | 0.1% | 0.0% | 0.1% | 0.1%
Class B | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | 0.0%
Class C | 0.1% | 0.2% | 0.1% | 0.1% | 0.1% | 0.2%
Class D | 0.1% | 0.2% | 0.1% | 0.2% | 0.1% | 0.0%
Class E |  |  |  |  |  | 
Overall | 0.1% | 0.2% | 0.1% | 0.1% | 0.1% | 0.1%
 | 0.1% | 0.2% | 0.1% | 0.1% | 0.1% | 0.1%
Class F | 0.2% | 0.3% | 0.3% | 0.2% | 0.3% | 0.3%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | 103% |  |  | 95% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.2% | -0.3% | 0.0% | -0.1% | 0.0%
Class C | 0.0% | 0.3% | 0.2% | 0.1% | 0.0% | 0.0%
Class D | 0.1% | 0.2% | 0.4% | 0.0% | 0.0% | -0.3%
Class E | 0.1% | 0.0% | 0.3% | -0.1% | -0.3% | -0.1%
Overall | 0.0% | 0.1% | 0.1% | 0.0% | -0.1% | -0.1%
 | 0.0% | 0.1% | 0.1% | 0.0% | -0.1% | -0.1%
Class F | 0.4% | 0.2% | 1.0% | 0.5% | 0.9% | 0.8%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | 88% |  |  | 87% |  | 
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.1% | 0.0% | 0.2% | -0.3%
Class C | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
Class D | 0.0% | -0.4% | -0.3% | 0.0% | 0.3% | -0.8%
Class E | -0.1% | -0.2% | -0.2% | 0.0% | 0.7% | -0.4%
Overall | 0.0% | -0.1% | -0.1% | 0.0% | 0.3% | -0.4%
 | 0.0% | -0.1% | -0.1% | 0.0% | 0.3% | -0.2%
Class F | 0.4% | 0.7% | 0.2% | 0.3% | 1.1% | 0.7%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | 88% |  |  | 87% |  | 
JCTVC-I0036
<number>/9

## Slide 8: Conclusion
Three solutions for parallel construction of AMVP candidate at different parallel levels are proposed
  Solution 1 : CU based
    Replace inner candidates with the outside ones of the CU
  Solution 2 : CU based (applied to 8x8 CU)
    All PUs in the CU share the same set of motion information with inter 2Nx2N PU
  Solution 3 : region based (region size 8x8)
    Disable candidates that are within the region
Experiment result
  Solution 1: 0.2%, 0.2 %, 0.2 % BD-rate increase for Y, U, V
  Solution 2: 0.1% , 0.1% , 0.0% BD-rate increase for Y, U, V
  Solution 3: 0.0%, 0.1%, -0.1% BD-rate increase for Y, U, V
It is recommended to adopt solution 2 or solution 3 into the HEVC draft
JCTVC-I0036
<number>/9