## Slide 1: Modification of recovery point SEI message (JCTVC-I0044)
K.Kazui, J.Koyama, S.Shimada and A.Nakagawa
FUJITSU LABORATORIES LTD.
9th JCT-VC Meeting

## Slide 2: Outline
The spec of recovery point SEI (RPSEI) should be updated.
  frame_num is no more used in HEVC.
Proposed modifications
  POC value is used to specify a recovery point instead of frame_num.
  Other minor issues
Draft text is ready

## Slide 3: Problem
RPSEI in HM6.0
  Inherited from AVC
  Recovery point is still specified by recovery_frame_cnt.
    The first picture in the decoding order with frame_num x is defined as a recovery point if x = (y + recovery_frame_cnt) % MaxFrameNum, where y is frame_num of a random access picture with RPSEI.
frame_num is removed from HM
  New “reference picture set” concept
New RPSEI spec is needed

## Slide 4: Proposal [1/2]
Recovery point is specified by POC value
  recovery_poc_cnt
    The first picture in the decoding order with pic_order_cnt_lsb x is defined as a recovery point if x = (y + recovery_poc_cnt) % MaxPicOrderCntLSB, where y is pic_order_cnt_lsb of a random access picture with RPSEI.
  Non-referenced picture can be a recovery point.
    Recovery point can be set earlier in some specific cases.

## Slide 5: Proposal [2/2]
Other minor issues
  prevPicOrderCntLsb and prevPicOrderCntMsb
    Those shall be reset to zero when decoding process starts from a random access picture with RPSEI.
    Ambiguity is removed.
  Additional text relating to APS and CRA