## Slide 1: Bitstream restriction flag to enable tile split
JCTVC-I0056
O. Nakagami and T. Suzuki
Sony Corporation
Joint Collaborative Team on Video Coding (JCT-VC) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11
9th Meeting: Geneva, CH, 27 April – 7 May 2012

## Slide 2: Introduction
In the current draft, tile can be split when some bitstream restrictions are satisfied.
By sending a 1-bit flag to indicate the restrictions for the bitstream or for each tile, decoder can decode only the required tile. It is asserted such flag enhances usability of tile coding in some application field. Eg. Frame packing 3D stereo coding, TV-conference systems etc.
TileID
1
TileID
2
TileID
3
TileID
4
stream
1
stream
2
stream
3
stream
4
split
stream A
decodable
rewrite
header

## Slide 3: Bitstream restrictions
Tile structure is kept through the sequence
For a slice in each tile, the slice size is equal to the tile size.
temporal_mv is not used in the different tile
TileID
1
TileID
2
TileID
3
TileID
4
TileID
1
TileID
2
TileID
3
TileID
4
ＰＯＣ
t-1
t

## Slide 4: Bitstream restriction for motion vector length
For all CU in a tile, no sample outside the current tile boundaries and no sample at a fractional sample position for which the sample value is derived using one or more samples outside the current tile boundaries is used for inter prediction of any sample.
NOTE - similar to the definition of motion_vectors_over_pic_boundaries_flag
TileID
i
CU
TileID
i-1
NG
OK
motion vector restriction

## Slide 5: Bitstream restrictions for loop filter parameters
loop_filters are disabled between tiles.
  loop_filter_across_tiles_enabled_flag==0
For SAO/ALF, no parameter copy between tiles.
  sao_offset_vlc(), alf_unit() should be used at the tile boundary.
TileID
i
TileID
i-1
NG

## Slide 6: Proposed syntax modification Method1 Send 1-bit flag to represent all tile
TileID
1
TileID
2
TileID
3
TileID
4
stream
1
stream
2
stream
3
stream
4
split
stream A

## Slide 7: Proposed syntax modification Method2 Send flags to represent each tile
TileID
1
TileID
2
TileID
3
TileID
4
stream
1
split
stream A
TileID
1
TileID
2
TileID
3

## Slide 8: Use case for Frame packing stereo 3D
Left
TileID
1
Right
TileID
2
Left
TileID
1
Right
TileID
2
3D playback
2D playback
Firstly, each view is encoded with the splittable tiles.
When only base view is necessary, decoders have a choice not to decode unnecessary view. Thus, low-power decode is achieved.

## Slide 9: Conclusion
Propose to add 1-bit bitstream restriction flag in VUI, for the bitstream(Method1) or for each tile(Method2).
It is asserted that the flag enhances the usability of tile coding for a kind of spatial scalability.