## Slide 1: Frame packing arrangement SEI extension for HEVC
JCTVC-I0057
O. Nakagami and T. Suzuki
Sony Corporation
Joint Collaborative Team on Video Coding (JCT-VC) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11
9th Meeting: Geneva, CH, 27 April – 7 May 2012

## Slide 2: Introduction
Frame packing arrangement SEI (FPA_SEI) is used for spatially/temporally packing stereo 3D coding.
In the current draft, FPA_SEI is defined as the same as SEI defined in AVC
This contribution proposes to modify FPA_SEI to support HEVC coding tools in order to enhance usability for the stereo 3D coding.
Left
Right
Stereo
Left
Right
Pack
Unpack
FPA_SEI
2D
(1view)
3D
(2 views)
3D
(2 views)
stereo 3D coding
based on the current draft

## Slide 3: HEVC coding tools for stereo 3D
Temporal_id and tile are beneficial coding tools for frame packing stereo 3D.
Two syntax extensions to FPA_SEI are proposed.
1. Frame sequential coding using temporal_id.
2. Frame packing coding using Tile.
Left
tile_ID 1
Right
tile_ID 2
side-by-side coding using tile
Left
POC0
Right
POC1
Left
POC2
Right
POC5
Right
POC3
Left
POC4
temporal_id
POC
temporal_id_left
frame sequential coding using temporal_id
temporal_id_right

## Slide 4: Frame sequential coding using temporal_id
Motivation
  Decoders can identify that a decoded frame is base view or not by temporal_id in NAL.
  Decoders can decode base view only by dropping AU which temporal_id is more than frame0_max_temporal_id_minus1.
Proposed extension
  maximum temporal id for each view
    frame0_max_temporal_id_minus1
      Base view
    frame1_max_temporal_id_minus1
      Both (base+additional) view
Left
POC0
Right
POC1
Left
POC2
Right
POC5
Right
POC3
Left
POC4
temporal_id
POC
frame0_max_temporal_id_minus1
frame1_max_temporal_id_minus1
frame sequential coding using temporal_id

## Slide 5: Frame packing coding using Tile
Motivation
  In AVC, view information is send as (x, y) position. In proposal, 1-bit for each tile and no pixel position.
  Combining with JCTVC-I0056, which propose a bitstream restriction flag to enable tile split, decoders can decode base-view only if necessary.
Proposed extension
  Add the following syntax to link tile and view
tile_coding_flag u(1)
if( tile_coding_flag )
for( j = 0, tileId = 0; j <= num_tile_columns_minus1; j++ )
for( i = 0; i <= num_tile_rows_minus1; i++, tileId++ )
frame_id // base-view or not for each tile u(1)
Left
tile_ID 1
Right
tile_ID 2
side-by-side coding using tile
Left
tile_ID 1
Right
tile_ID 2
top-bottom coding using tile

## Slide 6: Minimum expression for the FPA_SEI
The proposed SEI extensions make a link between view information and coding structure. It enables to minimize SEI message in the bitstream.
Access Unit for Left view
NAL Unit for FPA_SEI
Conventional
Proposed
time
・・・
・・・
Access Unit for Right view

## Slide 7: Conclusion
It is proposed to modify the frame packing arrangement SEI for HEVC to support tile and temporal_id.
It is asserted that the proposed extension enhances the usability of the frame packing stereo 3D coding by HEVC version1.