## Slide 1: On HEVC profiles JCTVC-I0063
J. Lainema, K. Ugur, M. Hannuksela, J. Ridge

## Slide 2: Summary
Three main aspects in our contribution:
Keep the number of profiles small.
  No need for separate Baseline, Main, High profiles
  No need for flexible profile definitions
Suggestions for Main Profile:
  Only include ALF if significantly simplified over current design
  Consider AMP but not NSQT
  For parallelism, have a single tool/functionality
Have a profile for still picture coding

## Slide 3: Number of Profiles HEVC Application Areas
1. Usage in open environment where devices share content with others (e.g. internet video)
A widely deployed multi-purpose profile is very important as content creators need to be confident all receivers are capable for playback.
Having a large number of profiles risks fragmentation, confuses content creators.
Multiple profiles mean that in practice content has to be created using the smallest subset of the coding tools.
2. Usage in systems with capability negotiation possibilities (e.g. video conferencing)
3. Usage in closed environment (e.g. traditional video broadcasting)
Less number of profiles in coding standard level would not have negative effects.
Make sure certain hooks are present in the specification so that system standards could allow certain subset of the tools to be enabled or negotiated.

## Slide 4: Number of Profiles HEVC in Internet Video
Less number of profiles is especially critical in Internet environment.
Minimization of the number of profiles has been strongly encouraged e.g. by Google in their recent webcast [1]:
  http://www.streamingmedia.com/Articles/Editorial/Featured-Articles/WebM-Taking-Another-Look-81428.aspx, Discussion between 07:00 – 08:20 minutes and 9:30 – 10:40 minutes, March 17, 2012.

## Slide 5: Suggestions for Main Profile
Significantly simplify ALF over the current CD design:
Do we need separate signaling mechanisms at LCU/APS levels?
Do we need to support picture level optimizations?
Consider AMP but not NSQT in Main Profile:
Our studies on developing optimized software decoder indicate that NSQT complicates the otherwise clean transform design. Inline with all previous optimized decoder implementations: H0693, G0757, G0988
For parallelism tools: Have one tool / functionality.

## Slide 6: Still Picture Profile
Motivations
Still picture resolutions are increasing vastly, especially on mobile devices:
  The Nokia PureView Pro imaging technology includes super high resolution sensor with an active area of 41Mpix.
  More info: http://europe.nokia.com/find-products/devices/nokia-808-pureview
HEVC could be very well suited for coding still pictures:
  Impressive coding performance (~56% gain over JPEG and ~34% gain over JPEG-XR)
  More details at JCTVC-I0461 (also subjective viewing could be arranged offline)
  Using tiles/slices, HEVC allows fast decoding of specific parts large images without the need to decode the whole image.
There are alternative ways to code a still picture better than JPEG but much worse than HEVC (e.g. WebP, JPEG-XR)

## Slide 7: Still Picture Profile
Identical to Main Profile with following restrictions:
Sequence contains one picture which consists of I slices only
Every tile contains one and only one slice and every slice contain one and only one tile.
  To make ”random access within picture” feature easy.