## Slide 1: JCTVC-I0070 Nested hierarchy of tiles and slices through slice header prediction
Miska M. Hannuksela and Antti Hallapuro Nokia Research Center

## Slide 2: Summary of Proposals
A picture delimiter NAL unit may carry a slice header, which may be used for decoding of more than one slice of the picture.
A slice header beyond the slice address need not be provided for any slice.
A slice header may be selectably predicted from the previous slice in scan order or from a slice header carried within the picture delimiter NAL unit.
A tile shall contain an integer number of slices. A slice cannot contain data from more than one tile.
JCTVC-I0070
<number>

## Slide 3: Proposal 1
Proposal 1: A picture delimiter NAL unit may carry a slice header, which may be used for decoding of more than one slice of the picture.
Motivation:
Most encoders keep the slice header unchanged during the encoding of a coded picture. Hence, for many coded pictures there are many redundant copies of the slice header.
In our experience, HEVC is vulnerable to transmission errors and any type of error concealment is likely to result into an increase in both the magnitude and the spatial area of the error over time.
  A good strategy to cope with transmission errors is to make use of temporal scalability.
Characteristic data for the coded picture, such as the used picture parameter set and referenced picture set, is given upfront in the access unit before SEI and other NAL units, which may be used in some environments for purposes such as fast-forward play.
JCTVC-I0070
<number>

## Slide 4: Proposal 2
Proposal 2: A slice header beyond the slice address need not be provided for any slice.
Motivation:
The overhead for coding regular slices is reduced as they can refer to the slice header carried in the access unit delimiter.
 | Low delay B Main |  | 
 | Y | U | V
Class A |  |  | 
Class B | -1,3% | -1,5% | -1,7%
Class C | -0,7% | -0,6% | -0,7%
Class D | 0,2% | 0,2% | 0,2%
Class E | -5,1% | -4,8% | -4,5%
Overall | -1,5% | -1,5% | -1,5%
 | -1,5% | -1,5% | -1,5%
Class F | -2,0% | -2,1% | -1,9%
Enc Time[%] | 82 % |  | 
Dec Time[%] | 99 % |  | 
Example results with slice size of about 36 LCUs of size 64x64
JCTVC-I0070
<number>
Notes: <number>

## Slide 5: Proposal 3
Proposal 3: A slice header may be selectably predicted from the previous slice in scan order or from a slice header carried within the picture delimiter NAL unit
Motivation:
The selectable encoding enables tiles and slices to predict a slice header either from the access unit delimiter or from the previous slice having a slice header, both of which are valid options for encoding.
The option for predicting from the previous slice having a slice header can be used particularly for an entropy slice.
JCTVC-I0070
<number>

## Slide 6: Proposal 4
Proposal 4: A tile shall contain an integer number of slices. A slice cannot contain data from more than one tile.
Motivation:
In our opinion, the picture partitioning becomes conceptually simpler with the proposal, as a tile is clearly a superset of a slice.
RD penalty is moderate unless tile size is very small
 | Low delay B Main |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0,8% | 0,6% | 0,4%
Class C | 0,7% | 0,8% | 0,5%
Class D | 0,2% | 0,2% | 0,2%
Class E | 0,8% | 0,0% | 0,7%
Overall | 0,6% | 0,4% | 0,4%
 | 0,6% | 0,5% | 0,5%
Class F | 0,6% | 0,7% | 0,5%
Enc Time[%] | 83 % |  | 
Dec Time[%] | 112 % |  | 
Example results with tile/slice size of about 6x6 LCUs of size 64x64
JCTVC-I0070
<number>
Notes: <number>

## Slide 7: Potential Additional Benefits
Packetization flexibility
  MTU size might not be known at the time of encoding, hence encoded slice size might not be optimal, but due to parallel processing the picture can contain many tiles
  Packetizer can determine how many tiles are encapsulated in one packet
Re-packetization for MTU size matching
  Media gateway may re-encapsulate a suitable number of tiles into one packet
  Slice header can be included in each such packet for loss robustness
Tile as a random access point for an intra-coded picture
  Still picture resolutions are increasing vastly, e.g.:
    Nokia PureView Pro technology includes super high resolution sensor with an active area of 41Mpix
  In many applications / use cases, only a part of a large image has to be displayed
  Random access within an intra-coded picture:
    Decode slice header from picture delimiter NAL unit
    Decode desired tiles/slices (using the slice header in the AU delimiter)
  HEVC CD would require
    sequential decoding of slice headers (fully),
    accessing to all tiles within a slice (to read tile_idx), and
    non-sequential access of the bitstream (the next slice and tile entry point have to be accessed to determine which slice and tile to be decoded)
JCTVC-I0070
<number>

## Slide 8: Summary of Proposals
A picture delimiter NAL unit may carry a slice header, which may be used for decoding of more than one slice of the picture.
A slice header beyond the slice address need not be provided for any slice.
A slice header may be selectably predicted from the previous slice in scan order or from a slice header carried within the picture delimiter NAL unit.
A tile shall contain an integer number of slices. A slice cannot contain data from more than one tile.
Specification text and source code have been provided
JCTVC-I0070
<number>