## Slide 1
Marco Arena
JCT-VC Geneva, 27 April – 8 May 2012
Request to define a technical solution to maintain interoperability and backward compatibility of frame compatible 3DTV transmission with 2D and 3D aware receivers
Notes: <number>

## Slide 2
Broadcasters and HEVC
The possibility for a second digital dividend (UHF/700 MHz band) as considered at WRC’2012 after 2015 could force a rapid migration of terrestrial HDTV services to new more efficient technical standards, such as DVB-T2 and HEVC coding.
  About 6-8 HDTV programmes could be allocated per DVB-T2 multiplex
The system shall be capable of Frame Compatible 3DTV formats (FC-3DTV)
FC-3DTV signal shall be 2D service compatible.
Notes: <number>

## Slide 3
2D-service compatible mode
A “2D service compatible” 3D system is defined as a 3D transmission mode which may be decoded by 2D receivers to deliver 2D video to 2D displays.
A 2D-service compatible mode of operation for frame compatible formats has already been defined in “ETSI TS 101 547 v1.1.1: Digital Video Broadcasting (DVB): Frame Compatible Plano-Stereoscopic 3DTV” leveraging on frame cropping rectangle and SAR.
The cropping rectangle can be used to delimit an area within the frame containing one of the two 2D views.
The output video, properly scaled, provides a 2D-compatible format.
Notes: <number>

## Slide 4
HD-Book DTT 2.1
Notes: Annex M of HD-Book DTT 2.1 already provides implementation guidelines on 2D service compatibility within 3DTV, endorsing “ETSI TS 101 547 v1.1.1: Digital Video Broadcasting (DVB): Frame Compatible Plano-Stereoscopic 3DTV” , based on using the cropping rectangle and sample aspect ratio of the AVC specification.
<number>

## Slide 5
Frame packing stereo 3D is beneficial until future extension to HEVC is standardized.
Definite interest in having the possibility to use frame compatible formats in HEVC together with the cropping rectangle so as to obtain 2D compatibility in the distribution of stereoscopic streams but …
HEVC
… it is missing a way to indicate to a 3D decoder willing to extract the 3D content that video content outside the cropping rectangle is still “legal”.
Notes: <number>

## Slide 6
Adding a second cropping rectangle to enclose the whole stereoscopic format
Defining suitable frame_packing_arrangement_type SEI messages
Other possible solutions
Possible solutions

## Slide 7
Thanks for your attention!!