## Slide 1: Reports on TMVP off versus TMVP on
Hyo Min Choi, Jung Hak Nam,
and Dong Gyu Sim
<number>
JCTVC-I0097
Notes: <number>

## Slide 2: History of TMVP on/off
7th JCT-VC meeting adopted to explicitly send the enable_temporal_mvp _flag at the PPS (JCTVC-G398)
  It is helpful in error robustness point of view.
7th and 8th JCT-VC meeting, it was insisted that the flag move to P and B slice header (JCTVC-G398, JCTVC-H0570, JCTVC-I0420)
  It cleans up marking process in decoder.
  It prevents a problem by slice headers sharing an identical PPS.
<number>

## Slide 3: Significant coding loss by TMVP off
We found that the TMVP off case makes significant coding loss
  About 2~3%
Coding loss by TMVP off , compared to TMVP on in RA case.
<number>
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 1.8% | -0.1% | -0.2% | 2.7% | 2.1% | 2.5%
Class B | 2.5% | 1.6% | 1.6% | 2.4% | 1.6% | 1.6%
Class C | 2.6% | 2.4% | 2.5% | 2.5% | 2.2% | 2.4%
Class D | 3.0% | 2.5% | 2.6% | 2.9% | 2.2% | 2.4%
Overall | 2.5% | 1.6% | 1.6% | 2.6% | 2.0% | 2.2%
Class F | 1.1% | 1.1% | 1.1% | 1.0% | 1.0% | 0.6%

## Slide 4: Significant coding loss by TMVP off (cont’d)
Coding loss by TMVP off, compared to TMVP on in LB case
Coding loss by TMVP off, compared to TMVP on in LP case
<number>
 | Low delay P Main |  |  | Low delay P HE10 |  | 
 | Y | U | V | Y | U | V
Class B | 2.3% | 1.7% | 1.5% | 2.1% | 1.8% | 1.5%
Class C | 2.5% | 2.5% | 2.3% | 2.3% | 2.0% | 2.1%
Class D | 2.5% | 1.9% | 2.2% | 2.4% | 1.9% | 1.8%
Class E | 2.0% | 2.6% | 2.7% | 2.0% | 2.7% | 3.1%
Overall | 2.3% | 2.1% | 2.1% | 2.2% | 2.0% | 2.0%
Class F | 2.0% | 1.8% | 2.5% | 1.7% | 2.2% | 3.6%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class B | 2.7% | 2.3% | 2.3% | 2.6% | 2.1% | 1.7%
Class C | 3.0% | 2.9% | 3.1% | 2.9% | 2.7% | 2.8%
Class D | 2.9% | 2.8% | 2.5% | 2.8% | 2.5% | 2.0%
Class E | 2.3% | 2.5% | 2.5% | 2.4% | 2.2% | 2.8%
Overall | 2.8% | 2.6% | 2.6% | 2.7% | 2.4% | 2.3%
Class F | 2.1% | 1.8% | 1.9% | 2.0% | 1.5% | 2.7%

## Slide 5: Propose
To compensate the coding loss by TMVP off, we suggest to send an auxiliary vector at the PPS or P and B slice header
  The way to generating the auxiliary vector is encoding issue only.
For error concealment or the others, it also would be helpful
  In this scenario, usage index for the auxiliary vector should be sent.
<number>

## Slide 6: Experiments to obtain the auxiliary vector
We extract the auxiliary vector for each P and B slice from HM6.1 bitstream on the three conditions
  1st condition
    Step 1. extract vectors from the AMVP and MERGE when the vector is not zero and reference index for the list_0 is 0.
    Step 2. estimate the number of frequency for those vector. A vector which has the highest frequency is chosen as the auxiliary vector for the slice.
    Step 3. If there are several vectors which have identical the number of frequency in Step 2, a vector which has the largest absolute value for the horizontal is chosen.
  2nd condition
    Step 1. extract vectors only from the AMVP on identical condition.
    Step 3. After procedure is same as well as the first condition.
  3rd condtion
    Step 1. extract vectors from the AMVP algorithm when the reference index for the list_0 is 0.
    Step 2. same as well
    Step 3. auxiliary vector for each P and B slice is sent to decoder when it is not zero vector.
<number>

## Slide 7: Experiment results for the proposal on TMVP off
The auxiliary vector is exploited as one of of candidates of AMVP and MERGE in decoder side when TMVP off case
We evaluate the proposed one for Class E and F with main profile on condition of LB and LP
  LB case
<number>

## Slide 8: Experiment results for the proposal on TMVP off
  LP case
<number>
 | HM6.1-TMVP on vs. HM6.1-TMVP off |  |  | HM6.1-TMVP off vs. HM6.1-proposal |  | 
 | Y | U | V | Y | U | V
FourPeople | 1.7% | 1.4% | 2.7% | 0.0% | -0.2% | -0.7%
Johnny | 1.9% | 2.1% | 1.9% | 0.1% | -0.9% | 0.3%
KristenAndSara | 2.5% | 4.5% | 3.3% | -0.3% | -1.2% | -1.5%
BasketballDrillText | 1.5% | 1.7% | 1.4% | 0.4% | 0.2% | 1.2%
ChinaSpeed | 2.0% | 1.4% | 2.3% | 0.0% | 0.4% | -0.4%
SlideEditing | 2.4% | 1.3% | 1.7% | -2.0% | -0.9% | -1.2%
SlideShow | 1.9% | 2.8% | 4.5% | -0.8% | -1.7% | -2.7%
Overall | 2.0% | 2.1% | 2.6% | -0.4% | -0.6% | -0.7%

## Slide 9: Conclusion
The proposed technique is very effective for such a sequence which has only single orientation or includes any particular movement
  SlideEditing and SlideShow.
In the future, we believe additional aux_idc syntax can describe the meaning of the auxiliary vector.
  Compensating coding loss by TMVP off
  Error concealment
  Other scenario.
<number>

## Slide 10: Recommendation
This contribution should be considered at not only any performance compensation for the TMVP off, but also other error concealment technique.
We recommend further study in adhoc group related to TMVP options
<number>