## Slide 1: AHG7: Level definition to limit memory bandwidth of MC JCTVC-I0107
Kenji Kondo and Teruhiko Suzuki
Sony

## Slide 2: Summary
Motivation
Proposed methods
  Removal of “inter_4x4_enabled_flag”
  Restrict small MC block and bi-prediction.
  Limit maximum number of motion vectors
Experiment
  BD% impact for block restriction
Conclusion

## Slide 3: Motivation
The bandwidth significantly increases as corresponding to image size and frame rate.
Class A and B

## Slide 4: Motivation
The bandwidth limitation is required.
  The bandwidth is depend on image size and frame rate.
    It is widely changing.
  Level definition should have flexibility.
    For example, when new level will be required in future it’s better to easily add new level.
Simple ideas how to limit the bandwidth
  PU restriction
  Limit number of MVs

## Slide 5: inter_4x4_enabled_flag
HEVC text specification draft 6, JCTVC-H1003
  The “inter_4x4_enabled_flag” is specified.
In common test condition, the “inter_4x4_enabled_flag” is equal to zero.
  Inter 4x4 block is disabled.
  It is good for memory bandwidth.
    Although it’s not enough for large image.
  We recommend that
    inter_4x4_enabled_flag always sets to zero.
    The flag is removed.
  Further restriction is required for large image or high frame rate.

## Slide 6: Idea to limit max bandwidth
PU restriction
Limit max number of motion vectors

## Slide 7: PU restriction
 | Prohibition mode (X mark means the mode is not to be used.) |  |  |  |  | Worst B/W, Worst mode
 | Bi-4x4 | Bi-4x8, Bi-8x4 | Uni-4x4 | Bi-8x8 | Uni-4x8, Uni-8x4 | 
Anchor | X |  | X |  |  | 0%, Bi-4x8
R0 |  |  |  |  |  | +52%, Bi-4x4
R1 | X |  |  |  |  | 0%, Bi-4x8
R2 | X | X | X |  |  | -44%, Bi-8x8
R3 | X | X | X | X |  | -50%, Uni-4x8
R4 | X | X | X | X | X | -58%, Bi-8x16

## Slide 8: Proposal for max number of MVs
This proposal limits max number of MVs as same as AVC standard.
The B2 is the same as level 3.1 and above of AVC.
 | Maximum number of MVs in one LCU |  | 
LCU size | B1 | B2 | B3
16x16 | 16 | 8 | 4
32x32 | 64 | 32 | 16
64x64 | 256 | 128 | 64

## Slide 9: Relationship between two methods
PU restriction | Number of MVs
R1 | B1
R2 | B2
R3 | B2
R4 | B3
For example, if the PU restriction R2 is protected, number of MVs limit B2 is automatically protected.
In AVC standard, the number of MVs is defined,
however in real encoder, we think that the PU restriction is often used.

## Slide 10: One example for level
 | Prohibition mode (X mark means the mode is not to be used.) |  |  |  |  | Number of MVs in one LCU 64x64 | Image size
 | Bi-4x4 | Bi-4x8, Bi-8x4 | Uni-4x4 | Bi-8x8 | Uni-4x8, Uni-8x4 |  | 
R1 | X |  |  |  |  | 256 (B1) | 
R2 | X | X | X |  |  | 128 (B2) | HD~
R3 | X | X | X | X |  | 128 (B2) | 4K2K 60p~
R4 | X | X | X | X | X | 64 (B3) | 8K2K 60p~

## Slide 11: Pros/Cons for two methods
PU restriction
  Simpler for encoder process
    Have some coding efficiency loss
  Easier to check a conformance
Max. number of MVs
  May reduce coding efficiency loss
    However difficult to control the number of MVs
    In real encoder, we think that the PU restriction is often used.
  Slight difficult to check a conformance
    we’re afraid that there will be illegal stream.
Recommendation
  PU restriction is recommended.

## Slide 12: Avg. BD% for class A, B
Cs | Class | R2 | R3 | R4 | R3+I0107
LB-HE10 | A | 0.4 | 0.9 | 1.3 | 0.2
 | B | 0.3 | 1.3 | 1.6 | 0.6
LB-HE10 |  | 0.3 | 1.1 | 1.5 | 0.4
LB-Main | A | 0.4 | 1.3 | 1.8 | 0.5
 | B | 0.4 | 1.6 | 2.1 | 0.8
LB-Main |  | 0.4 | 1.5 | 2.0 | 0.7
RA-HE10 | A | 0.2 | 0.6 | 0.9 | 0.2
 | B | 0.2 | 1.0 | 1.3 | 0.7
RA-HE10 |  | 0.2 | 0.8 | 1.1 | 0.5
RA-Main | A | 0.3 | 0.9 | 1.3 | 0.5
 | B | 0.3 | 1.3 | 1.7 | 0.9
RA-Main |  | 0.3 | 1.1 | 1.5 | 0.7
 | Overall | 0.3 | 1.1 | 1.5 | 0.6
Unfortunately, the restriction brings coding efficiency loss.
However, it’s possible to reduce with other techniques such as JCTVC-I0107.

## Slide 13: Conclusions
It is recommended that
  The removal of “inter_4x4_enabled_flag”
    inter_4x4_enabled_flag permanently sets to 0.
  To limit the memory bandwidth of MC,
    the PU restriction or number of MVs is included in level definition.
      We think that the PU restriction is better.

## Slide 14: Supplemental slides

## Slide 15: Discussion of desirable restriction
Possible to constrain the max memory bandwidth
  In relevant small region
    A restriction for PU level is best to limit the bandwidth but it will increase the coding efficiency loss.
    A restriction for picture level is difficult to design hardware both encoder and decoder, but it will decrease the coding efficiency loss.
    We think that the restriction for each LCU or CU is good trade-off.
Easy to check the conformance
  To motivate us to protect this level definition.
Good flexibility for new level
  In the future, new level may be defined by something reason.
Harmless coding performance

## Slide 16: Avg. BD% for class A, B
Class A is added for Low Delay case.