## Slide 1: AHG7: Modification of merge candidate derivation to reduce MC memory bandwidth JCTVC-I0107
Kenji Kondo, T. Suzuki (Sony)
and
Tomoyuki Yamamoto (Sharp)

## Slide 2: Summary
Memory bandwidth is important issue for MC because
  the decoder throughput is limited by bandwidth of MC in especially large image application.
Introduce the proposed methods
Experiment
  Check coding efficiency
Conclusion

## Slide 3: Overview how to limit bandwidth
The restriction of small PU is proposed in JTCVC-I0106.
  As corresponding to level
    Prohibit small block size and bi-prediction.
    Limit max number of motion vectors.
This proposal helps merge mode
  When bi-prediction is restricted by level, the encoder can not choose merge candidates of bi-prediction.
    Unfortunately it brings coding efficiency loss.
  To use merge mode, this proposal replaces prediction direction.
    It can avoid the coding efficiency loss.

## Slide 4: Proposal
Send “disable_bip_small_mrg_idc” in sps
  It replaces merge candidates of bi-prediction to L0-prediction for following block size
    0: no modification
    1: 4x4
    2: 4x4, 8x4, 4x8
    3: 4x4, 8x4, 4x8, 8x8
In derivation of merge candidates
  When current block size is included in above groups corresponding to the “disable_bip_small_mrg_idc”,
    Bi prediction is replaced to uni-predcition.
It can increase a chance to use merge mode when bi-pred is restricted.

## Slide 5: Experiments 1
Check the overhead of this proposal
  The common test condition is used.
  “disable_bip_small_mrg_idc” sets to 0.

## Slide 6: Overhead
 | Random Access Main |  |  | Random Access HE10 |  |  | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E |  |  |  |  |  |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 99% |  |  | 100% |  | 

## Slide 7: Experiments 2
Check to avoid coding efficiency loss with proposal
  Compare BD% between with/without this proposal based on PU restriction
  “inter_4x4_enabled_flag” sets to 1
    However, 4x4 bi-prediction is restricted by the PU restriction in encoder.

## Slide 8: Experiments 2
Restriction | Without proposal | With proposal
R1 | Case-B | Case-F disable_bip_small_mrg_idc=1
R2 | Case-C | Case-G disable_bip_small_mrg_idc=2
R3 | Case-D | Case-H disable_bip_small_mrg_idc=3
This Restriction case is proposed in JCTVC-I106
R1: (4x4) bi-prediction
R2: (4x4, 4x8, 8x4) bi-prediction, 4x4 uni-prediction
R3: (4x4, 4x8, 8x4, 8x8) bi-prediction, 4x4 uni-prediction

## Slide 9: BD% Results
Cs | Class | R1 | R2 | R3 | R1+proposal | R2+proposal | R3+proposal
LB-HE10 | A | 0.0 | 0.4 | 0.9 | 0.0 | 0.1 | 0.2
 | B | 0.0 | 0.3 | 1.3 | 0.0 | 0.2 | 0.6
 | C | 0.0 | 0.7 | 1.9 | -0.1 | 0.4 | 1.1
 | D | -0.1 | 1.0 | 2.4 | -0.2 | 0.7 | 1.5
 | E | 0.0 | 0.3 | 0.9 | 0.0 | 0.1 | 0.3
LB-HE10 |  | 0.0 | 0.5 | 1.4 | -0.1 | 0.3 | 0.7
LB-Main | A | 0.0 | 0.4 | 1.3 | 0.0 | 0.1 | 0.5
 | B | 0.0 | 0.4 | 1.6 | 0.0 | 0.2 | 0.8
 | C | 0.0 | 0.9 | 2.4 | -0.1 | 0.5 | 1.3
 | D | 0.0 | 1.2 | 2.7 | -0.1 | 0.7 | 1.6
 | E | 0.0 | 0.7 | 1.6 | 0.1 | 0.2 | 0.5
LB-Main |  | 0.0 | 0.7 | 1.9 | 0.0 | 0.3 | 0.9
RA-HE10 | A | 0.0 | 0.2 | 0.6 | 0.0 | 0.0 | 0.2
 | B | 0.0 | 0.2 | 1.0 | 0.0 | 0.2 | 0.7
 | C | 0.0 | 0.4 | 1.3 | -0.1 | 0.3 | 1.0
 | D | -0.1 | 0.7 | 1.8 | -0.1 | 0.6 | 1.5
RA-HE10 |  | 0.0 | 0.4 | 1.2 | -0.1 | 0.3 | 0.8
RA-Main | A | 0.0 | 0.3 | 0.9 | 0.0 | 0.1 | 0.5
 | B | 0.0 | 0.3 | 1.3 | 0.0 | 0.2 | 0.9
 | C | -0.1 | 0.6 | 1.7 | -0.1 | 0.4 | 1.2
 | D | -0.1 | 0.8 | 2.1 | -0.2 | 0.7 | 1.7
RA-Main |  | 0.0 | 0.5 | 1.5 | -0.1 | 0.4 | 1.1
 | Overall | 0.0 | 0.5 | 1.5 | -0.1 | 0.3 | 0.9

## Slide 10: BD% Results
Cs | R1 | R2 | R3 | R1+proposal | R2+proposal | R3+proposal
LB-HE10 | 0.0 | 0.5 | 1.4 | -0.1 | 0.3 | 0.7
LB-Main | 0.0 | 0.7 | 1.9 | 0.0 | 0.3 | 0.9
RA-HE10 | 0.0 | 0.4 | 1.2 | -0.1 | 0.3 | 0.8
RA-Main | 0.0 | 0.5 | 1.5 | -0.1 | 0.4 | 1.1
Overall | 0.0 | 0.5 | 1.5 | -0.1 | 0.3 | 0.9
Class A is added for low delay case
0.6% improving on R3
0.2% improving on R2

## Slide 11: Avg. BD% on R2

## Slide 12: Avg. BD% on R3

## Slide 13: Conclusions
Introduced proposed methods
  Send “disable_bip_small_mrg_idc” in sps
  In derivation of merge, it replace bi-prediction to uni-prediction when block size is corresponding to “disable_bip_small_mrg_idc”.
In experiments,
  The overhead of this proposal was negligible.
  With this proposal, the BD% is improved on condition of PU restriction.
    0.6% improved on R3
Recommendation
  Adopt level dependent restriction of bi-pred in small blocks
  Adopt proposed merge derivation modification

## Slide 14: Supplementary
Encoding time
Decoding time
R0 + proposal

## Slide 15: Summary for R1
Restriction | R1 (4x4 bi-prediction) | 
 | Without proposal | With proposal disable_bip_small_mrg_idc=1
LB-Main | 0.0% (109, 100) | 0.0% (116, 99)
LB-HE10 | 0.0% (114, 101) | -0.1% (114, 101)
RA-Main | 0.0% (109, 100) | -0.1% (114, 100)
RA-HE10 | 0.0% (107, 100) | -0.1% (112, 100)
(Enc. time%, Dec. time%)

## Slide 16: Summary for R2
Restriction | R2 (4x4, 4x8, 8x4 bi-prediction, 4x4 uni-prediction) | 
 | Without proposal | With proposal disable_bip_small_mrg_idc=2
LB-Main | 0.8% (91, 100) | 0.4% (91, 100)
LB-HE10 | 0.6% (92, 101) | 0.3% (93, 101)
RA-Main | 0.5% (92, 100) | 0.4% (93, 100)
RA-HE10 | 0.4% (94, 100) | 0.3% (94, 100)
(Enc. time%, Dec. time%)

## Slide 17: Summary for R3
Restriction | R3 (4x4, 4x8, 8x4, 8x8 bi-prediction, 4x4 uni-pred.) | 
 | Without proposal | With proposal disable_bip_small_mrg_idc=3
LB-Main | 2.1% (86, 98) | 1.1% (88, 98)
LB-HE10 | 1.7% (89, 100) | 0.9% (90, 100)
RA-Main | 1.5% (89, 99) | 1.0% (91, 99)
RA-HE10 | 1.2% (91, 99) | 0.8% (93, 99)
(Enc. time%, Dec. time%)

## Slide 18: Results
Restriction | R0 (non restriction) | 
 | Without proposal | With proposal disable_bip_small_mrg_idc=0
RA-Main | -0.1% (114, 100) | -0.1% (114, 100)
RA-HE10 | -0.1% (112, 100) | -0.1% (112, 100)
LB-Main | -0.1% (116, 99) | -0.1% (116, 100)
LB-HE10 | -0.1% (114, 101) | -0.1% (114, 101)
(Enc. time%, Dec. time%)