## Slide 1
Long-term picture signaling for error-free environments (JCTVC-I0112)
Karsten Suehring, Heiko Schwarz, Thomas Wiegand

## Slide 2: Proposed method
Simplified coding of long-term pictures for error-free environments
Very bitrate efficient
Switchable in the SPS

## Slide 3: Example: DPB state
POC: 5
POC: 7
POC: 10
In error-free environments both encoder and decoder share the same DPB state
only pictures marked “used for reference” shown here
POC: 9
POC: 8
POC: 1

## Slide 4: Step 1: Apply short-term RPS
POC: 5
POC: 7
POC: 10
POC: 9
POC: 8
POC: 1
Short-term RPS marking
Not changed

## Slide 5: Step 2: Order remaining pictures
POC: 5
POC: 7
POC: 10
POC: 9
POC: 8
POC: 1
Order remaining pictures by POC (assign indexes)
0
1
2

## Slide 6: Step 3: long-term marking
POC: 5
POC: 7
POC: 10
POC: 9
POC: 8
POC: 1
Mark long-term pictures based on index
0
1
2
long_term_idx[ 0 ] = 0
long_term_idx[ 1 ] = 2

## Slide 7: Step 4: discard remaining pictures
POC: 5
POC: 7
POC: 10
POC: 9
POC: 8
POC: 1
mark remaining pictures unused for reference

## Slide 8: SPS Syntax

## Slide 9: Slice Header Syntax

## Slide 10: Results
Based on Common conditions for reference picture marking and list construction proposals
Case 2.6 (Interview type scene cuts)
 | 10/30 with 4800 frames | 20/60 with 9600 frames
HM 6.1 | 87937 | 190867
proposed | 21527 | 43127
 | -75.5% | -77.40%
Δbits/SH | -13.8 | -15.4
60 fps
24 fps
 | 10/30 with 1920 frames | 20/60 with 3840 frames
HM 6.1 | 32137 | 68763
proposed | 8567 | 17207
 | -73.34% | -74.98%
Δbits/SH | -12.3 | -13.4

## Slide 11: Results
Based on Common conditions for reference picture marking and list construction proposals
Case 3.3 (two long-term pictures based on decoder feedback)
 | 200 ms RTT 600 frames | 1000 ms RTT 600 frames
HM 6.1 | 11890 | 15590
proposed | 5419 | 5155
 | -54.42% | -66.93%
Δbits/SH | -10.8 | -17.4
60 fps
24 fps
 | 200 ms RTT 240 frames | 1000 ms RTT 240 frames
HM 6.1 | 3916 | 5296
proposed | 2215 | 2059
 | -43.44% | -61.12%
Δbits/SH | -7.1 | -13.5

## Slide 12: Summary
Very effective long-term coding (up to ~75% gain on long-term syntax elements)
Simplified decoding and marking processes
Switchable in SPS
Complete syntax, semantics and decoding process in the contribution