## Slide 1
I0125: On Reference List Combination
Ilkoo Kim
Samsung Electronics Co., Ltd
April. XX, 2012
Notes: <number>

## Slide 2: Background
Combined list
  Non-normative part
    Restrict encoder search for duplicated reference pictures in both lists for uni-directional prediction search
    In the above example, Ref4 in List0 and Ref2 in List1 are restricted to be searched
  Normative part
    Construction process for combined list (By default or By explicit signaling)
    Need to keep where each element in the combined list is originated from in each list
    Mapping motion information of LC to motion information of L0 or L1 to be used motion information prediction
    Needs condition checking whether it goes with L0 or L1 ref index coding or LC ref index coding
<number>

## Slide 3: Motivation
Keep non-normative part and cleanup normative part
  Maintaining encoder search restriction by reference list combination
    If the encoder doesn’t restrict uni-directional prediction search for duplicated pictures, then it potentially improves coding efficiency while complexity is increased by flexibility
    The decoder doesn’t construct the combined list
  Unify reference index coding for uni-directional and bi-directional prediction in B slice type
    Do not convert ref idx of Pred_LC to ref idx of either Pred_L0 or Pred_L1
  Unify reference index coding for uni-directional prediction between P and B slice types
    Use L0 or L1 for uni-directional in B slice as L0 is used in P slice
<number>

## Slide 4: Slice data change
Reference index
  The branch to differentiate between uni-directional in combined list and others is removed
Inter prediction mode
  Pred_LC is changed to Pred_L0 and Pred_L1
  The number of bins coded is changed from 1 to 2 in maximum
<number>
slice_type | Inter_pred_flag | Name of inter_pred_flag
P | Inferred | Pred_L0
B | 0 | Pred_LC
 | 1 | Pred_BI
slice_type | Inter_pred_flag | Name of inter_pred_idc
P | Inferred | Pred_L0
B | 0 | Pred_L0
 | 1 | Pred_L1
 | 2 | Pred_BI
First bin
Second bin
0
1
0
1
Pred_BI
Pred_L0
Pred_L1

## Slide 5: Inter prediction mode coding
The current context model index derivation
  Determined by the CU depth having values range 0..3 ctxIdx = cuDepth
The proposed context model index derivation
  Keeping the same number of context model
    The first bin is capped by 2 (range 0..2) ctxIdx = (cuDepth > 2? 2 : cuDepth)
    The second bin is coded with the context corresponding to 3
  Using the one additional context model
    The first bin is unchanged (range 0..3) ctxIdx = cuDepth
    The second bin is coded with the new context = 4
<number>
 | Same context models | 1 Additional context
RA Main | -0.1% | -0.1%
LDB Main | -0.1% | -0.1%
RA HE10 | 0.0% | 0.0%
LDB HE10 | 0.0% | -0.1%
Average | 0.0% | -0.1%

## Slide 6: WD and HM modification
Several syntaxes specified for combined list are removed
  ref_pic_list_combination()
  lc wp parameters in pred_weight_table()
  lc motion information such as ref_idx_lc, mvd_lc, mvp_lc_flag
Special branches for combined list are removed
  Lc related part in ‘Weighted sample prediction process’
  Converting part for LC in ‘Derivation process for motion vector components and reference indices’
Special sections for combined list process are removed
  ‘Mapping process for reference picture lists combination in B slices’
<number>

## Slide 7: Conclusion
By removing combined list,
  Several syntaxes and decoding process are cleaned up
  Syntaxes are unified with P slice and Bi-directional prediction in B slice
  Performance improvement is also observed as 0.1% gain in random access and no loss in low delay B condition
  It is proposed to remove normative parts of combined list while keeping non-normative parts in SW.
<number>

## Slide 8
Thank you !
<number>