## Slide 1
I0130: Simplification on SAO syntax
Elena Alshina
Samsung Electronics Co., Ltd
April. XX, 2012
Notes: <number>

## Slide 2: APS SAO parameters
APS specified SAO parameters
  There are syntaxes exists for APS mode: one unit flags and repeat row flags
    One unit flags exist for each color components and specify that all coding treeblocks are processed using the same SAO parameters or not
    Repeat row flags exist for each color components and specify that the SAO parameters of coding treeblocks in the current coding treeblock row are the same as those of above coding treeblocks
<number>

## Slide 3: APS SAO parameters
Syntax and semantics of one unit flags and repeat row flags
<number>
sao_one_luma_unit_flag equal to 1 specifies that all of coding treeblocks in luma component of current slice are processed using the same SAO parameters; equal to 0 specifies that the SAO parameters for the luma component are signalled on a coding treeblock basis.
sao_one_cb_unit_flag equal to 1 specifies … for the Cb component …
sao_one_cr_unit_flag equal to 1 specifies … for the Cr component …
sao_repeat_row_flag[ cIdx ] equal to 1 specifies that the SAO parameters of coding treeblocks in the current coding treeblock row are the same as those of above coding treeblocks for the colour component cIdx; equal to 0 specifies that the current coding treeblock row has new SAO parameters. When sao_repeat_row_flag is not present, it is inferred to be equal to 0.

## Slide 4: Experimental results
CE1 SW where the most right and bottom pixels (which are modified during deblocking filter) are not used for statistics collection as the base SW and follows the CE1 test condition.
The anchor data is SAO off and the test conditions are RA Main and RA HE10 for LCU size of 64, 32 and 16.
The following results summarize overall performance difference from SAO on case
<number>
 | No One Unit Flags |  | No Repeat Row Flags |  | No One Unit & Repeat Row | 
LCU Size | RA_Main | RA_HE10 | RA_Main | RA_HE10 | RA_Main | RA_HE10
64 | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.1
32 | 0.1 | 0.1 | 0.2 | 0.1 | 0.3 | 0.2
16 | 0.1 | 0.1 | 0.5 | 0.3 | 0.7 | 0.6

## Slide 5: Conclusion
Since there is negligible performance drop by removing “one unit flags” while keeping syntax as clean, it is proposed to remove one unit flags.
However, “repeat row flags” proves coding efficiency in small LCU sizes.
<number>

## Slide 6
Thank you !
<number>