## Slide 1
NAL Unit header for scalable extension
Byeongdoo Choi, Chanyul Kim, Jaehyun Kim, Jeonghoon Park
Samsung Electronics Co., Ltd
Apr., 2012
Notes: <number>

## Slide 2: Introduction
NAL unit header
  MVC/SVC : base (1 byte), non-base (4 bytes) -> variable
    Extended 3 byte : view ID, priority ID, temporal ID, dependency ID, quality ID are present
  HEVC-extension : 2 bytes -> fixed
    Reserved 5 bits for 3D/scalable extension
  Needs on flexible design of NAL unit header
  for signaling scalability information
<number>

## Slide 3: Goal
Signaling most of useful scalability information in NAL unit header
  In order that Network Elements get the important scalability information only by parsing NAL unit header for bitstream management
  No needs to parse any parameter set in Network-level
No change to the current specification text
  Without change to NAL unit header or new parameter set.
  The modification is only swapping the position of the temporal_id and the reserved_one_5bits in NAL unit header, but not mandatory.
<number>

## Slide 4: NAL unit design
Current NAL unit header of HEVC
<number>
F: forbidden_zero_bit
NRF: nal_ref_flag
NUT: nal_unit_type
TID : temporal_id
R5 : reserved_one_5bits

## Slide 5: Concept
<number>
Base layer :
Enhancement layer :
(non-base)
NAL unit header of HEVC
+ VCL
Proposed NAL unit header
+ VCL

## Slide 6: Proposed NAL unit design
Proposed NAL unit header for scalable/3D extension
<number>
SET : scalable_extension_type specifies the type of scalability currently used, and how to map the layer_id into several scalability identifiers, e.g. dependency_id, quality_id, view_id, temporal_id, priority_id and so on.
LID : layer_id specifies the layer identifier, which can be mapped into the dependency_id, quality_id, view_id, temporal_id, priority_id and so on.
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
F
NRF
NUT
LID
SET
M bits
(2~3 bits)
N bits
(5~6bits)

## Slide 7: Mapping method of layer_id #1
<number>
SET (2bits) | layer_id_0 (3bits) | layer_id_1 (3bits)
0 | priority_id (6bits) | 
1 | view_id (3bits) | temporal_id (3bits)
2 | dependency_id (3bits) | quality_id (3bits)
3 | dependency_id (3bits) | temporal_id (3bits)
Direct mapping into scalability ID by splitting sub-layer IDs
  The layer_id (6bits) can be split into two or three sub_layer_id,
  and each sub_layer_id can be mapped into a specific identifier.

## Slide 8: Mapping method of layer_id #2
<number>
Indirect mapping with predefined mapping tables
  The mapping method using a look-up table, which is signaled in SEI message or predefined in the specification text.
Layer ID (SET = k) | Dependency ID | Quality ID | View ID | Temporal ID
0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0
2 | 2 | 0 | 0 | 0
3 | 3 | 0 | 0 | 0
4 | 3 | 1 | 0 | 0
5 | 4 | 0 | 0 | 0
6 | 1 | 0 | 1 | 0
7 | 1 | 0 | 1 | 1

## Slide 9: Conclusion
Without change to HEVC specification text
  All scalable/3D extension is possible
  Most of useful information for scalability can be delivered in NAL unit header.
Only one syntax modification recommended is to swap the position of the temporal_id and the reserved_one_5bits in NAL unit header.
<number>

## Slide 10
Thank you !
<number>