## Slide 1
POC signalling for CRA picture
Byeongdoo Choi, Chanyul Kim, Jaehyun Kim, Jeonghoon Park
Samsung Electronics Co., Ltd
Apr., 2012
Notes: <number>

## Slide 2: Proposal
Explicit signaling of POC MSB in CRA picture
  Benefit
    Detection of random access and frame loss without system’s notification
      By comparing the POC MSB inferred from the previous POC and the POC MSB signaled explicitly.
    POC synchronization in multiview extension
      Prevention of POC mismatch between views in view-point/layer switching points
<number>

## Slide 3: Detection of random access and frame loss
Detection of random access
  Detection of random access in CRA pictures without a notification from systems is helpful for discarding unused leading pictures at decoders.
Detection of frame loss
  The corrupted POC MSB shall be corrected by the MSB calculated from the cycle of MSB signalled in slice headers.
  It is asserted that error propagation should be stopped at random access points.
The explicit signaling of POC MSB in CRA pictures would have a negligible effect on coding efficiency.
<number>

## Slide 4: POC synchronization
Prevention of the POC mismatch in multi-views/multi-layers.
<number>
Layer switching or random access of each layer
may result in POC mismatch between layers(views)
I
B
I
b
b
View N
View 0
(base)
B
I
b
b
B
P
b
b
B
I
b
b
B
P
b
b
B
I
b
b
I
CRA
POC MSB is equal to 0 at view N
POC MSB is equal to k at base view
CRA
View-point/layer switching

## Slide 5: How to signal
<number>
slice_header( ) { | Descriptor
…………… | u(1)
if( IdrPicFlag ) { | 
idr_pic_id | ue(v)
no_output_of_prior_pics_flag | u(1)
} else { | 
if( nal_unit_type == 4 ) | 
pic_order_cnt_msb_cycle | u(v)
pic_order_cnt_lsb | u(v)
short_term_ref_pic_set_sps_flag | u(1)
…………… | 
} | 
In Slice header
pic_order_cnt_msb_cycle is used to determine the value of the most significant bits of the picture order count value of the CRA picture.

## Slide 6: How to calculate POC MSB
<number>
PicOrderCntMsb of the current picture is derived as follows
- If the current picture is a CDR picture,
PicOrderCntMsb = pic_order_cnt_msb_cycle* MaxPicOrderCntLsb
- Otherwise as specified by the following pseudo-code:
  if( ( pic_order_cnt_lsb < prevPicOrderCntLsb ) && ( ( prevPicOrderCntLsb − pic_order_cnt_lsb ) >= ( MaxPicOrderCntLsb / 2 ) ) ) PicOrderCntMsb = prevPicOrderCntMsb + MaxPicOrderCntLsb else if( (pic_order_cnt_lsb > prevPicOrderCntLsb ) && ( (pic_order_cnt_lsb − prevPicOrderCntLsb ) > ( MaxPicOrderCntLsb / 2 ) ) ) PicOrderCntMsb = prevPicOrderCntMsb − MaxPicOrderCntLsb else PicOrderCntMsb = prevPicOrderCntMsb

## Slide 7: Conclusion
We recommend to adopt the explicit signaling of POC MSB in slice header because of the following benefits.
  Detection of random access and frame loss without system’s notification
  POC synchronization in multiview extension
<number>

## Slide 8
Thank you !
<number>