## Slide 1: JCTVC-I0135: AHG15: Modification on picture marking process
<number>

## Slide 2
<number>
Problem statement
In current CD text, a picture marking process is described in section 8.3.2
  a long term picture marking process is conducted at first.
  After that, a short term picture marking process is conducted
In HM6.1 software,
  a short term picture marking process seems to be conducted at first
  After that, a long term picture marking process is conducted
 It seems a mismatch between text and software
Moreover, if one picture is assigned to both long term and short term picture at the same time, “no reference picture” would be assigned to either RefPicSetStCurrBefore or RefPicSetStCurrAfter
 it would not satisfy below bitstream conformance
In current specification, it seems possible to assign one picture to both long term and short term at the same time by RPS
  Encoder has to take care of whether or not RPS includes the picture which should be assigned to long term picture
  if encoder would set them illegally or mistakenly, the conformance error would be happened
When the first coded picture in the bitstream is an IDR picture or the current coded
picture is not a leading picture of the first coded picture in the bitstream,
there shall be no entry in RefPicSetStCurrBefore, RefPicSetStCurrAfter or RefPicSetLtCurr that is equal to "no reference picture".

## Slide 3
To prevent conformance error even if one picture is assigned to both long term and short term picture at the same time by RPS
Modified picture marking process is proposed
Proposed method

## Slide 4
Proposal
One picture could be assigned to both long term and short term picture at the same time
 However, long term assignment would be taken high priority
Assignment on short term picture would be ignored if a picture has been already marked as long term picture
Benefit
Encoder would not be needed to take care of whether or not RPS includes the picture which should be assigned to long term picture
Even if encoder would set them illegally or mistakenly, conformance error would be avoidable
No need to change RPS for short term picture even if long term picture is used
 RPS in SPS could be reused base on the position of coding structure
Modified picture marking process

## Slide 5
Modified part of CD text
The derivation process for the reference picture set and picture marking in section 8.3.2
Short term picture marking process
Calculate NumPocTotalCurr
If picX has already been assigned to long term,
short term picture assignment would be ignored

## Slide 6
Related issue on NumPocTotalCurr
In CD text, decoding process for RPS in section 8.3.2 is invoked after decoding of a slice header
However, the variable NumPocTotalCurr is used to parse list_entry_lX parameters in the slice header even though NumPocTotalCurr is calculated in section 8.3.2
  It would seem inconsistent
  This dependency might cause increasing waiting time for decoding a slice header
Especially, in this proposal, NumPocTotalCurr would be calculated after picture marking process to reflect ignored assignment of short term picture
  This dependency would affect more
Proposal
list_entry_lX parameters are decoded by using ue(v) instead of u(v)
The condition “NumPocTotalCurr > 1” is removed
ref_pic_list_modification( ) { | Descriptor
if( slice_type = = P ¦ ¦ slice_type = = B ) { | 
ref_pic_list_modification_flag_l0 | u(1)
if( ref_pic_list_modification_flag_l0 && NumPocTotalCurr > 1 ) | 
for( i = 0; i <= num_ref_idx_l0_active_minus1; i++ ) | 
list_entry_l0[ i ] | ue (v)
} … | 
Resolve inconsistency in CD text and remove dependency

## Slide 7
<number>
Simulation Result
Condition
The proposed method was implemented to HM6.1-dev-ahg15 software
It was evaluated whether bitstream conformance error would be happened or not if one picture is assigned to both long term picture and short term picture at the same time
  The test case 2.6 in the common conditions for reference picture marking and list construction described in JCTVC-H0725 was used
  the encoder function “rpsContainsShortTermReference()” was comment out to evaluate without encoder based restriction
Result
It was confirmed that decoding errors would be happened without this proposal, if the picture was marked as both long term and short term picture at the same time
It was confirmed that any errors would not be happened by applying this proposal, even though the picture was marked as both long term and short term picture at the same time
Cross checked by JCTVC-I0538 (Thanks to Sharp)

## Slide 8
<number>
Mismatch on picture marking process between CD text and HM6.1 software was reported
It was proposed to ignore short tem picture assignment for a picture which got duplicated assignment of long term and short term reference at the same time
It was confirmed that any errors would not be happened by applying this proposal, even though the picture was marked as both long term and short term picture at the same time
We suggest the proposed method be adopted in the DIS of HEVC
Conclusion