## Slide 1
Syntax on wavefront information
(JCTVC-I0139)
Chanyul Kim, Seungsoo Jeong
(Samsung)
Notes: <number>

## Slide 2: Background
HEVC has many tools to support parallel processing in multi-core environments
  Tiles, WPP, Slice, Entropy Slice
In the last meeting, it was adopted that Tiles, WPP and Entropy Slice shall be used exclusively and any combination of those is disallowed.
Since the purpose of those tools is regarded as similar each other, these tools’ syntaxes can be designed and controlled in a same manner.
Now, in Tile & WPP, signaling information is sent by the syntax “tiles_or_entropy_coding_sync_idc” ( 0: nothing, 1: Tile, 2: WPP )
In Tile case, the number of Tile is signaled in SPS level after parsing the syntax “tiles_or_entropy_coding_sync_idc”.
In WPP case, the number of substreams is not signaled in SPS level after parsing the syntax “tiles_or_entropy_coding_sync_idc”.
It is proposed to unify syntax design by sending WPP information in SPS level too.
<number>

## Slide 3: Proposed
Move the syntax “num_substreams_minus1” from PPS to SPS.
Add substreams_info_present_flag into PPS.
<number>
pic_parameter_set_rbsp( ) { | Descriptor
… | 
if( tiles_or_entropy_coding_sync_idc = = 1 ) { | 
tile_info_present_flag | u(1)
tile_control_present_flag | u(1)
if( tile_info_present_flag) { | 
num_tile_columns_minus1 | ue(v)
num_tile_rows_minus1 | ue(v)
uniform_spacing_flag | u(1)
if( !uniform_spacing_flag ) { | 
for( i = 0; i < num_tile_columns_minus1; i++ ) | 
column_width[ i ] | ue(v)
for( i = 0; i < num_tile_rows_minus1; i++ ) | 
row_height[ i ] | ue(v)
} | 
} | 
if( tile_control_present_flag ) | 
loop_filter_across_tiles_enabled_flag | u(1)
} | 
else if( tiles_or_entropy_coding_sync_idc = = 2 ) { | 
substreams_info_present_flag | u(1)
if(substreams_info_present_flag ) { | 
num_substreams_minus1 | ue(v)
} | 
} | 
… | 
} | 
seq_parameter_set_rbsp( ) { | Descriptor
… | 
tiles_or_entropy_coding_sync_idc | u(2)
if( tiles_or_entropy_coding_sync_idc = = 1 ) { | 
num_tile_columns_minus1 | ue(v)
num_tile_rows_minus1 | ue(v)
uniform_spacing_flag | u(1)
if( !uniform_spacing_flag ) { | 
for( i = 0; i < num_tile_columns_minus1; i++ ) | 
column_width[ i ] | ue(v)
for( i = 0; i < num_tile_rows_minus1; i++ ) | 
row_height[ i ] | ue(v)
} | 
loop_filter_across_tiles_enabled_flag | u(1)
} | 
else if( tiles_or_entropy_coding_sync_idc = = 2 ) { | 
num_substreams_minus1 | ue(v)
} | 
… | 
} | 

## Slide 4: Proposed
Assuming that WPP is never turned off within a sequence if it is signalled as enabled in SPS, the number of substreams would be the greater than or equal to 2
The syntax “num_substreams_minus1” is changed to the syntax “num_substreams_minus2”
<number>
pic_parameter_set_rbsp( ) { | Descriptor
… | 
if( tiles_or_entropy_coding_sync_idc = = 1 ) { | 
tile_info_present_flag | u(1)
tile_control_present_flag | u(1)
if( tile_info_present_flag) { | 
num_tile_columns_minus1 | ue(v)
num_tile_rows_minus1 | ue(v)
uniform_spacing_flag | u(1)
if( !uniform_spacing_flag ) { | 
for( i = 0; i < num_tile_columns_minus1; i++ ) | 
column_width[ i ] | ue(v)
for( i = 0; i < num_tile_rows_minus1; i++ ) | 
row_height[ i ] | ue(v)
} | 
} | 
if( tile_control_present_flag ) | 
loop_filter_across_tiles_enabled_flag | u(1)
} | 
else if( tiles_or_entropy_coding_sync_idc = = 2 ) { | 
substreams_info_present_flag | u(1)
if(substreams_info_present_flag ) { | 
num_substreams_minus2 | ue(v)
} | 
} | 
… | 
} | 
seq_parameter_set_rbsp( ) { | Descriptor
… | 
tiles_or_entropy_coding_sync_idc | u(2)
if( tiles_or_entropy_coding_sync_idc = = 1 ) { | 
num_tile_columns_minus1 | ue(v)
num_tile_rows_minus1 | ue(v)
uniform_spacing_flag | u(1)
if( !uniform_spacing_flag ) { | 
for( i = 0; i < num_tile_columns_minus1; i++ ) | 
column_width[ i ] | ue(v)
for( i = 0; i < num_tile_rows_minus1; i++ ) | 
row_height[ i ] | ue(v)
} | 
loop_filter_across_tiles_enabled_flag | u(1)
} | 
else if( tiles_or_entropy_coding_sync_idc = = 2 ) { | 
num_substreams_minus2 | ue(v)
} | 
… | 
} | 
num_substreams_minus2 plus 2 specifies the maximum number of subsets included in a slice when tiles_or_entropy_coding_sync_idc is equal to 2. When not present, the value of num_substreams_minus2 is inferred to be equal to 0.

## Slide 5: Proposed
slice_data( ) { | Descriptor
CtbAddrRS = SliceCtbAddrRS | 
CtbAddrTS = CtbAddrRStoTS[ CtbAddrRS ] | 
moreDataFlag = 1 | 
if( adaptive_loop_filter_flag && alf_cu_control_flag ) | 
AlfCuFlagIdx = −1 | 
do { | 
xCtb = InverseRasterScan( CtbAddrRS, CtbSize, CtbSize, pic_width_in_luma_samples, 0 ) | 
yCtb = InverseRasterScan( CtbAddrRS, CtbSize, CtbSize, pic_width_in_luma_samples, 1 ) | 
NumPCMBlock = 0 | 
CtbAddrInSlice = CtbAddrRS − ( slice_address >> SliceGranularity ) | 
AddrUp= CtbAddrRS – PicWidthInCtbs | 
… | 
if( moreDataFlag && ( ( tiles_or_entropy_coding_sync_idc = = 1 && TileId[ CtbAddrTS ] != TileId[ CtbAddrTS − 1 ] ) ¦ ¦ ( tiles_or_entropy_coding_sync_idc = = 2 && ( num_substream_minus2 + 1) > 0 && CtbAddrTS / PicWidthInCtbs <= ( num_substream_minus2 + 1) && CtbAddrTS % PicWidthInCtbs = = 0 ) ) ) { | 
rbsp_trailing_bits( ) | 
if( nextbits(24) = = 0x000002 ) { | 
entry_point_marker_two_3bytes | f(24)
tile_idx_minus_1 | u(v)
} | 
} | 
} while( moreDataFlag ) | 
} | 
<number>

## Slide 6: Conclusion
It is proposed to signal the number of substreams in SPS as well as in PPS to make current syntax design of WPP be more consistent with other parallel processing tool ( eg. Tile )
It makes a decoding strategy efficient according to decoder system to inform how many substreams are coded at higher syntax level (SPS).
Assuming that WPP is never turned off within a sequence if it is signalled as enabled in SPS, it is also proposed to signal the number of substreams as “num_substreams_minus2” instead of “num_substreams_minus1”
<number>