## Slide 1: AHG11: High level syntax modifications
Bin Li, Houqiang Li, Haitao Yang
University of Science and Technology of China
Huawei Technologies Co., Ltd.

## Slide 2: Outline
The nal_ref_flag restriction of CRA picture
Differentially signaling of per-temporal layer information
Position of signaling per-temporal layer information in SPS
POC derivation when num_reorder_pics is 0
Counter of Combined merge candidates

## Slide 3: The nal_ref_flag restriction of CRA picture
nal_ref_flag shall be equal to 1 for NAL units with nal_unit_type equal to 5 (IDR)
CRA picture may also be used as the first decoding picture of a sequence
  CRA picture should be used as reference picture
To make sure we can find prevRefPic when deriving POC

## Slide 4: Differentially signaling of per-temporal layer information
max_dec_pic_buffering[ i ] and num_reorder_pics[ i ] should be non-dreasing
We suggest to differentially signal those two syntax elements
for( i = 0; i <= max_temporal_layers_minus1; i++ ) { | 
max_dec_pic_buffering[ i ] | ue(v)
num_reorder_pics[ i ] | ue(v)
max_latency_increase[ i ] | ue(v)
} | 

## Slide 5: Position of signaling per-temporal layer information in SPS
Per-temporal layer information is too far always from max_temporal_layers_minus1
We suggest move those syntax elements together

## Slide 6: Position of signaling per-temporal layer information in SPS (Cont.)
Bitstream extracting may be applied at media gateway.
Per-temporal layer information may be used when extracting bitstream
  E.g. max_dec_pic_buffering
Move per-temporal layer information at earlier position in SPS

## Slide 7: POC derivation when num_reorder_pics is 0
num_reorder_pics equals to 0 means non-decreasing POC number
Non-dreasing POC derivation when num_reorder_pics is 0
When num_reorder_pics[max_temporal_layers_minus1] is equal to 0, maxPicOrderCnt – minPicOrderCnt shall be less than MaxPicOrderCntLsb / 2 is not necessary (C.3.2)

## Slide 8: Counter of Combined merge candidates
Already reported in ticket #395 and #396
JCTVC-I0141 proposes the same aspect
Propose to remove counter of combined merge candidate

## Slide 9
Int iCombinedCount = 0; ... for (Int idx=0; idx<uiCutoff*(uiCutoff-1) && uiArrayAddr!=MRG_MAX_NUM_CANDS && iCombinedCount<5; idx++) { ... if (...) {} else { uiArrayAddr++; iCombinedCount++; } }
When uiArrayAddr!=MRG_MAX_NUM_CANDS is satisfied, iCombinedCount<5 is also always satisfied.
iCombinedCount is not necessary