## Slide 1: Virtual large transform unit over maximum transform size with zero CBF
J. Kim
JCTVC-I0150

## Slide 2: Introduction
Chroma blocks cannot use maximum TU size since it should have identical transform split pattern to its corresponding luma block
64
64
Tr Depth=0
64x64TU : not available
Tr Depth=1
32x32TU : available
<Luma component>
32
32
<chroma component>
Tr Depth=0
32x32TU : available but not used
Tr Depth=1
16x16TU : available

## Slide 3: Proposed Method
We introduce virtual TU always has zero luma CBF to activate unused maximum TU size for chroma blocks
64
64
Tr Depth=0
64x64TU : VIRTUALLY available
Tr Depth=1
32x32TU : available
<Luma component>
32
32
<chroma component>
Tr Depth=0
32x32TU : available and used
Tr Depth=1
16x16TU : available

## Slide 4: Proposed Method
  In case of 2*maxTUsize x 2*maxTUsize, transform_split_flag is coded to indicate the TU is split or virtually
  In case of 2*maxTUsize x 2*maxTUsize, CBF for luma component should be 0

## Slide 5: Experimental Results
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -0.8% | -1.0% | 0.1% | -0.7% | -1.5%
Class B | 0.1% | -0.2% | -0.4% | 0.1% | -0.3% | -0.5%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.1% | -1.4% | -1.8% | 0.2% | -1.8% | -2.2%
Overall | 0.1% | -0.4% | -0.6% | 0.1% | -0.5% | -0.8%
 | 0.1% | -0.4% | -0.6% | 0.1% | -0.5% | -0.8%
Class F | 0.0% | -0.4% | -0.5% | 0.1% | -0.6% | -0.9%
Enc Time[%] | 96% |  |  | 96% |  | 
Dec Time[%] | 100% |  |  | 99% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -1.1% | -1.1% | 0.1% | -1.0% | -0.8%
Class B | 0.1% | -0.8% | -0.6% | 0.1% | -0.7% | -0.8%
Class C | 0.0% | -0.3% | -0.2% | 0.0% | -0.3% | -0.2%
Class D | 0.0% | -0.1% | 0.0% | 0.0% | 0.1% | 0.1%
Class E |  |  |  |  |  | 
Overall | 0.1% | -0.6% | -0.5% | 0.1% | -0.5% | -0.5%
 | 0.0% | -0.6% | -0.5% | 0.1% | -0.5% | -0.4%
Class F | 0.1% | -0.4% | -0.2% | 0.1% | -0.5% | -0.7%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.1% | -0.9% | -1.0% | 0.1% | -1.3% | -1.7%
Class C | 0.0% | -0.6% | -0.6% | 0.0% | -0.4% | -0.6%
Class D | 0.0% | -0.3% | -0.3% | 0.0% | 0.1% | 0.1%
Class E | 0.1% | -1.0% | -2.6% | 0.1% | -2.2% | -1.5%
Overall | 0.1% | -0.7% | -0.9% | 0.1% | -0.9% | -1.0%
 | 0.1% | -0.6% | -0.9% | 0.1% | -0.9% | -1.0%
Class F | 0.1% | -0.4% | -1.2% | 0.1% | -1.7% | -0.4%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
<bd rate in the common condition : maxCU 64x64, maxTU 32x32>

## Slide 6: Experimental Results
<bd rate in the common condition : maxCU 64x64, maxTU 16x16>
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.3% | -2.3% | -3.4% | 0.3% | -1.8% | -2.9%
Class B | 0.5% | -1.9% | -2.4% | 0.5% | -2.0% | -2.6%
Class C | 0.2% | -0.7% | -0.7% | 0.2% | -0.9% | -0.9%
Class D | 0.1% | -0.9% | -0.8% | 0.2% | -1.0% | -0.9%
Class E | 0.3% | -4.8% | -6.5% | 0.3% | -5.0% | -6.4%
Overall | 0.3% | -2.0% | -2.6% | 0.3% | -2.0% | -2.6%
 | 0.3% | -2.0% | -2.6% | 0.3% | -2.0% | -2.6%
Class F | 0.2% | -1.5% | -1.3% | 0.2% | -1.6% | -1.6%
Enc Time[%] | 91% |  |  | 92% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.6% | -3.0% | -2.3% | 0.5% | -2.4% | -2.2%
Class B | 0.4% | -2.7% | -2.4% | 0.4% | -2.7% | -2.6%
Class C | 0.2% | -1.3% | -1.6% | 0.2% | -1.2% | -1.3%
Class D | 0.1% | -0.8% | -0.6% | 0.1% | -0.7% | -0.7%
Class E |  |  |  |  |  | 
Overall | 0.3% | -2.0% | -1.7% | 0.3% | -1.8% | -1.7%
 | 0.4% | -2.0% | -1.7% | 0.3% | -1.8% | -1.7%
Class F | 0.2% | -1.0% | -0.9% | 0.2% | -1.5% | -1.0%
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 101% |  |  | 100% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.5% | -4.5% | -5.0% | 0.5% | -4.7% | -5.1%
Class C | 0.3% | -2.5% | -2.2% | 0.3% | -2.1% | -2.2%
Class D | 0.1% | -1.8% | -1.4% | 0.1% | -1.8% | -1.2%
Class E | 0.4% | -5.9% | -9.5% | 0.4% | -6.6% | -8.0%
Overall | 0.3% | -3.4% | -4.0% | 0.3% | -3.7% | -4.0%
 | 0.3% | -3.3% | -4.0% | 0.3% | -3.6% | -3.9%
Class F | 0.1% | -1.1% | -1.2% | 0.3% | -1.6% | -2.8%
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 101% |  |  | 100% |  | 

## Slide 7: Conclusions
We propose to use virtually large TU exceeds maximum TU size with zero luma CBF to enable maximum size of chroma transform
The proposed method introduces small change in the Text and the S/W