## Slide 1: JCTVC-I0151: LM mode with Uniform Bit-width Multipliers
Lingzhi Liu
Yongbing Lin
Guichun Li

## Slide 2: Proposed
Propose to unify the bit-widths of the multipliers used in LM mode in HEVC standard..
This is a continuous work of JCTVC-H0491 “Remove the large multiplier for LM mode calculation”.
  Large multipliers (13/15-bit) in a1, a2 and beta calculation have been replaced by (8/10-bit) multipliers in H0491
  Large multiplier in a3 calculation is replaced by (8/10-bit) multiplier in this contribution

## Slide 3: a1, a2 and b in LM mode
Parameters:
a1 = ( LC << k2 ) – L*C a2 = ( LL << k2 ) – L*L
b = ( C – ( ( alpha * L ) >> k1 ) + ( 1 << ( k2 – 1 ) ) ) >> k2
13-b by 13-b (IBD=8)
15-b by 15-b
(IBD=10)
8-b (IBD=8)
10-b
(IBD=10)
13/15-b

## Slide 4: Unify the Large Multiplier for a1, a2 and “b” calculations
b = avgC – ( ( alpha * avgY’ ) >> k1 )
a1 = LC– (2*nS*avgY’*avgC+avgY’*RErrC+avgC*RErrY’) a2 = LL – (2*nS*avgY’2+2*avgY’*RErrY’)
where avgY’, RErrY’, avgC, and RErrC are defined as:
8-b (IBD=8)
10-b (IBD=10)
8x5-b (IBD=8)
10x5-b (IBD=10)

## Slide 5: Another encoder implementation for a1 and a2 calculation (JCTVC-H0491)
Where
8-b singed (IBD=8)
10-b (IBD=10)
No multiplification

## Slide 6: New calculation of LC and LL
beta = avgC – ( ( alpha * avgY’ ) >> k1 )
8-b singed (IBD=8)
10-b (IBD=10)
8-b

## Slide 7: Unify the Multiplier in a3
a1s is restrained in the range of ((-2BitDepthC -1, 2BitDepthC-1-1)
output value of lmDiv is restrained in the range of ((0, 2BitDepthC-1)
a3= a2s < 1 ? 0 : Clip3( −215, 215−1, a1s*lmDiv >> k1 )
15-b by 15-b
if (a1==0), k2=0
otherwise, k2= Max( 0, Floor(log2(abs(a1))) – BitDepthC + 2 )
a1s = a1 >> k2
lmDiv = a2s < 1 ? 0 : ( ( lmDiv + ( 1 << ( 15 - BitDepthC- 1 ) ) ) >> (15 - BitDepthC) ) )
lmDiv = Clip1C (lmDiv)

## Slide 8: Simulation results
 | All Intra HE |  | 
 | Y | U | V
Class A | 0.0% | 0.1% | 0.2%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.1%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.1%
 | 0.0% | 0.0% | 0.1%
Class F | 0.0% | 0.2% | 0.4%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Testing results of proposed algorithm in Section 3 vs. HM 6.0 AI_HE10

## Slide 9
Thank You