## Slide 1: AHG 4: Picture Raster Scan Decoding in the presence of multiple tiles JCTVC-I0158
Gordon Clare, Félix Henry, Stéphane Pateux – ORANGE LABS
Notes: presentation title
<number>

## Slide 2: Problem statement
Multiple tiles introduce delay & buffering when doing single core decoding (problem already identified in JCTVC-H0463 [1])
  [1] W. Wan, T. Hellman, “Comments on specifying tile support in HEVC Profiles and Levels”, JCTVC-H0463, San Jose, February 2012.
tile 1
tile 2
tile 3
tile 4
JCTVC-I0158
Notes: presentation title
<number>

## Slide 3: Existing approach to handle delay and buffering issues
In order to reduce delay and buffering, the decoder needs to decode LCUs in picture raster scan order
Bitstream jumping + pointer store + cabac state store/restore
Bitstream jumping + cabac state restore
…
…
JCTVC-I0158
Notes: presentation title
<number>

## Slide 4: Summary of decoder requirements for single core raster scan decoding of multiple tiles
Additional processing steps compared to single tile decoding, required at the end of each LCU row in a tile
  Bit-level bitstream pointer storage
  Bit-level bitstream pointer restore
  Cabac state (codIRange & codIOffset) storage
  Cabac state (codIRange & codIOffset) restore
  Bitstream jump
Not all operations are needed in corner cases (eg. end of tile)
Example 1080p Main Profile, worst case happens with 5 tile columns and LCU width of 8
  Each of the above processing steps is performed about 675 times per frame
    5*(1080/8)=675
JCTVC-I0158
Notes: presentation title
<number>

## Slide 5: Summary of decoder requirements for single core raster scan decoding of multiple tiles
Additional buffers
  1 bit level bitsream pointer per tile column (at least 4 bytes)
  1 Cabac state buffer for each tile column (4 bytes)
Example worst case for 1080p Main Profile (5 tile columns)
  40 bytes
    (4+4)*5=40
Example worst case for 1080p outside Main Profile (tile width = 1 LCU with LCU width of 8)
  960 bytes
    (4+4)*1920/8=960
JCTVC-I0158
Notes: presentation title
<number>

## Slide 6: Proposal
Bit level Cabac flush at the end of each LCU row in a tile
  Except last row in a tile were flush and byte alignment is already performed
JCTVC-I0158
Notes: presentation title
<number>

## Slide 7: Impact of Proposal
Additional processing steps compared to single tile decoding, required at the end of each LCU row in a tile
  Bit-level bitstream pointer storage
  Bit-level bitstream pointer restore
  Cabac state (codIRange & codIOffset) storage
  Cabac state (codIRange & codIOffset) restore
  Bitstream jump
Additional buffers
  1 bit level bitstream pointer per tile column (at least 4 bytes)
  1 Cabac state buffer for each tile column (4 bytes)
JCTVC-I0158
Notes: presentation title
<number>

## Slide 8: Performance
JCTVC-H1100 test conditions with tile size of class D (as per JCTVC-F335)
  Anchor is HM6.1
  Measure is the proposal (additional Cabac Flush)
Impact is 0.1% (I), 0.6% (RA), 1.5% (LDB)
JCTVC-I0158
Notes: presentation title
<number>

## Slide 9: Conclusion
Picture raster scan single core decoding is needed in the presence of multiple tiles in order to avoid delay and buffering
Proposed modification allows the removal of processing steps and associated buffers
Suggested to adopt this modification in the standard
Text is provided
We thank Qualcomm for crosschecking this proposal
  Crosscheck JCTVC-I0387
JCTVC-I0158