## Slide 1: AHG 4: Proposals on entry points signalling JCTVC-I0159
Gordon Clare, Félix Henry, Stéphane Pateux – ORANGE LABS
Notes: presentation title
<number>

## Slide 2: Problem statement
This contribution proposes modifications of entry points signalling in order to solve the following issues
  Unnecessary TileID index written with an entry point marker when WPP is used
  Low delay encoding when offset entry points are used
  Necessary tile entry points in order to enable picture raster scan decoding of multiple tiles
JCTVC-I0159
Notes: presentation title
<number>

## Slide 3: 1. TileID cleaning
Problem statement
  Currently, when a marker is used to signal the start of a substream, a TileID is also written.
  However this syntax element has no use when tiles_or_entropy_coding_sync_idc is equal to 2 (WPP).
Proposed solution
  It is proposed to write this syntax element only when tiles_or_entropy_coding_sync_idc is equal to 1.
JCTVC-I0159
Notes: presentation title
<number>

## Slide 4: 2. Encoder delay when using offset entry points
Problem statement
  Entry point offsets are written in the Slice Header
  This can be done only when substream/tile sizes are known
  This introduces encoder delay (both for single core and multiple core operations)
  Delay can be solved by using markers
    But RD performance is affected
Proposed solution
  Writing offsets at the beginning of each substream/tile
    Slice header can be built before processing the tiles/substream
    substreams/tiles can be written when ready
JCTVC-I0159
Notes: presentation title
<number>

## Slide 5: 2. Encoder delay when using offset entry points
Byte aligning the offsets
  Since the substream is generated before its offset, but the offset is written before the substream, this implies that a bit-aligned offset would require bit shifting of the whole substream.
  Byte aligning the offset allows a simple byte level concatenation with the substream/tile
JCTVC-I0159
Notes: presentation title
<number>

## Slide 6: 3. Mandatory offsets for Tiles
Problem statement
  Picture raster scan decoding of LCUs in tile-divided frames has been identified as a needed feature to avoid decoder delay/buffering.
    Requires bitstream jumping (as described JCTVC-H0463 and JCTVC-I0158) See next slide
  Bitstream jumping requires that each tile can be individually accessed in the bitstream.
  This is not possible if some tiles do not have entry points.
Proposed solution
  It is proposed that one entry point offset per tile is made mandatory.
JCTVC-I0159
Notes: presentation title
<number>

## Slide 7: 3. Mandatory offsets for Tiles
JCTVC-I0159
Bitstream jumping + pointer store + cabac state store/restore
Bitstream jumping + cabac state restore
…
…

## Slide 8: Performance using WPP
JCTVC-H1100 test conditions using HM.6.1
  with WPP activated
  one WPP substream per LCU row
Negligible impact
  0.0%(I), 0.0%(RA), 0.1% (LDB)
JCTVC-I0159
Notes: presentation title
<number>

## Slide 9: Performance using tiles
JCTVC-H1100 test conditions using HM.6.1
  with tiles activated
  tiles of size class D (as per JCTVC-F335)
Negligible impact
  0.0%(I), 0.0%(RA), 0.0% (LDB)
JCTVC-I0159
Notes: presentation title
<number>

## Slide 10: Conclusion
The proposed modifications of entry points provides the following functionalites
  Cleaning of TileID
  Low delay encoding when offset entry points are used
  Enables picture raster scan decoding of multiple tiles
Proposed modification is harmonious for WPP and tiles
Proposed modification has negligible impact on R/D performance
It is suggested that the proposed modifications are adopted in the standard
Text is provided
We thank LGE for crosschecking this proposal
  Crosscheck JCTVC-I0267
JCTVC-I0159

## Slide 11: Update
Source code/text of the proposal
  Last tile/substream has no offset
  However this creates a potential problem because the decoder cannot identify the last substream/tile in a slice
Even the last substream/tile in a slice should have an offset
  Problem is solved
  Regular design
JCTVC-E196