## Slide 1: On Signaling of Several Syntax Elements in Slice Header
JCTVC-I0165
Presented by Xun Guo
9th Meeting in Geneva, CH
Apr.27-May 7, 2012
Jicheng An, Xun Guo, Chih-Wei Hsu, Yu-Wen Huang and Shawmin Lei
MediaTek Inc.

## Slide 2: Summary
Some changes are proposed to be added on top of aps_id and inherit_dbl_params_from_aps_flag
aps_id
  The conditions are revised by considering some related syntax elements to save some bits
inherit_dbl_params_from_aps_flag
  One constrain is proposed to be added in the sematics

## Slide 3: APS ID in Slice Header
aps_id
Some other related syntax elements should also be considered
if( scaling_list_enable_flag ¦ ¦ deblocking_filter_in_aps_enabled_flag ¦ ¦ ( sample_adaptive_offset_enabled_flag && !slice_sao_interleaving_flag ) ¦ ¦ adaptive_loop_filter_enabled_flag ) | 
aps_id | ue(v)

## Slide 4: Proposed Changes
deblocking_filter_control_present_flag (PPS)
  If 0, inferred deblocking parameters are used rather than APS
slice_sample_adaptive_offset_flag (Slice header)
  If 0, SAO is off for current slice
alf_coef_in_slice_flag (SPS)
  If 0, ALF coefficients in slice header are used rather than APS
if( scaling_list_enable_flag ¦ ¦ (deblocking_filter_in_aps_enabled_flag && deblocking_filter_control_present_flag) ¦ ¦ ( sample_adaptive_offset_enabled_flag &&! slice_sao_interleaving_flag && slice_sample_adaptive_offset_flag) ¦ ¦ (adaptive_loop_filter_enabled_flag && !alf_coef_in_slice_flag ) ) | 
aps_id | ue(v)

## Slide 5: Deblocking Inherit Flag
inherit_dbl_params_from_aps_flag
  Indicate if the deblocking parameters from APS shall be used for the current slice
aps_deblocking_filter_flag
  Indicate if the deblocking parameters are present in APS
Contradictory case
  aps_deblocking_filter_flag = 0
  inherit_dbl_params_from_aps_flag = 1
Solution – adding constrain
  It is a requirement of the bitstream that if there is an active APS and the value of aps_deblocking_filter_flag is 0, then the value of inherit_dbl_from_aps_params_flag shall be 0.

## Slide 6
Thank you!