## Slide 1: Simplified Parameter Calculation for Chroma LM Mode
JCTVC-I0166
Presented by Xun Guo
9th Meeting in Geneva, CH
Apr.27-May 7, 2012
Juliana Hsu, Mei Guo, Xun Guo, and Shawmin Lei
MediaTek Inc.

## Slide 2: Summary
Reduced the complexity of the parameter derivation for chroma LM mode
  Reduced the bit of the multiplier from 16 to the internal bit depth
  Reduced the entries of an online generated look-up table from 63 to 32, and from 16 bit to 10 bit
    Saved 70% of the storage memory
Experimental Results
  Almost no BD-rate and running time changes

## Slide 3: Derivation of parameters
a1s: dynamic range of 16-bit
lmDiv: 16-bit unsigned integer
  on-line generated look-up table with input a2s
  entries in look-up table: 1~64
  lmDiv(a2s) = ( (1 << 15) + a2s/2 ) / a2s
k1 = Max( 0, Log2( abs( a2 ) ) − 5 ) - Max( 0, Log2( abs( a1 ) ) − 14 ) + 2
a1s = a1 >> Max(0, Log2( abs( a1 ) ) − 14 )
a2s = abs( a2 >> Max(0, Log2( abs( a2 ) ) − 5 ) )
a3 = a2s < 1 ? 0 : Clip3( −215, 215−1, a1s*lmDiv + ( 1 << ( k1 − 1 ) ) >> k1 )
a = a3 >> Max( 0, Log2( abs( a3 ) ) − 6 )
k = 13 – Max( 0, Log2( abs( a ) ) − 6 )
b = ( L – ( ( a*C ) >> k1 ) + ( 1 << ( k2 − 1 ) ) ) >> k2

## Slide 4: Proposed Method 1
Make the bit depth of a1s and lmDiv identical to IBD (internal bit depth)
  a1s= a1 >> Max(0, Log2( abs( a1 ) ) − (IBD-2))
  lmDiv(a2s)=( (1 << (IBD-1) ) + a2s/2 ) / a2s
a2s | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lmDiv | 512 | 256 | 171 | 128 | 102 | 85 | 73 | 64 | 57 | 51 | 47 | 43 | 39 | 37 | 34 | 32
a2s | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
lmDiv | 30 | 28 | 27 | 26 | 24 | 23 | 22 | 21 | 20 | 20 | 19 | 18 | 18 | 17 | 17 | 16
a2s | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
lmDiv | 16 | 15 | 15 | 14 | 14 | 13 | 13 | 13 | 12 | 12 | 12 | 12 | 11 | 11 | 11 | 11
a2s | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 
lmDiv | 10 | 10 | 10 | 10 | 10 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 8 | 8 | 8 | 

## Slide 5: Proposed Method 2
Reduce the entries of look-up table from 63 to 32
  Most of a2s is not less than 32
  if a2s < 32, lmDiv = 0;
  otherwise,
lmDiv(a2s)=( (1 << (IBD+4)) + a2s/2 ) / a2s
a2s | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47
lmDiv | 512 | 496 | 482 | 468 | 455 | 443 | 431 | 420 | 410 | 400 | 390 | 381 | 372 | 364 | 356 | 349
a2s | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63
lmDiv | 341 | 334 | 328 | 321 | 315 | 309 | 303 | 298 | 293 | 287 | 282 | 278 | 273 | 269 | 264 | 260

## Slide 6: Experimental Results
Anchor – HM6.0
Test conditions – JCTVC-H1100
Thank Intel for cross verifying our results (JCTVC-I0322).
63 Entries | All Intra HE10 |  | 
 | Y | U | V
Class A | 0.00% | -0.42% | -0.45%
Class B | 0.00% | -0.01% | -0.02%
Class C | 0.00% | -0.01% | 0.05%
Class D | 0.00% | -0.02% | 0.04%
Class E | 0.00% | -0.05% | 0.05%
Overall | 0.00% | -0.10% | -0.07%
 | 0.00% | -0.09% | -0.07%
Class F | 0.00% | -0.02% | 0.00%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
32 Entries | All Intra HE10 |  | 
 | Y | U | V
Class A | 0.00% | -0.06% | 0.00%
Class B | 0.00% | -0.05% | -0.02%
Class C | 0.00% | 0.02% | 0.00%
Class D | 0.00% | -0.02% | 0.04%
Class E | 0.00% | 0.02% | 0.02%
Overall | 0.00% | -0.02% | 0.01%
 | 0.00% | -0.02% | 0.00%
Class F | 0.00% | -0.06% | 0.00%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 

## Slide 7: Conclusions
Two simplifications are proposed
Multiplier in parameter derivation of chroma LM mode is limited to internal bit depth
A lookup table is simplified
Propose to be adopted

## Slide 8
Thank you!