## Slide 1: CE2: Line memory reduction fix at tile boundaries
Semih Esenlik
Ann-Kathrin Seifert
Matthias Narroschke
Thomas Wedi
Panasonic Corporation
9th JCT-VC meeting, Geneva 27 April-07 May 2012

## Slide 2: Summary
Problem:
Application of double padding at tile boundaries when loop_filter_across_tiles_enabled_flag is set to 0.
Proposal:
Virtual boundary padding is skipped at tile boundaries when loop_filter_across_tiles_enabled_flag is set to 0.

## Slide 3
Loop filtering accross tile boundaries
Loop filters across the tile boundaries are controlled with the following flag in SPS:
  loop_filter_across_tiles_enabled_flag
If loop_filter_across_tiles_enabled_flag is 0, loop filters do not cross tile boundaries.
There is no line memory at horizontal tile boundaries in this case.

## Slide 4
Line memory at tile boundaries
Example (loop_filter_across_tiles_enabled_flag is equal to 0):
  During the processing of LCU 8 with ALF, pixels from LCU 14 are not required.
  During the processing of LCU 14 with ALF, pixels from LCU 8 are not required.
If loop_filter_across_tiles_enabled_flag is 0; no line memory required for ALF along tile boundaries.
Tile2
Tile4
Tile1
Tile3
LCU 8
LCU 14

## Slide 5
Problem
Problem related to virtual boundary padding of ALF:
Double padding occurs at independent tile boundaries.
Virtual Boundary padding is applied on top of boundary padding although it is not actually required.

## Slide 6
Proposal
The following simple rule is included in Virtual Boundary padding operation of ALF:
“If loop_filter_across_tiles_enabled_flag is 0, then Virtual Boundary padding is not applied at horizontal tile boundaries.”
*Remark: Virtual Boundary padding is currently not applied at frame boundaries already.

## Slide 7: Simulation results Test 1
Loop_filters_across_tiles_enabled_flag is set to 0.
8 tiles per frame for class D, 16 tiles per frame for class other sequences.

## Slide 8: Simulation results Test 2
Only ALF is not allowed to cross the tile boundaries.
8 tiles per frame for class D, 16 tiles per frame for class other sequences.

## Slide 9
Jonny, LD_HE_P, QP37, frame no. 218
Loop_filters_across_tiles_flag is set to 0
HM6.0
Proposal

## Slide 10
Jonny, LD_HE_B, QP37, frame no. 153
Loop_filters_across_tiles_flag is set to 0
HM6.0
Proposal

## Slide 11
KristenAndSara, LD_HE_P, QP32, frame no. 372
Loop_filters_across_tiles_flag is set to 0
HM6.0
Proposal

## Slide 12
KristenAndSara, LD_HE_P, QP32, frame no. 435
HM6.0
Proposal
Only ALF is switched off across tile boundaries
Proposal

## Slide 13: Conclusion
Problem:
Application of double padding at tile boundaries when loop_filter_across_tiles_enabled_flag is set to 0.
Proposal:
Virtual boundary padding is skipped at tile boundaries when loop_filter_across_tiles_enabled_flag is set to 0.
Benefits:
  Coding gain of 0.1% for luma and 0.2% for chroma.
  Improvement in the subjective quality.