## Slide 1: Non-CE2: Grid displacements for ALF
Semih Esenlik
Matthias Narroschke
Thomas Wedi
Panasonic Corporation
9th JCT-VC meeting, Geneva, 27.April – 7.May 2012

## Slide 2: Summary
Proposal:
Shift ALF filter grid 4 pixels up.
Benefits:
Elimination of coefficient line buffer (3.6kBytes reduction in memory) in the case of LCU-based ALF syntax.

## Slide 3
LCU-based processing of ALF
Line memory
ALF application window in LCU-based filtering
LCU
In the Encoder
A different ALF filter is designed for each LCU.
In the Decoder
ALF is applied on the red region (ALF application window) due to delayed deblocking filtering.
9 lines
4 lines
Line memory
Line memory

## Slide 4
LCU-based processing of ALF
ALF application window intersects 4 different LCUs.
Problem in the Decoder:
Filter coefficient line memory: The filter coefficients for the whole LCU row need to be stored in the line memory (~3.6kBytes)(max # of LCUs per picture width * 3 color component * 10 Bytes).
9 lines

## Slide 5
Proposed solution: Grid displacement for ALF
ALF design grid
Shift 4 pixels up
LCU
Line memory
ALF filter grid is shifted 4 pixels up.
Filter coefficients from upper LCU row are not required to be buffered.

## Slide 6
Proposed solution: Grid displacement for ALF
LCU boundary
ALF Grid
LCU boundary
ALF Grid
LCU boundary
ALF Grid
Resulting ALF filter Grid

## Slide 7: Experimental results
Average change in bitrate < 0.01%

## Slide 8: Conclusion
Proposal
Shift ALF filter grid 4 pixels up.
Benefits
Elimination of coefficient line buffer (3.6kBytes reduction in memory) in the case of LCU-based ALF syntax.
Proposal:
Adopt into the next version of HM.