## Slide 1
<number>
Table size reduction and CABAC context reduction for last significant position coding---JCTVC-I0177
Feng Zou, Oscar C. Au, Jingjing Dai, Xingyu Zhang, Chao Pang
HKUST

## Slide 2: JCTVC I0177 Outline
<number>
Context modeling for last significant coefficient position coding
Problems within the current scheme
  Table with redundant entries
  Similar context states for several bins
Proposed solution
  Scheme 1: Table size reduction
  Scheme 2: Reduce CABAC contexts by allowing several bins to share the same contexts
Simulation Results
Notes: <number>

## Slide 3: JCTVC I0177 Related techniques
<number>
In HM6.0, last significant (none zero) coefficient position coding, comprises horizontal position x and vertical position y.
The last significant coefficient position is represented by a binary string which consists of two parts. The first part is truncated unary code where each bin is encoded with CABAC contexts, while the second part is fixed binary code with by-pass coding (no context).
Notes: <number>

## Slide 4: JCTVC I0177 Related Technique
<number>
Table 1. Last position coding for TU 4x4 Luma
Table 2. Last position coding for TU 8x8 Luma
Notes: <number>

## Slide 5: JCTVC I0177 Related Technique
<number>
Table 3. Last position coding for TU 16x16 Luma
Table 4. Last position coding for TU 32x32 Luma
Notes: <number>

## Slide 6: JCTVC I0177 Related Technique
<number>
Table 5. The context assignment for each bin in the truncated unary codeword for Luma.
Table 6. 1D table to store the CABAC context index for each bin of different TU sizes in HM6.0. (Note that the entries with red label are redundant.)
Notes: <number>

## Slide 7: JCTVC I0177 Proposed Technique
<number>
Scheme 1: Table Size reduction (Reduce the 1D table size from 28 to 24.)
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lastCtx[ i ] | 0 | 1 | 2 | 3 | 4 | 5 | 5 | 2 | 6 | 7 | 8 | 8 | 9 | 9
i | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 |  |  |  | 
lastCtx[ i ] | 2 | 10 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 2 |  |  |  | 
No RD performance change.
Notes: <number>

## Slide 8: JCTVC I0177 Proposed Technique
<number>
Scheme 2: CABAC context reduction
Similar statistics for several bins for TU32x32, and therefore, several bins share the same CABAC contexts (Reducing the CABAC context from 15 to 12 for each direction x /y).
Bin index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
TU 4x4 | 0 | 1 | 2 |  |  |  |  |  | 
TU 8x8 | 3 | 4 | 5 | 5 | 2 |  |  |  | 
TU 16x16 | 6 | 7 | 8 | 8 | 9 | 9 | 2 |  | 
TU 32x32 | 10 | 10 | 10 | 10 | 11 | 11 | 11 | 11 | 2
Table 7. The CABAC context index for each bin of different TU sizes(Total contexts 12 for each direction x/y)
Notes: <number>

## Slide 9: JCTVC-I0177 Test Condition and Results
Test Condition and Results
The anchor is HM6.0 with encoding conditions specified in the common test conditions in JCTVC-H1100.
The results are verified at the decoder and cross checked by Inter-Digital in JCTVC-I0423.
Simulation results show that there is 0.01%, 0.02%, 0.03%, 0.05%, 0.01% and 0.05% Y-BD rate change for Intra Main, Intra HE10bit, RA Main, RA HE10bit, LD-B Main and LD-B HE10bit respectively under the common test condition

## Slide 10: JCTVC-I0177 Test Condition and Results
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.07% | 0.07% | 0.02% | 0.07% | 0.00% | 0.06%
Class B | 0.01% | 0.01% | 0.00% | 0.01% | -0.01% | -0.03%
Class C | 0.00% | -0.02% | 0.02% | 0.00% | 0.00% | 0.07%
Class D | 0.00% | 0.01% | -0.01% | 0.02% | -0.03% | -0.02%
Class E | 0.00% | -0.02% | 0.00% | 0.03% | -0.05% | 0.03%
Class F | -0.01% | 0.09% | 0.00% | 0.02% | 0.03% | 0.00%
Overall | 0.01% | 0.03% | 0.00% | 0.02% | -0.01% | 0.02%
 | 0.01% | 0.02% | 0.00% | 0.02% | 0.00% | 0.02%
Enc Time[%] | 100% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 99% |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.20% | 0.13% | 0.14% | 0.11% | 0.08% | 0.18%
Class B | 0.03% | -0.05% | 0.12% | 0.03% | -0.09% | -0.11%
Class C | -0.02% | 0.00% | -0.05% | 0.02% | 0.00% | -0.13%
Class D | -0.02% | -0.10% | -0.19% | 0.02% | -0.12% | 0.02%
Class E |  |  |  |  |  | 
Class F | -0.03% | 0.02% | -0.09% | 0.05% | -0.08% | 0.04%
Overall | 0.03% | 0.00% | -0.01% | 0.05% | -0.04% | -0.01%
 | 0.03% | -0.02% | -0.01% | 0.04% | -0.01% | -0.01%
Enc Time[%] | 99% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.07% | -0.35% | -0.09% | 0.06% | -0.18% | 0.01%
Class C | 0.06% | 0.18% | 0.10% | 0.02% | 0.04% | -0.09%
Class D | 0.06% | -0.30% | 0.19% | 0.04% | -0.19% | -0.05%
Class E | -0.02% | -0.13% | 0.52% | 0.05% | 0.07% | 0.33%
Class F | -0.15% | 0.06% | 0.26% | 0.10% | -0.94% | 2.22%
Overall | 0.01% | -0.12% | 0.17% | 0.05% | -0.25% | 0.47%
 | 0.01% | -0.08% | 0.20% | 0.05% | -0.26% | 0.48%
Enc Time[%] | 95% |  |  | 94% |  | 
Dec Time[%] | 96% |  |  | 94% |  | 

## Slide 11: JCTVC-I0177 Conclusion
Reduce the table size for significant coefficient position coding (28 24, 14.2%)
Reduce the CABAC contexts for significant coefficient position coding (1512, 20%) with no significant RD loss
Recommend to adopt them into the HEVC standard