## Slide 1
Changes to the Hash SEI calculation for improved usability
(JCTVC-I0218)
Tim Hellman and Wade Wan
Broadcom Corporation

## Slide 2: Problem Statement
WD Presently Defines 2 Hash functions
  MD5: Excellent error detection, More complicated calculation
  CRC: Simpler calculation, less robust detection
  These are very valuable for testing and conformance
Both hashes are order-dependent
  Pixels must be processed in the defined order
Problem: Both process Y/U/V in sequential raster order
  3 passes over memory to compute!
JCTVC-I0218

## Slide 3: How are Hashes used in Real Systems?
1: Decoder computes at video feeder stage
JCTVC-I0218
2: Encoder/Decoder Compute At Decode Output
  Order-independence is valuable here

## Slide 4: Solution Part 1: Break MD5 into 2 hashes
Generate Separate Y and UV Hashes
  Can do UV together, because sub-sampling is the same
Decoder can now compute this at display time
JCTVC-I0218

## Slide 5: Solution Part 2: Replace CRC with Checksum
32-bit Checksum
  Completely order-independent
  Can be easily generated by real-time encoder
  XOR in position to make ‘swap errors’ more detectable
  Compute separately for Y/UV (consistent with part 1)
Generic Calculation Example
  xor_mask = (x & 0xFF) ^ (y & 0xFF) ^ (x >> 8) ^ (y >> 8)
  Checksum += component[ x ][ y ] ^ xor_mask
JCTVC-I0218