## Slide 1
Changing cu_qp_delta parsing to enable
CU-level processing
(JCTVC-I0219)
Tim Hellman and Wade Wan
Broadcom Corporation

## Slide 2: Problem: Delta QP prevents CU-level pipeline
CU Quantization Group
  QP applies to one or more CUs in a square area
  At most one cu_qp_delta per quantization group
Problem: Where is cu_qp_delta inserted?
  In the first CU with non-zero coefficients
  Can have up to 63 CUs waiting for QP!
JCTVC-I0218

## Slide 3: Why is this a problem?
Deblocker needs QP
  Used to compute filter strength
Decoder must wait before starting deblocking
  Forces LCU-level pipeline
  This is the only syntax element that can affect a previous CU!
JCTVC-I0218

## Slide 4: Solution #2 – Change definition of QP group
Only apply cu_qp_delta after it’s received.
  Earlier CUs use predicted QP
No change to delta QP syntax
JCTVC-I0218

## Slide 5: Solution #2 – QP Prediction
QP Prediction method unchanged
Neighboring CU QP used, rather than Pred Group QP
JCTVC-I0218

## Slide 6: Conclusion
Adopt some change to fix this problem
JCTVC-I0218

## Slide 7: 2 Possible Solutions
Solution 1: Move cu_delta_qp to the first CU in the group
Insert if:
  CU size is less than QP group size OR
  CU has coefficients.
Delta QP checked in two places
  Start of prediction unit
  Start of transform tree
JCTVC-I0218

## Slide 8: Syntax Change
JCTVC-I0218

## Slide 9: Results: QP Group Size = 16x16
JCTVC-I0218
 | Random Access Main |  |  | Random Access HE10 |  |  | 
 | Y | U | V | Y | U | V | 
Class A | 0.4% | 0.5% | 0.3% | 0.2% | 0.4% | 0.0% | 
Class B | 0.3% | 0.2% | 0.2% | 0.3% | 0.5% | 0.1% | 
Class C | 0.3% | 0.3% | 0.3% | 0.2% | 0.1% | 0.2% | 
Class D | 0.3% | 0.0% | 0.3% | 0.2% | -0.1% | 0.1% | 
Class E |  |  |  |  |  |  | 
Overall | 0.3% | 0.2% | 0.3% | 0.2% | 0.2% | 0.1% | 
 | Low delay B Main |  |  | Low delay B HE10 |  |  | 
 | Y | U | V | Y | U | V | 
Class A |  |  |  |  |  |  | 
Class B | 0.4% | 0.2% | 0.4% | 0.3% | 0.2% | 0.4% | 
Class C | 0.4% | 0.3% | 0.5% | 0.2% | 0.2% | 0.3% | 
Class D | 0.3% | 0.1% | -0.2% | 0.4% | 0.2% | 0.6% | 
Class E | 0.5% | -0.4% | 0.3% | 0.1% | 0.0% | 1.5% | 
Overall | 0.4% | 0.1% | 0.2% | 0.3% | 0.2% | 0.6% |