## Slide 1: Results for Non-Square Intra Prediction with NSQT
Copyright © MediaTek Inc. All rights reserved.
Ximin Zhang, Shan Liu and Shawmin Lei
Presented by Shan Liu
9th JCT Meeting in San Jose
27 April – 7 May, 2012
JCTVC-I0224

## Slide 2: Introduction
Motivation
  Non-square prediction partitions and transforms bring coding gains to Inter prediction and are already included in HM.
  Non-square Intra prediction partitions using NSQT reported coding gains for both Intra and Inter configurations
    JCTVC-H0437 (AhG16)

## Slide 3: Introduction
Prediction partition modes in proposed main profile (current HM)
  INTRA
  INTER
2Nx2N
2Nx2N
Nx2N
2NxN
SCU
nLx2N
2NxnD
2NxnU
nRx2N
Asymmetric
NxN
NxN

## Slide 4: HM + Proposed Intra Prediction Partitions
Prediction partition modes in the proposed scheme
  INTRA
  INTER
Asymmetric
2Nx2N
2Nx2N
Nx2N
2NxN
SCU
nLx2N
2NxnD
2NxnU
nRx2N
NxN
NxN
Nx2N
2NxN

## Slide 5: Partition Mode Binarization
PredMode | Value of part_mode | PartMode | Bin string |  | 
 |  |  | cLog2CUSize > Log2MinCUSize | cLog2CUSize = = Log2MinCUSize | 
 |  |  |  | cLog2CUSize = = 3 && !inter_4x4_enabled_flag | cLog2CUSize > 3 ¦ ¦ inter_4x4_enabled_flag
MODE_INTRA | 0 | PART_2Nx2N | 1 | 1 | 1
 | 1 | PART_2NxN | 01 | 001 | 001
 | 2 | PART_Nx2N | 00 | 000 | 000
 | 3 | PART_NxN | - | 01 | 01
PredMode | Value of part_mode | PartMode | Bin string |  | 
 |  |  | cLog2CUSize > Log2MinCUSize | cLog2CUSize = = Log2MinCUSize | 
 |  |  |  | cLog2CUSize = = 3 && !inter_4x4_enabled_flag | cLog2CUSize > 3 ¦ ¦ inter_4x4_enabled_flag
MODE_INTRA | 0 | PART_2Nx2N | - | 1 | 1
 | 1 | PART_NxN | - | 0 | 0
MODE_INTER | 0 | PART_2Nx2N | 1 | 1 | 1
 | 1 | PART_2NxN | 011 | 01 | 01
 | 2 | PART_Nx2N | 001 | 00 | 001
 | 3 | PART_NxN | - | - | 000
 | 4 | PART_2NxnU | 0100 | - | -
 | 5 | PART_2NxnD | 0101 | - | -
 | 6 | PART_nLx2N | 0000 | - | -
 | 7 | PART_nRx2N | 0001 | - | -

## Slide 6: Prediction Modes and Transforms
35 Intra prediction modes used in current HM are applied to non-square partition.
  32x16, 16x32, 16x8, 8x16, 8x4 and 4x8.
Non-square transforms used in current HM (i.e. NSQT) are applied to non-square Intra prediction units.
PU | TU
32x16 | 32x8
16x32 | 8x32
16x8 | 16x4
8x16 | 4x16
8x4 | 4x4
4x8 | 4x4
2Nx2N
Intra 2Nx2N CU
2NxN PU
2Nx0.5N TU
TU1
TU2
TU3
TU0
PU0
PU1
Nx2N PU
0.5Nx2N TU
TU1
TU2
TU3
TU0
PU0
PU1

## Slide 7: Encoder Optimization
Early skip checking Cost(non-square) depending on Cost(2Nx2N)
CU > SCU (8th JCT-VC meeting AhG16 encoder optimization)
SCU (8x4 and 4x8 PU)
HAD
Quant and entropy coding
11 modes
2 best modes
Selected mode
Most probable modes
Best 2Nx2N modes
Selected mode
MPM0, MPM1
2 NxN modes
Planar mode
Quant and entropy coding

## Slide 8: Results
HM6 anchor
HE10 configurations
Thanks to MERL (JCTVC-I0418) and Intel (JCTVC-I0323) for cross verification.
 | All Intra HE10 |  |  | Random Access HE10 |  |  | Low Delay B HE10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | -0.9% | -2.5% | -2.7% | -0.6% | -1.1% | -2.0% |  |  | 
Class B | -1.3% | -3.0% | -3.3% | -0.7% | -1.5% | -1.6% | -0.2% | -1.0% | -0.4%
Class C | -1.3% | -2.5% | -2.8% | -0.6% | -1.4% | -1.6% | -0.3% | -0.5% | -0.7%
Class D | -1.2% | -1.9% | -1.8% | -0.5% | -0.8% | -0.8% | -0.2% | -1.1% | -0.2%
Class E | -2.0% | -3.5% | -4.4% |  |  |  | -0.4% | -1.1% | -1.7%
Overall | -1.3% | -2.7% | -3.0% | -0.6% | -1.2% | -1.5% | -0.3% | -0.9% | -0.6%
 | -1.3% | -2.7% | -3.0% | -0.6% | -1.2% | -1.5% | -0.3% | -0.8% | -0.6%
Class F | -1.3% | -1.6% | -1.4% | -0.9% | -1.2% | -1.1% | -0.5% | -1.0% | 0.8%
Enc Time[%] | 130.8% |  |  | 103.9% |  |  | 103.4% |  | 
Dec Time[%] | 100.9% |  |  | 100.4% |  |  | 100.3% |  | 

## Slide 9: Results – additional encoder optimization
If Cost(NxN) < Cost(2Nx2N), check Cost(non-square).
Reduce 11 modes to 4 modes for HAD.
Thanks to MERL (JCTVC-I0418) and Intel (JCTVC-I0323) for cross verification.
 | All Intra HE10 |  | 
 | Y | U | V
Class A (8bit) | -0.7% | -2.4% | -2.5%
Class B | -1.1% | -3.0% | -3.3%
Class C | -1.0% | -2.4% | -2.6%
Class D | -0.9% | -1.8% | -1.8%
Class E | -1.8% | -3.4% | -4.4%
Overall | -1.1% | -2.6% | -2.9%
 | -1.1% | -2.6% | -2.9%
Class F | -1.1% | -1.5% | -1.5%
Enc Time[%] | 122% |  | 
Dec Time[%] | 101% |  | 

## Slide 10: Conclusion
Reported results for non-square Intra prediction using NSQT.
  Coding gains with some encoder complexity increase,
    AI-HE10: 1.3% BD-rate reduction, 31% encoding time increase (or 1.1% BD-rate reduction, 22% encoding time increase);
    RA-HE10: 0.6% BD-rate reduction, 4% encoding time increase;
    LDB-HE10: 0.3% BD-rate reduction, 3% encoding time increase;
  Decoder complexity increase is negligible.
Small amount of change to syntax and semantics text.
Moderate amount of change to decoding process text.
Recommend to adopt the proposed method.

## Slide 11
Copyright © MediaTek Inc. All rights reserved.
www.mediatek.com