## Slide 1: Deblocking of IPCM-coded blocks
Matthias Narroschke, Semih Esenlik, Thomas Wedi, Steffen Kamp
Panasonic Corporation
9th JCT-VC meeting, Geneva, 27. April -07. May 2012

## Slide 2: Outline
Deblocking of PCM blocks in CD
Proposed deblocking of PCM blocks
  Send slice level QP value
  Send block level QP values
Experiments and results
Conclusion
Notes: Jul 31, 2026
<number>

## Slide 3: Deblocking of PCM blocks in CD
Deblocking control:
  Average QP of neighboring blocks used
  Fixed QP=0 used for PCM blocks
Problems:
  Fixed QP=0 may lead to degraded picture quality if quantization noise of PCM blocks does not correspond to QP=0.
  Encoder architectures deciding to use PCM in a final entropy coding step after deblocking would
    need to perform deblocking again if they did not use QP=0, or
    accept drift between the encoder and decoder

## Slide 4: Proposed deblocking control for PCM blocks
Solution: Send slice level QPPCM value
  Instead of QP=0, the slice level QPPCM is used
  Advantage: Solve problem 1 with a minimum change
Solution: Send QP value for each PCM region
  Following JCTVC-suggestion of last meeting corresponding to scheme 2 of JCTVC-I0035
  Difference: Avoid insertion of emulation_prevention_three_bytes by inversion of bits used to signal QP values
  Advantage: Solve problems 1 and 2 with small changes
QP | Binary representation of QP | Inversion
0 | 000000 | 111111
1 | 000001 | 111110
... | ... | ...
51 | 110011 | 001100

## Slide 5: Experiments
Common conditions: IPCM is not used in the common conditions => No influence
Additional experiments following JCTVC-I0035
  Synthesized test sequence “Sandstorms”, CIF, 30 Hz
  RA-Main
  Low QPs: 2, 6, 10, and 14

## Slide 6: Results
 | Mean rate for QPs [kbps] | Mean of (Rate for QPs / Overall rate) [%] | Mean Y-PSNR diff. [dB] | Mean U-PSNR diff. [dB] | Mean V-PSNR diff. [dB] | Enc Time diff. [%] | Dec Time diff. [%]
Solution 1, qp_pcm=0 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 100 | 100
Solution 1, qp_pcm=Slice_QP | 0,14 | 0,00 | 0,00 | -4,10 | -4,10 | 100 | 100
Solution 2, QP=0 | 14,69 | 0,04 | 0,00 | 0,00 | 0,00 | 100 | 100
Solution 2, QP=Slice QP | 14,66 | 0,04 | 0,00 | -4,10 | -4,10 | 100 | 100
=> Very small overhead

## Slide 7: Conclusion
Two solutions for deblocking control of PCM blocks
  Send slice level QP
  Send block level QPs
Cross check: Ericsson
Proposal: Adoption of one of the two solutions