## Slide 1: Prediction Modes and Mode Coding for Large Size Intra Blocks
Copyright © MediaTek Inc. All rights reserved.
Ximin Zhang, Shan Liu and Shawmin Lei
Presented by Shan Liu
9th JCT Meeting in San Jose
27 April – 7 May, 2012
JCTVC-I0227

## Slide 2: Introduction
Prior to the 7th JCT-VC meeting, 4 modes were used for 64x64 Intra prediction with the need of
  Intra mode mapping,
  MPM derivation and coding.
In current HM, 35 modes are used for 64x64 Intra prediction.
  MPM derivation and coding.
It was observed that beyond 4 modes for 64x64 Intra prediction, the coding efficiency saturates.

## Slide 3: Proposed Solutions
Method 1
  4 modes for 64x64 Intra prediction
  2bin fixed length coding of the 4 modes (PL, DC, V, H)
Method 2
  1 mode for 64x64 luma Intra prediction
  No need for mode coding, the mode is inferred to
    Planar
    DC
  Corresponding 32x32 chroma prediction
    Inferred DM mode for main profile
    DM and LM modes (1bin to specify) for HE10 configuration

## Slide 4: Results – Method 1
4 modes for 64x64 Intra prediction
Thanks to Motorola Mobility (JCTVC-I0270) for cross verification
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.4% | 0.4% | 0.0% | 0.5% | 0.6%
Class B | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.1% | 0.0% | -0.2% | 0.1% | -0.1% | 0.0%
Overall | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1%
 | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1%
Class F | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0%
Enc Time[%] | 93% |  |  | 94% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 5: Results – Method 2.a
Single mode (Planar inferred) for 64x64 luma Intra prediction
Two modes (LM, DM) for 32x32 chroma Intra prediction
Thanks to Motorola Mobility (JCTVC-I0270) for cross verification
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 1.2% | 1.1% | 0.0% | 0.8% | 1.2%
Class B | 0.0% | 0.2% | 0.2% | 0.0% | 0.1% | 0.0%
Class C | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.2% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Overall | 0.0% | 0.3% | 0.3% | 0.0% | 0.2% | 0.2%
 | 0.0% | 0.3% | 0.3% | 0.0% | 0.2% | 0.3%
Class F | 0.0% | 0.2% | 0.1% | 0.1% | 0.0% | -0.1%
Enc Time[%] | 90% |  |  | 91% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 6: Results – Method 2.b
Single mode (DC inferred) for 64x64 luma Intra prediction
Two modes (LM, DM) for 32x32 chroma Intra prediction
Thanks to Motorola Mobility (JCTVC-I0270) for cross verification
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.9% | 0.8% | 0.0% | 0.8% | 1.2%
Class B | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.2% | -0.3% | -0.3% | 0.2% | -0.4% | -0.3%
Overall | 0.1% | 0.2% | 0.1% | 0.1% | 0.1% | 0.2%
 | 0.1% | 0.2% | 0.1% | 0.1% | 0.1% | 0.2%
Class F | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | -0.1%
Enc Time[%] | 90% |  |  | 91% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 7: Conclusion
Proposed two methods for simplifying 64x64 Intra prediction.
  Method 1 reported average 0.0% BD-rate change with 6-7% encoding runtime reduction.
  Method 2 reported average 0.0% (using Planar mode) or 0.1% (using DC mode) BD-rate increase with 9-10% encoding runtime reduction.
  Both methods need no mode mapping or MPM derivation and coding, instead the prediction mode is straightforwardly coded (FLC) or inferred.
Recommend to adopt one of the two proposed methods.

## Slide 8
Copyright © MediaTek Inc. All rights reserved.
www.mediatek.com