## Slide 1: LCU based Input order scanning for HASH SEI Message
Authors:
Srinivasan, Ranga Ramanujam ; Mody, Mihir; Ghone, Chaitanya
Source:
Texas Instruments

## Slide 2: Introduction
Hash SEI messages are defined to provide checksum of the decoded picture in the current access unit
Checksum can be used for encoder-decoder bit-match, i.e., compliance testing purpose
Checksum can as well be used to detect error in the stream transmission or storage
This message computation as currently defined in standard, requires scanning of lines in raster order and calculating checksum at the end of frame
There is a sequential dependency between lines in raster-scan order and also between different color components
Checksum computation can’t be done at LCU level decoding process as input pixel order to check-sum calculation is line based raster
This results in additional fetch of decoded frames from external memory, only purpose of checksum

## Slide 3: Checksum Calculation: Sequential Dependency

## Slide 4: Proposal – Part 1
Two options suggested in this proposal to break the sequential dependency
  Send three checksums, one each for three color components (Y, Cb and Cr). This breaks the sequential dependency between different color components
  Do LCU based raster-scan of filtered components
Changes in standard specification
Decoded_picture_hash( payloadSize ) { | Descriptor
hash_type | u(8)
if( hash_type = = 0 ) | 
for(comp=0; comp<3; comp++) | 
for( i = 0; i < 16; i++) | 
Picture_md5[comp][ i ] | b(8)
else if( hash_type = = 1 ) | 
for(comp=0; comp<3; comp++) | 
picture_crc[comp] | u(16)
} | 

## Slide 5: LCU Based scan-order
The new scan order proposed is similar to the decoding order of pixels and provides controls to handle the delay in final pixel data availability due to loop-filtering operations
Consider a stream with LCU size of 64x64, frame size 256x256 as shown below with de-blocking introducing a delay 4 pixels to the left and top.
In this case, when the first LCU is decoded only Region0 will contain the final loop-filtered pixel data. So the scan-order shall be raster within Region 0 (12x12 block)

## Slide 6: LCU Based scan-order
As we move, to next LCU in decoding order, in Region 1 the scan-order shall span across the first and second LCU.
Block sizes shall be 16x12 in Region1
When we reach the last LCU, the block size shall be 20x12
Example scan order are shown for the first row in the figure along side
As we move to further into picture decoding, the block sizes shall be
  16x12 in Region3
  16x16 in Region 4
  20x16 in Region 5
  20x12 in Region 6
  20x16 in Region 7
  20x20 in Region 8

## Slide 7: LCU Based scan-order
Block sizes shall differ with different types (ALFonly , SAO only, ALF+SAO, Deblock only, etc…) of loop-filtering.
The delays in pixel decoding differ for each of the scenarios
Further if image size is not multiple of LCU size, the block sizes need to be modified for the last row and last columns.
The next slide provides the block sizes for a more generic scenario

## Slide 8: Region Definition
Region number | Height | Width
0 | Lcu_height - k | Lcu_width – k
1 | Lcu_height - k | Lcu_width
2 | Lcu_height - k | LastColWidth
3 | Lcu_height | Lcu_width – k
4 | Lcu_height | Lcu_width
5 | Lcu_height | LastColWidth
6 | LastRowHeight | Lcu_width – k
7 | LastRowHeight | Lcu_width
8 | LastRowHeight | LastColWidth
Filtering Process | K for Luma | K for Chroma
No Inloop de-blocking | 0 | 0
Only De-blocking filter | 4 | 2
Only SAO filter | 1 | 1
Only ALF | 4 | 4
WidthModLcuSz = ((floor)(Width + Lcu_width - 1/Lcu_width) );
LastColWidth = Width – (WidthModLcuSz-1)* Lcu_width + k;
HeightModLcuSz = ((floor)(Height + Lcu_height - 1/Lcu_height) );
LastRowHeight = Height – (HeightModLcuSz-1)* Lcu_height + k;
Lcu_height and Lcu_width are height and width of Largest Coding Unit respectively

## Slide 9: Region Definition (Example 176x144)
Region number | Height | Width
0 | 63 | 63
1 | 63 | 64
2 | 63 | 49
3 | 64 | 63
4 | 64 | 64
5 | 64 | 49
6 | 17 | 63
7 | 17 | 64
8 | 17 | 49
176x144 stream where only deblocking and ALF is enabled.
The k value for Y will be 8 and for Cb/Cr will be 6.
Below table is for steam where only SAO is enabled. K is 1 for both Luma and Chroma

## Slide 10: Results
There is no change in BD-PSNR/BD-Bitrate numbers as SEI messages are not counted as bits consumed for PSNR calculations
Enables in loop LCU decoding process for easier implementation, enabling real-time calculation of Checksums
It saves 90 MB/second memory bandwidth for 1080p30 sequence and removes frame-end computations