## Slide 1: SAO Type Coding Simplification
E. Maani (Sony), K. Minoo, D. Baylon (Motorola Mobility), E. Alshina (Samsung)
Proposal
JCTVC-I0246
Apr 25 2012

## Slide 2: SAO Type coding in WD6
<number>
JCTVC-I0246
Mode | Codeword
SAO Off | 0
EO_0 | 1 0
EO_1 | 1 10
EO_2 | 1 110
EO_3 | 1 1110
BO | 1 11110
ctx0
ctx1
  BO statistics vary a lot from a sequence to another
    Ctx1 cannot track BO/EO stats
  EO additional information (direction) is coded in SAO type but BO additional information (starting band) is coded separately as side information
  EO types have different code lengths. Logically, they should have the same code length. EO type statistics is uniform not GEOMETRIC

## Slide 3: Proposed vs WD6
<number>
JCTVC-I0246
WD6
Proposed
Notes: Number of offsets always (BO or EO) is always 4.
<number>

## Slide 4: Summary
Cleaner, simplified design with a performance gain
Same number of contexts, but more bypass coding
Same length codewords for different EO directions
  Symmetry in a large collection of images
<number>
JCTVC-I0246

## Slide 5: Results (CE1 test conditions)
<number>
JCTVC-I0246
 | Low delay B Main CU64x64 |  |  | Low delay B HE10 CU64x64 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.8% | -0.9% | 0.0% | -0.6% | -0.7%
Class C | 0.0% | -0.7% | -0.7% | 0.0% | -0.3% | -0.7%
Class D | 0.0% | -0.6% | -0.4% | 0.0% | -0.8% | -0.3%
Class E | 0.1% | -0.8% | -1.5% | 0.1% | -0.4% | -1.0%
Overall | 0.0% | -0.7% | -0.7% | 0.0% | -0.6% | -0.6%
 | 0.0% | -0.7% | -0.7% | 0.0% | -0.6% | -0.6%
Class F | -0.2% | -0.9% | -1.0% | 0.0% | -0.3% | -0.7%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
 | Low delay B Main CU32x32 |  |  | Low delay B HE10 CU32x32 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.3% | -0.7% | 0.0% | -0.2% | -0.2%
Class C | -0.1% | -0.5% | -0.9% | -0.1% | -0.3% | -0.4%
Class D | 0.0% | -0.7% | -0.3% | 0.0% | -0.1% | -0.5%
Class E | 0.0% | -0.2% | -0.5% | 0.0% | 0.1% | 0.1%
Overall | 0.0% | -0.4% | -0.6% | 0.0% | -0.1% | -0.3%
 | 0.0% | -0.4% | -0.6% | 0.0% | -0.1% | -0.2%
Class F | -0.2% | 0.0% | -1.4% | -0.1% | -0.4% | -0.7%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
 | Low delay B Main CU16x16 |  |  | Low delay B HE10 CU16x16 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.1% | 0.1% | 0.0% | -0.3% | -0.2%
Class C | -0.1% | -0.2% | -0.1% | -0.1% | 0.0% | 0.2%
Class D | 0.0% | 0.2% | -0.3% | 0.0% | 0.3% | 0.3%
Class E | -0.1% | -0.1% | 0.1% | 0.1% | 0.2% | 0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
Class F | -0.2% | -0.6% | -0.9% | -0.1% | 1.0% | 0.6%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -0.2% | 0.0% | 0.0% | -0.4% | -0.3%
Class B | 0.0% | -0.3% | -0.3% | 0.0% | -0.2% | -0.3%
Class C | 0.0% | -0.2% | -0.3% | 0.0% | -0.1% | -0.3%
Class D | 0.0% | -0.5% | -0.2% | 0.0% | -0.1% | -0.1%
Class E |  |  |  |  |  | 
Overall | 0.0% | -0.3% | -0.2% | 0.0% | -0.2% | -0.2%
 | 0.0% | -0.3% | -0.2% | 0.0% | -0.2% | -0.2%
Class F | -0.1% | -0.2% | -0.3% | 0.0% | -0.3% | -0.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  | 

## Slide 6
Notes: <number>