## Slide 1: Continuity in Band Offset SAO
E. Maani, O. Nakagami,
Proposal
JCTVC-I0247
Apr 25 2012

## Slide 2: Band Offset Discontinuity Issues
An offset is added to reconstructed values
SAO only improves the average. Pixel values that are close before SAO can end up very far apart due to SAO BO
Pixels with values close to each other usually appear as spatial neighbors in natural images (especially smooth areas)
  Offset discontinuity can cause a visible artifact (artificial edges)
  HEVC does not enforce offset continuity and offsets can be quite large (e.g. 32 in difference)
<number>
JCTVC-I0247

## Slide 3: Proposed solution
Alternative: restricting the encoder results in large BD-rate losses
Solution: Impose offset function continuity
  The problem can be resolved by simple processing of the band boundaries
    Linearly smooth band boundaries (5 boundaries will be processed)
<number>
JCTVC-I0247
Notes: This example shows 4 bands, and band for which an offset is not transmitted can also end up with a nonzero offset near the band boundary
<number>

## Slide 4: Smoothing band boundaries
<number>
JCTVC-I0247
offset for pixel i
bit precision
smoothing size
left-hand side original offset
right-hand side original offset
 | i=1 | i=2 | i=3 | i=4
D=2, d=4 | 1 | 2 | 4-2 | 4-1
D=4, d=4 | 3 | 6 | 16-6 | 16-3
D=8, d=4 | 51 | 102 | 256-102 | 256-51
Notes: <number>

## Slide 5: Results
<number>
JCTVC-I0247
 | Low delay B Main CU64x64 |  |  | Low delay B HE10 CU64x64 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | -0.1% | -0.1% | 0.0% | -0.2% | -0.1%
Class D | 0.0% | -0.1% | 0.0% | -0.1% | -0.2% | -0.3%
Class E | -0.1% | -0.3% | -0.3% | 0.0% | 0.1% | 0.0%
Overall | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | -0.1%
 | 0.0% | -0.1% | 0.0% | 0.0% | -0.2% | -0.1%
Class F | -0.2% | -0.4% | -0.3% | -0.1% | 0.2% | -0.2%
Enc Time[%] | 98% |  |  | 98% |  | 
Dec Time[%] | 101% |  |  | 103% |  | 
 | Low delay B Main CU32x32 |  |  | Low delay B HE10 CU32x32 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.1% | -0.5% | 0.0% | 0.0% | 0.1%
Class C | 0.0% | -0.2% | -0.1% | 0.0% | 0.1% | 0.0%
Class D | 0.0% | -0.1% | -0.1% | 0.0% | -0.3% | -0.7%
Class E | -0.1% | 0.1% | 0.1% | 0.0% | 0.0% | -0.1%
Overall | 0.0% | -0.1% | -0.2% | 0.0% | 0.0% | -0.2%
 | 0.0% | -0.1% | -0.2% | 0.0% | 0.0% | -0.1%
Class F | -0.3% | 1.2% | 0.4% | 0.0% | -0.4% | 0.1%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
 | Low delay B Main CU16x16 |  |  | Low delay B HE10 CU16x16 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | -0.2% | 0.1% | 0.0% | -0.1% | 0.4%
Class C | 0.0% | -0.1% | 0.2% | 0.0% | -0.1% | 0.1%
Class D | 0.0% | 0.1% | 0.2% | 0.0% | 0.4% | -0.2%
Class E | 0.0% | 0.2% | 0.1% | 0.0% | 0.1% | -0.1%
Overall | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1%
 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1%
Class F | -0.2% | 0.2% | -0.9% | 0.0% | 0.3% | 0.8%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.4% | 0.2% | 0.1% | 0.0% | 0.2%
Class B | -0.1% | -0.2% | -0.1% | 0.0% | 0.0% | 0.1%
Class C | -0.1% | -0.3% | -0.2% | -0.1% | 0.0% | 0.0%
Class D | -0.4% | -0.5% | -0.4% | -0.3% | -0.4% | -0.4%
Class E |  |  |  |  |  | 
Overall | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0%
 | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | 0.0%
Class F | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.1%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 99% |  | 
Band boundary smoothing
(d=4, D= 8)

## Slide 6: LCU Boundary
SAO causes visual artifacts also if a BO partition is neighbor with an EO
The same linear smoothing can be applied to LCU boundary
<number>
JCTVC-I0247
Notes: <number>

## Slide 7: LCU Boundary Processing
If a BO partition is not merged into a neighbor, the offset for that boundary is reduced
  Reduction is linearly done between original offset and zero (if no merge)
  The offsets of the neighboring LCUs do not need to be stored/remembered (just the merge flags)
  Each LCU only needs pixels within that LCU for processing (no line buffer needed)
<number>
JCTVC-I0247
(Current LCU)
Notes: <number>

## Slide 8: Results
<number>
JCTVC-I0247
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.4% | 0.2% | 0.0% | -0.2% | -0.4%
Class B | -0.1% | -0.2% | -0.1% | 0.0% | 0.0% | 0.1%
Class C | -0.1% | -0.3% | -0.2% | 0.0% | 0.0% | 0.1%
Class D | -0.4% | -0.5% | -0.4% | 0.0% | 0.0% | 0.0%
Class E |  |  |  |  |  | 
Overall | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0%
 | -0.1% | -0.2% | -0.1% | 0.0% | -0.1% | 0.0%
Class F | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
 | Low delay B Main CU64x64 |  |  | Low delay B HE10 CU64x64 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | -0.2% | -0.1%
Class C | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | 0.1%
Class D | 0.0% | 0.2% | 0.7% | 0.0% | -0.5% | -0.3%
Class E | 0.0% | 0.1% | 0.0% | 0.1% | 0.2% | 0.1%
Overall | 0.0% | 0.1% | 0.3% | 0.0% | -0.2% | -0.1%
 | 0.0% | 0.1% | 0.3% | 0.0% | -0.2% | -0.2%
Class F | -0.1% | 0.2% | 0.3% | -0.1% | 0.5% | -0.2%
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 102% |  |  | 102% |  | 
 | Low delay B Main CU32x32 |  |  | Low delay B HE10 CU32x32 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.2% | -0.3% | 0.0% | 0.1% | 0.2%
Class C | 0.0% | 0.2% | 0.1% | 0.0% | 0.2% | 0.2%
Class D | -0.1% | -0.1% | 0.1% | 0.0% | 0.3% | -0.1%
Class E | 0.0% | -0.1% | -0.3% | 0.1% | 0.2% | -0.4%
Overall | 0.0% | 0.1% | -0.1% | 0.0% | 0.2% | 0.0%
 | 0.0% | 0.1% | -0.1% | 0.0% | 0.2% | 0.0%
Class F | -0.2% | 0.4% | 0.3% | 0.0% | -0.3% | 1.0%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
 | Low delay B Main CU16x16 |  |  | Low delay B HE10 CU16x16 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.1% | 0.3% | 0.0% | -0.3% | 0.0%
Class C | 0.0% | 0.0% | -0.1% | -0.1% | -0.2% | 0.2%
Class D | -0.1% | -0.2% | -0.5% | 0.0% | 0.3% | 0.1%
Class E | 0.0% | 0.3% | 0.1% | 0.0% | -0.1% | -0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.1%
 | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.1%
Class F | 0.0% | -0.1% | -0.4% | 0.0% | 0.5% | 0.8%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  | 
Band boundary smoothing +
(d=4, D= 8)
LCU boundary smoothing
(d=2, D= 8)

## Slide 9: Visual Evaluation (combined)
<number>
JCTVC-I0247
CE1 anchor
proposed

## Slide 10: Visual Evaluation (combined)
<number>
JCTVC-I0247
CE1 anchor
proposed

## Slide 11: Visual Evaluation (combined)
<number>
JCTVC-I0247
CE1 anchor
proposed

## Slide 12
Notes: <number>