## Slide 1: Level restrictions on tiles for line buffer reduction
JCTVC-I0255
Andrey Norkin, Rickard Sjöberg
Ericsson
Notes: 2010-10-07
Ericsson AB 2010
<number>

## Slide 2: Problem formulation
There have been many proposals in in-loop filtering addressing line buffer reduction
  Special processing on hor. LCU boundary for ALF
  Special processing on hor. LCU boundary for SAO
  Special processing hor. LCU boundary for deblocking
Line-buffer reduction methods typically introduce irregularities in in-loop filtering (like padding or using different filters on hor. LCU boundary)
Subjective quality may be affected
LCU
#0
LCU
#1
Line buffer
decoded LCU’s
LCU’s to be decoded
To decrease a number of memory accesses (esp. in hardware) in-loop filtering is performed in LCU order after decoding the LCU
Several bottom lines in LCU are kept in on-chip memory (line buffer) until pixels in next LCU to bottom are available to in-loop filters
Currently, 4 lines need to be kept in line buffer
Resolutions 4Kx2K – 2 times larger line buffer than in H.264 1920x1080
Notes: 2010-10-07
Ericsson AB 2010
<number>

## Slide 3: Proposed solution – mandate tiles
LCU
#0
LCU
#1
LCU
#6
LCU
#7
LCU
#14
Vert. tile boundary
Tile #1
Line buffer
Column buffer
(saved in the memory)
decoded LCU’s
LCU’s to be decoded
Tile #0
Include restriction on maximum tile width in level definitions

## Slide 4: Example of level restriction on tiles
Level | MaxTileWidthIn LCU | MinTileWidthIn LCU | MinTileHeightIn LCU
5 and above | 30 | 3 | 3
Level | MaxTileWidthIn Pixels | MinTileWidthIn Pixels | MinTileHeightIn Pixels
5 | 1920 | 192 | 192

## Slide 5: Conclusions
It is proposed to impose level limits on tile size
  This means that use of multiple tiles in pictures would be mandated for certain levels for larger resolutions
Tiles can reduce line buffer without any modifications to in-loop filters structure
Tiles can also be used together with any other proposals reducing line buffers (reducing line buffer size even more)
It is proposed to impose limitations on tile size into HEVC levels definitions

## Slide 6
Notes: 2010-10-07
Ericsson AB 2010
<number>