## Slide 1: JCTVC-I0257 On Intensity Dependent Quantization in the HEVC Codec
R&D
© BBC MMXII
Matteo Naccari, Marta Mrak, David Flynn, Andrea Gabriellini
BBC Research and Development

## Slide 2: Intensity Dependent Quantisation (IDQ): Main idea
Human eye is less sensitive to the coding distortion in bright and dark image areas
These areas can be then quantised coarsely (perceptual quality won’t change)
This is done as:
Luma average computation
TU predictor
IDQ profile (look-up table)
µ
Q-1
QP(µ)
TU residues
To inverse transform
Fine granularity for perceptual QP selection (TU basis)
No need to transmit the Delta QP (DQP)

## Slide 3: Experimental results: Bitrate reductions against the HM-6.0
The proposed IDQ leads to the same perceptual quality
At the same quality level the bitrate reductions are measured:
10th percentile
Average reduction: 8%
50th percentile
Average reduction: 4.5%
Average bitrate reductions of 2% over all conditions
Reduction peaks in the range 18 – 20% were observed

## Slide 4: Experimental results: BD-rates against non-normative perceptual quantisation (using DQP)

## Slide 5: Integration in the HEVC codec: IDQ profile transmission
Mean luma intensity
QP offset
5
4
3
2
1
0
20
40
60
80
100
150
180
200
220
255
The IDQ profile is transmitted by performing DPCM:
Differences in QP offsets = {±1}
Interval width
Profile is signalled in the Picture Parameter Set (PPS)
Provides per component profile

## Slide 6: Integration in the HEVC codec: Deblocking filter
CU(i)
CU(j)
TU(0)
TU(1)
TU(2)
TU(3)
TU(0)
P
Q
Current HEVC design derives the deblocking filter parameters using the QP of the CU which contains pixel P
In this proposal the QP is given by the TU which contains pixel P

## Slide 7: Used IDQ profile for experiments
Derived from a state-of-the-art literature work [1]:
[1] Y. Jia, W. Lin and A. A. Kassim, “Estimating the just-noticeable distortion for video”, IEEE Transactions on Circuits and Systems for Video Technology, vol. 16, no. 7, pp. 820-829, July 2006.
IDQ profile values have been modified by the authors of this contribution
 | Pair number |  |  |  |  |  |  |  |  |  |  |  |  | 
[0..13] | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
µ | 0 | 3 | 7 | 12 | 17 | 21 | 26 | 30 | 35 | 40 | 45 | 51 | 57 | 64
idQP | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
 | Pair number |  |  |  |  |  |  |  |  |  |  |  |  | 
[14..27] | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27
µ | 76 | 120 | 136 | 147 | 158 | 168 | 178 | 187 | 197 | 207 | 217 | 227 | 238 | 249
idQP | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
QP 22 and 27

## Slide 8: Used IDQ profile for experiments
QP = 32
 | Pair number |  |  |  |  |  |  |  |  |  |  | 
[0..11] | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
µ | 0 | 3 | 8 | 13 | 18 | 23 | 29 | 34 | 39 | 46 | 52 | 61
idQP | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
 | Pair number |  |  |  |  |  |  |  |  |  |  | 
[12..23] | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
µ | 73 | 123 | 142 | 156 | 169 | 180 | 192 | 203 | 215 | 226 | 238 | 250
idQP | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
QP = 37
 | Pair number |  |  |  |  |  |  |  |  |  | 
[0..10] | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
µ | 0 | 2 | 8 | 13 | 18 | 24 | 30 | 36 | 42 | 49 | 58
idQP | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
 | Pair number |  |  |  |  |  |  |  |  |  | 
[11..21] | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
µ | 72 | 126 | 147 | 163 | 177 | 190 | 203 | 215 | 228 | 241 | 254
idQP | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10

## Slide 9: Intensity Dependent Quantisation (IDQ): Main idea
Human eye is less sensitive to the coding distortion in bright and dark image areas
These areas can be quantised coarsely
In this contribution the average pixel intensity masking is considered:
The quantisation step may be higher in darker and brighter images areas: Intensity Dependent Quantisation (IDQ)
Average pixel intensity for a given image block (e.g. TU)

## Slide 10: Integration in the HEVC codec: Intensity Dependent Quantisation (IDQ) profile
Mapping between µ and the Q(µ) is denoted as Intensity Dependent Quantisation (IDQ) profile
Q(µ) is related to the HEVC QP as:
By referring QP(µ) to the base QP it yields the intensity differential QP (idQP):